## Slide 1: 3GPP Subnetworks in Rel-20 Motivation, Use Cases, and Proposal Bosch, Siemens, Fraunhofer IIS
S1-240120

## Slide 2: Motivation
3GPP Subnetworks
Many vertical use cases require highly localized communication within sub-systems.
  e.g., within a vehicle, or a machine tool to partially replace existing communication technologies e.g., Ethernet, CAN, Profinet which have often stringent QoS requirements.
  Wireless subnetworks may bring many benefits, such as lower complexity, higher flexibility and lower costs e.g., by simplifying the wiring harness in a car.
Existing 3GPP communication modes/topologies are not optimal for such localized communication requirements since:
  Integration and operation of all sub-system devices through the 3GPP infrastructure can be cumbersome.
  Loss of the connection to the 3GPP network may lead to an outage of the sub-system, which is not tolerable for such sub-systems e.g., a car.
  Routing of sub-system traffic and management functions through public mobile networks leads to unnecessarily higher latency and network load.

## Slide 3: Definition and Example
3GPP Subnetworks
Parent network
Subnetworks
Subnetwork config/control
Inter-subnetwork comm.
Parent network (E.g. PLMN or NPN)
Enable subnetwork external connectivity.
Main security anchor.
If needed, charging & billing.
Grant bulk communication resources to subnetworks.
Subnetworks (can be nested)
Manage granted resources within subnetworks.
Route internal traffic of subnetworks.
Limited core network functionalities for partial autonomy (e.g. during loss of connectivity).
3GPP Subnetworks: use-case-centric local wireless networks, which are attached to a parent mobile network (e.g., PLMN or NPN), having partial autonomy to survive.
  E.g., survival in case of a temporary loss of connection to the parent network.

## Slide 4: Alternative 3GPP Topologies
3GPP Subnetworks
Non-Terrestrial Networks
PLMN1
Non-Public Networks
Subnetworks
Satellite Operator
MNO2
Enterprise
Use Case
Centricity
Worldwide
Country
Building, Campus
(Sub-)System
Typical
Coverage Area
Millions
Millions
Thousands
Tens
Typical Size (#devices)
Partial
No
No, nomadic
Yes
Mobility of the network
Logistics, V2X, Consumer
Consumer, V2X
Manufacturing, Ports, PMSE3
In-Car, Robot Cell, Collaborative robots
Examplary Applications
1Public Land Mobile Networks 2Mobile Network Operator 3Programme-making & special events * Only in unicast, more UEs in groupcast/broadcast
Sidelink
Link
Link
Two*
Yes
V2V

## Slide 5: Characteristics
3GPP Subnetworks
A Subnetwork management entity may exist within/outside the subnetwork, which can share the required configuration and management functions with the parent (traditional) network to control the subnetwork.
  The subnetwork management entity can be configured to take care of control/RRM functions by the parent network to maintain QoS requirements within the subnetwork.
Subnetworks can be configured with partial autonomy from the parent network, e.g. to sustain at least limited operation during loss of connectivity (based on network policies).
Subnetworks may be nested, to enable formation of subnetworks within subnetworks i.e., network of networks.
  Subnetwork devices maybe configured to be part of more than one subnetwork, also accounting for mobility between networks.
Potentially comprising of subnetwork devices with heterogenous capabilities, as well as Radio Access Technologies (3GPP-based and/or non-3GPP-based).
Parent network
Subnetworks
Subnetwork config/control
Inter-subnetwork comm.
Subnet
management entity
General example for Subnetworks

## Slide 6: Use Case Examples
3GPP Subnetworks
Subnetwork allows simple integration of in-machine components and workpieces (plug-and-play).
  Other subnetwork entities, such as HMIs or transport vehicle might join the subnetwork on-demand.
Sensor / Actuator
ECU
Zonal Controller
Centralized generic compute platform
Passenger Entertainment
Subnetwork
Infotainment
PLC
Workpiece
Machining
Inspection
Moving/transport
HMI
AGV
PLC: Programmable Logic Controller HMI: Human-Machine-Interface AGV: Automated Guided Vehicle ECU: Electronic Control Unit E/E Architecture: Electrical/Electronic Architecture
Subnetwork serves as communication backbone to integrate vehicle components wirelessly in the automotive E/E architecture.
Multiple application and use-case-specific subnetworks can be created, e.g., with consumer devices for passenger entertainment.
Use case 1: Subnetworks on a factory floor
Use case 2: In-vehicle subnetworks to enable an
efficient automotive E/E architecture
Subnet
management entity

## Slide 7: Required Enhancements and Objectives of the Study
3GPP Subnetworks
High-level objective: Identification of use cases and potential requirements to enable subnetworks.
Study on potential new requirements to enable subnetworks could address the following aspects:
The necessary features and mechanisms to enable partial autonomy from the parent network.
  The subnetwork management entity is able to handle control (dynamic integration and RRM) for subnetwork devices and coordination with parent network.
  E.g., discovery of subnetwork devices or other subnetworks.
Considerations for enabling the formation of nested local networks.
Interfacing to heterogenous Radio Access Technologies (3GPP and non-3GPP).
Possible work tasks may include the following:
Discussion of use cases, associated service/performance requirements and KPIs.
Authorization, (de)activation, service provisioning, and control.
  Based on coverage scenarios, level of subnetwork autonomy (full/partial/none), communication range, QoS requirements, RATs, etc.