## Slide 1: Discussion on enhanced support of dual RX/TX MUSIM UE
CableLabs
3GPP SA WG1 Meeting #105
Athens, Greece Meeting, 26 Feb – 01 Mar 2024
S1-240135, 3GPP TSG-SA WG1 Meeting #105, 26 Feb – 01 Mar 2024

## Slide 2: Motivations
Existing service requirements to support MUSIM capable devices have been limited to 1Tx/1Rx and 1Tx/2Rx implementation of MUSIM UE
Limitation with dual steer requirements
  Current requirements don’t clearly capture how Multi-SIM UEs should be able to access services via multiple networks simultaneously, and with minimum interruption
  There’s no support for traffic splitting across networks.
Lack of coordination between networks supporting multi-SIM UE for efficient UE and network resource management, power consumption.
Lack of support for various deployment scenarios and features of multi-SIM UEs.
  Simultaneous access of PLMN+PLMN over 4G/5G
  Simultaneous access of PLMN+SNPN over 4G/5G.
Support UE and network energy savings by enabling co-ordination between networks and multi-SIM UE needs to be studied.
Single operator cannot support diverse features, ubiquitous coverage given the multitude of use cases and service experiences requested by the end-user. With co-ordination between MU-SIM UE networks and UE, providers can fulfill deliver service optimally.
S1-240135, 3GPP TSG-SA WG1 Meeting #105, 26 Feb – 01 Mar 2024

## Slide 3: Use Cases
Operator offering 5G services on SIM1 and 4G services on SIM2
  Dual Connectivity requires signaling between the two 3GPP access networks
  Connectivity to the master node needs to be always maintained
Operator offering PLMN services on SIM1 and SNPN services on SIM2
  A SNPN may provide better performance for targeted services at specific geographic location while a PLMN might be used for all other services
Operator offering HPLMN services on SIM1 (data only) and VPLMN services (voice at all times and data when outside of HPLMN coverage) on SIM2
  Certain operators' may have a smaller geographical footprint and may provide targeted services while relying on other roaming partners to provide other services and services outside their geographical footprint
UE network energy saving
  To achieve energy efficiency goals, a network would like to perform traffic offloading and MUSIM capable UEs can perform traffic switching between networks for energy savings.
Efficient Resource Utilization
  Signaling, procedures like RA/TA updates can be unified between networks serving a MUSIM UE and radio resources can be utilized efficiently.
S1-240135, 3GPP TSG-SA WG1 Meeting #105, 26 Feb – 01 Mar 2024

## Slide 4: Use Case: PLMN + PLMN
UE can simultaneously maintain “active” and “idle” connections owning to the dedicated transceiver for each SIM.
Unlike single TX with single RX or dual RX UE devices, dual RX/TX UE devices can connect and maintain connection simultaneously. Procedures that needed with single TX radio like paging cause indication, graceful leaving and resumption may need to be studied if they’re needed with dual TX MUSIM devices.
MUSIM UEs can connect to 4G network with one SIM and a 5G network associated with the other SIM. UE registration, paging, connection establishment can be done independently.
If the same MNO owns both the networks, subscriber can be able to bundle both the connections with single subscriptions and different services can be provisioned in different networks.
S1-240135, 3GPP TSG-SA WG1 Meeting #105, 26 Feb – 01 Mar 2024
Some of the scenarios, we can think of are:
  If data connection services like Netflix use the PLMN-A, voice calls can be routed through PLMN-B.
  If data connection in PLMN-A experiencing reaching data performance thresholds like Latency, error rates, Queue lengths new services can be provisioned with PLMN-B.

## Slide 5: Use Case: PLMN + SNPN
With the 5G NPN, there is a possibility to adopt novel decentralized operation models, where the roles and responsibilities for setting up and operating the network can be distributed over several stakeholders.
Study multiple deployment models and operational models to identify the roles of different stake holders and system requirements to support these models.
Study inter network procedures to enable efficient resource usage, session continuity and data session switching between the networks to enable better user experience.
S1-240135, 3GPP TSG-SA WG1 Meeting #105, 26 Feb – 01 Mar 2024

## Slide 6: Use Case: Network/UE Energy Efficiency
PLMN-A and PLMN-B have different energy savings policies and energy efficiency goals. MUSIM UE has the knowledge about energy efficiency KPIs for each of the PLMNs.
Based on the current energy savings requirements of the UE (like if UE is in energy saving mode or reaching the energy saving mode), UE may prefer moving a service from PLMN-A to PLMN-B.
In other use cases, a service is better serviced if that service is hosted in PLMN-B rather than PLMN-A because of the service requirements and current network energy savings KPIs (like PLMN-A prefer to scale down resources for energy savings).
We should study how a MUSIM UE can negotiate with networks to move services between networks.
S1-240135, 3GPP TSG-SA WG1 Meeting #105, 26 Feb – 01 Mar 2024

## Slide 7: Proposal
The objective of the proposed work item is:
To specify service requirements for supporting dual RX/TX Multi-SIM (MUSIM) UE.
Study and identify use cases for supporting different multi-USIM scenarios
  Identify potential requirements to overcome challenges of lack of coordination between networks to support multi-USIM scenarios;
  For identified use cases, perform a gap analysis between newly identified requirements and existing 3GPP requirements
The scope of the work will include:
Single Operator and Multi-Operator
Single RAT and Multi-RAT (4G/5G)
PLMN-PLMN and PLMN-SNPN
The service requirements will cover the following aspects:
Co-ordination across 3GPP access networks associated with the two SIM
  Network awareness of two USIMs (UEs) belonging to one MUSIM device
  Provide unified coverage, service capabilities
Ability of the UE in one 3GPP network to partial switch Tx/Rx chains to other 3GPP network (distribution of Tx/Rx chains limiting MIMO capabilities)
Any MUSIM applicable features specified for single RX/TX and single Tx dual Rx MUSIM UEs that may be applicable to dual RX/TX UE
UE/network energy saving via cross-paging capabilities/tight-coordination
S1-240135, 3GPP TSG-SA WG1 Meeting #105, 26 Feb – 01 Mar 2024

## Slide 8: Backup
S1-240135, 3GPP TSG-SA WG1 Meeting #105, 26 Feb – 01 Mar 2024

## Slide 9
Background
The following features were specified as part of the MUSIM work item:
Connection Release - allows requesting the network to release the UE from RRC-CONNECTED due to inactivity
Paging Cause Indication for Voice Service – allows network to indicate the UE when it is being paged for voice
Reject Paging Request- allows UE to indicate non acceptance of paging and request to return to CM-IDLE
Paging Restriction - allows UE to request not be paged for any MT service, or be paged only for voice, or for traffic arriving on selected PDU session, etc
Paging Timing Collision Control – allows UE to request a new 5G-GUTI used for determination of paging occasions
UE and 5GC exchange their MUSIM capabilities as part of the Registration procedure
NOTE: All the MUSIM work has been focused on 1Tx/1Rx and 1Tx/2Rx UEs.