## Slide 1: Supplemental Network Extension (SupNet)
Qualcomm
3GPP TSG SA WG 1 Meeting #105 S1-240142
Athens, Greece, Feb 24 – Mar 1, 2024 (rev of S1-233224)

## Slide 2: Motivations & Background
Reducing MNO CAPEX/OPEX or cost vs price/GB for RAN deployment is a constant and increasing issue
  Especially challenging for densified/small cells, indoor coverage, remote areas, ad-hoc hotspots
An independent entity (e.g., premises/real-estate owner, 3rd party small cells provider) can deploy RAN nodes providing supplemental coverage/capacity extension for MNOs’ services
  The entity deploying the NW can be incentivized, by the MNO, for contributing to the MNO’s extended coverage & connectivity, e.g. based on proof of coverage/use
  The supplemental NW can also provide specific CN functions, services or local breakout data connectivity
  Spectrum can be licensed/unlicensed, can be owned by the MNO or the 3rd-party entity managing the NW
Some example target scenarios are:
  Indoor venues, e.g. shopping malls, commercial/enterprise buildings
  Remote/rural areas with no/limited MNOs coverage
  Ad-hoc events / venues (e.g., music festival, sport venues)

## Slide 3: High-level concept
SupNet provider manages:
  Coordination with MNOs, settlement of coverage/data offloading requirements
  Operation & configuration functions related to the SupNet RAN nodes
  Handling of Proof-of-Coverage (e.g. from dedicated UEs), support access to MNO & inbound roaming UEs,
  (optionally) CN functions e.g., for inter-connecting RAN to MNO core network, or to provide local data offloading
Assisting UE (A-UE) is a UE with new functionality performing Proof-of-Coverage & Reporting
  It can be normal UE or a dedicated UE for Proof-of-Coverage purpose, authorized and configured by SupNet provider
  A-UE performs Proof-of-Coverage operation and reports to SupNet provider (who manages records of Proof-of-Coverage)
MNO requests coverage/capacity extension services from SupNet provider
  MNO provides configuration information/requirement to meet their coverage demand in particular location(s) and/or time
  MNO collects consolidated records of Proof-of-coverage/Proof-of-usage from SupNet provider
SupNet RAN
UE
SupNet provider
Data Network
MNO
Core Network
Data connectivity
Control/OAM
[Legend]
A-UE
Proof of Coverage
“SupNet provider”: the 3rd party entity managing the “SupNet NW”

## Slide 4: Service Scenarios & Flow
Premises owner or 3rd party entity provisions / installs RAN nodes, in specific locations or areas, managed by a SupNet provider
Based on MNO’s demand, SupNet provider configures RAN nodes (for access to MNO’s UEs, connection with MNO’s NW, etc.)
SupNet provider configures and collects proof of coverage reports and validates NW operation and coverage service toward MNO
MNO rewards SupNet provider (who can reward SupNet node owner)
SupNet node
SupNet Provider
SupNet Provider
Indoor UEs
Indoor UEs
outdoor UEs
outdoor UEs
<Shopping mall>
<Dense urban area>
Indoor UEs
MNO#1
MNO#2
MNO#3
Node owner
Premise owner
Smart city network provider
Enterprise owner
Building owner
Indoor/outdoor UEs
<Rural / Remote area>

## Slide 5: Potential SA1 Gaps
Previous SA1 studies and requirements, including similar scenarios/aspects:
  SON
  RAN sharing
  NPN
  PALS
  Residential 5G
  PIN
Gaps: the above do not cover specific SupNet scenarios, aspects and functionalities, including
  SupNet NW can be managed by a 3rd party (may not be an MNO, like for MOCN or PALS)
  Specific policies and configuration between parties) to provide coverage/capacity service
  Configuration, collection and reporting of Proof of coverage / usage by authorized UEs

## Slide 6: Proposal for SA1 – SID Objectives
Study use cases and requirements to support scenarios where MNO(s) could rely on a 3rd party to install and manage network resources (e.g. RAN nodes) used to provide supplemental coverage and/or capacity to the MNO’s users, e.g. in indoor, hotspot or remote areas.
The following aspects should be covered:
Coordination between the 3rd party (SupNet provider) and the MNO(s) for the control and settings of the supplemental NW resources managed by the 3rd party
Management and configuration, by the SupNet provider, of the connectivity between the supplemental network and the MNO network, as well as appropriate coverage and access to MNO’s users
Support of proof of coverage and/or usage for network operation verification, including configuration of participating UEs / entities, relevant metrics, reporting to the SupNet provider and exposure to the MNO
Other aspects, e.g. charging, security and regulatory requirements

## Slide 7: ANNEX 1 Extra slides

## Slide 8: Business drivers
MNO
NW/UE vendor
SupNet
Provider
Network Participant
(SupNet owner, Users)
Gain: Reduced cost for Coverage /Capacity extension
Gain: Roaming / Service fee, Data offloading reward
Gain: Selling SupNet NW, PoC devices
Gain: Reward for participating in
- Data offloading
- Proof of Coverage / Usage

## Slide 9: High-level concepts
Coverage & capacity extension service (to MNO / PLMNs)
Proof of Coverage / Proof of Usage
SupNet Provider
SupNet RAN
PoC participants
(Assisting UE)
Normal UEs (using SupNet RAN)
Proof of coverage
Proof of usage
PLMN A
PLMN B
PLMN C
Sharing coverage/ offloading data
SupNet Provider
SupNet RAN nodes/cells

## Slide 10: Areas/Topics for SA1 study
Coordination bw SupNet provider and MNO for coverage/capacity extension service, e.g.:
  To negotiate area/time for coverage/capacity extension, how much traffic/UEs are expected
  To determine/select candidates SupNet nodes, update the configuration to serve the request from the MNO
Authorization and configuration of the SupNet network, e.g.:
  How to support authorization of SupNet nodes
  How to configure SupNet network
  How to enforce a policy that MNO requires
Proof of Coverage, e.g.:
  How to verify the location & coverage of the SupNet nodes
  How to verity the operation time of SupNet nodes (e.. To verify availability of the network –24 hrs, part time, etc.)
  How to authenticate/authorize the participants and the transactions for Proof of Coverage operation
Proof of Usage, e.g.:
  How to authenticate the UE accessing the SupNet NW (UE with MNO credential)
  Monitoring RAN/CN performance, and the amount of data offloaded

## Slide 11: ANNEX 2 (Answers/clarifications to comments & questions raised in S1-104)

## Slide 12: Clarifications (1/2)
Setup/Config of Supnet (how/by who)?
  Anyone who buys SupNet node becomes SupNet owner
  SupNet node owner selects SupNet provider and enrolls.
  SupNet provider manages the enrolled SupNet node, and provides incentives for contributing coverage/capacity extension
  SupNet node owner can change SupNet provider at will
UE authorization (how/by who)?
  A-UE:
    A-UE needs to enroll SupNet provider to participate Proof-of-coverage program.
    A-UE is authorized by SupNet provider
    SupNet provider incentivizes A-UE according to its Proof-of-coverage record
  UE accessing to SupNet UE
    It is a normal UE (if SupNet node serves MNO frequency band) or roaming UE (if SupNet node serves CBRS, or if SupNet node services PLMN with roaming agreement). No specific handling of authorization is needed.
Clarify what CN functions can be managed by SupNet
  It depends on deployment scenarios.
    thin CN (e.g., only providing gateway to access to MNO’s CN), or
    min CN feature e.g., only providing local data offloading (Session management to establish PDU session for local DN), or basic access and mobility management (if needed)
    full CN if SupNet provider is private network provider.

## Slide 13: Clarifications (2/2)
Relationship with PLMN MNO?
  normal inbound/outbound roaming?
    Same as current roaming architecture and principles.
  What is the MNO role?
    To request coverage/capacity extension to SupNet provider, and provides requirements for coverage/capacity, and radio configuration parameters.
  Clarify diff with RAN sharing or private network, or VMR.
    It is orthogonal. SupNet node can be VMR. Only difference will be whether/how to be connected to MNO’s Core Network.
Reporting of PoC (to who)?
- PoC is managed by SupNet provider
- A-UE sends the report of PoC to SupNet provider.
- user awareness?
- User of A-UE has to be aware as it requires to enroll PoC program of SupNet provider