## Slide 1: Motivation for a Study on satellite access - Phase 4
Novamint, Thales, Airbus, Eutelsat Group, Fraunhofer IIS, TNO, ESA, SES, ETRI, vivo, SKY Perfect JSAT, Sateliot, Lockheed Martin, Hughes Network systems, CATT, Nokia, Nokia Shanghai Bell, OQ Technology, China Telecom, Firstnet

## Slide 2: Outline
Where we are:
  New capabilities have been addressed in SA1 5GSat phase 3 for Release 19:
    Store and Forward Satellite operation for delay-tolerant communication services
    UE-Satellite-UE communication (without the user data going through the ground network)
    GNSS independent operation
    Positioning enhancements for satellite access
  First commercial deployments of 5G based satellite are happening and many new use cases/demands for satellite access emerging to be addressed still in the context of 5G advanced.
  Beyond 5G Advanced, Satellite will be part of unified communication
What is expected:
  To address the use cases/service requirements and KPIs that are still part of 5G advanced

## Slide 3: Satellite access Phase 4 for 5G Advanced
Use cases/service requirements:
  Support of Multicast and Broadcast Services (MBS) over satellite
  Enhanced support for emergency communications and mission critical services via satellite
  Enhanced support for multi-orbits satellite networks
  Enhanced Network selection between satellites including roaming between multi orbits satellites or between satellites and terrestrial
  Enhanced resilient UE-Satellite-UE communication with intermittent ground connectivity
  Enhanced Satellite sharing for network entities on-board satellite
KPIs
  Review KPIs of 5G satellite networks (especially for service to vehicular/drone mounted devices for verticals),
  Clarify KPIs associated to service continuity
See back up slides for details

## Slide 4
Details of objectives for study on Satellite Access phase 4

## Slide 5: Support of Multicast and Broadcast Services (MBS) over satellite
Context/Motivation:
  Broadcast services constitute more than 50% of the revenue of satellite operators today based on classical DVB systems.
  A migration to 3GPP based technology shall enable MBS services to be available to allow a smooth evolution of the satellite operator’s broadcast services.
  MBS has the potential to complement the terrestrial and satellite networks with an efficient means to multicast and broadcast content to the end users which can provide substantial improvements, especially regarding efficient resource usage to distribute content, such as software updates, media content for example
  New service requirements are needed to support this (see contribution S1-240064 on Use Cases motivations for 5G MBS over NTN)
Objectives for Rel-20
  Identify New service requirements
  Gap analysis

## Slide 6: Enhanced support for emergency communications/mission critical via satellite
Context/Motivation:
  Strong demand to be able to have enhanced support for emergency communication via satellite
    Emergency call for automotive
    Emergency messaging for handsets or devices
    …
  New regulation is expected with more stringent requirements
  Impacts of regulation on those services for satellite access need to be assessed
Objectives for Rel-20
  Impact of evolving regulatory requirements (i.e. UE location accuracy)
  Gap analysis

## Slide 7: Enhanced support for multi-orbits satellite networks
Context/Motivation:
  Several satellite operators are expected to deploy multi-orbits satellite networks combining LEO, MEO and GEO
  Mega constellation likely to require new service requirements
  There are several aspects to investigate such as QoS, SLA, traffic/resources/energy consumption management…
Objectives for Rel-20
  Identify New service requirements
  Gap analysis

## Slide 8: Network selection between NTN and NTN/TN
Context/Motivation:
  Network selection between NTN/NTN
    Roaming between multi orbits satellites
    Parameters to consider (policies depending on the location, selection based on metrics, part of mega constellation, availability of the coverage if discontinuous…)
  Network selection between NTN/TN
    New parameters to consider
Objectives for Rel-20
  Identify New service requirements
  Gap analysis

## Slide 9: Enhanced resilient UE-Sat-UE communication with intermittent ground connectivity
Context/Motivation:
  In case of ground disaster or ground connection failure (ISL outage or feeder link failure), there is need to have more robust and resilient satellite access system
  UE-Satellite-UE communication with intermittent ground connectivity needs to be enhanced to support such resilience
Objectives for Rel-20
  Identify New service requirements
  Gap analysis

## Slide 10: Enhanced Satellite sharing for network entities on-board satellite
Context/Motivation:
  Consider the different scenarios of sharing entities on-board satellite with MNOs for services/features based on different business models/needs
  Take into account the security (e.g. Lawful Interception), charging, roaming, hide complexities related to satellite communication from MNOs…
  Take into consideration regulatory aspects to support network sharing between the satellite operators and terrestrial MNOs (e.g. one satellite network shared with different MNOs in different geographical areas).
Objectives for Rel-20
  Identify New service requirements
  Gap analysis

## Slide 11: Enhanced Satellite access KPIs
Context/Motivation:
  KPIs for a 5G system with satellite access have been introduced in TS 22.261 (section 7.4) in the context of Rel-16
  Since they have not been updated and do not reflect KPIs for 5G Advanced
  This is especially valid for service to vehicular/drone mounted devices for verticals
  It is important to review the KPIs of 5G satellite networks
  Furthermore, there is a need to clarify KPIs associated to service continuity
Objectives for Rel-20
  Review and update KPIs of 5G satellite networks, especially to study use cases of vehicular/drone mounted devices/IoT devices serving vertical through satellite access.
  Clarify KPIs associated to service continuity