## Slide 1: Discussion on Disaster Communication Service (DCS) without Centralized 5G Core
3GPP TSG SA1 #105 meeting
February 26 – March 1, 2024
Agenda Item: 7
TDOC#: S1-240028
For: Discussion
Source: US Department of Homeland Security, Homeland Security Systems Engineering and Development Institute (HSSEDI), an FFRDC Operated by the MITRE Corp. under contract to DHS
TSG SA1 #105 meeting
February 26 – March 1, 2024
S1-240028

## Slide 2: What is Disaster Communication Service (DCS)?
Disaster Communication Service (DCS): A 5G system supports instant direct device connection with ProSe UE-to-UE Relays where a 5G core cannot be accessed during disaster’s condition for public safety subscribers.

## Slide 3: Why do we need DCS?
There are use cases where user equipment (UE) is not able to get access to a centralized 5G core due to a) 5G gNBs are not available, b) a 5G core is not available, or c) both 5G gNB and a 5G core are not available Here are a few use cases.

## Slide 4: Use Cases
There are natural disasters, such as a) hurricane, b) flood, c) earthquake, and d) wildfire or war, destroy 5G cellular infrastructure and power infrastructure.
In this natural disaster use case, first responders as well as search and rescue teams from different areas, including different countries, gather at the scene to conduct rescue missions. They need instant and on-the-fly, device-to-device communications (i.e., direct device connection as defined in TS 22.261) between them to share critical information, coordinate response operations, and conduct damage assessment, using 5G devices, which are the only common communication devices available.

## Slide 5: Do we need authentication in DCS?
The direct device connection is to leverage 5G New Radio (NR) sidelink technology with ProSe UE-to-UE Relays to support out-of-coverage cases. This deployment scenario is already supported by SA2 architecture.
For public safety subscribers, to prevent 3rd parties from listening or disrupting communications, there is a need to provide authentication.
One current practice used to support authentication in out-of-coverage cases with sidelink technology has the following steps:
  1) UEs are authenticated while in-coverage with an 5G infrastructure network first (with a centralized 5G core)
  2) security credentials are pre-provisioned to UEs
  3) UEs join the out-of-coverage network.
However, during the natural disaster use case discussed, steps 1) and 2) cannot be done because there is no 5G gNB or centralized 5G core available and there are often first responders from other locations providing assistance. As a result, we need to extend the current 5G capabilities with new requirements to support instant and on-the-fly direct device connection leveraging sidelink technology with ProSe UE-to-UE Relays for public safety personnel during disaster condition.

## Slide 6: Can solutions leveraging ad-hoc infrastructure-based 5G systems meet the requirements in the use cases?
The infrastructure-based 5G systems could be 5G cell on wheels (COWS) and /or 5G systems in a box (e.g., solutions proposed in 4G Isolated Operation for Public Safety [IOPS]). However, from past experiences, it took days for 5G systems to be properly configured and deployed to cover all the areas affected by the disaster and to hand out SIM cards to public safety personnel. During those days when there were no cellular communications, precious human lives were possibly lost.

## Slide 7: Gap analysis of the current 5G specifications for supporting the proposed requirements
3GPP TS | Relevant texts and their purpose | Regular or public safety subscribers | Access to gNB required? | Access to core required? | Access to 5G NR sidelink required?
Proposed DCS | A 5G system supports instant direct device connection where a 5G core cannot be accessed during disaster’s condition. | Public safety only | No | No | Yes (pre-provisioning of security credentials is not required for UEs) (Support direct device connections leveraging sidelink with U2U relays)
IOPS 23.180 (SA6) 23.401 (SA2) 22.346 (SA1) 22.280 (SA1) | The IOPS mode of operation is defined in 3GPP TS 23.401 Annex K. “IOPS-capable eNodeB is co-sited with, or can reach, a Local EPC instance which is used in IOPS mode.” without the support of backhaul communications. It is for LTE only. | Public safety only | Yes | Yes | No
Disaster roaming 22.261 (SA1) | “provide the 5GS with the capability to mitigate interruption of service. UEs can obtain service in the event of a disaster, if there are PLMN operators prepared to offer service.” | All | Yes | Yes | No
IOPS: Isolated Operation for Public Safety
TS 23.180 "Mission critical services support in the Isolated Operation for Public Safety (IOPS) mode of operation; Functional architecture and information flows".
TS 23.401 "General Packet Radio Service (GPRS) enhancements for Evolved Universal Terrestrial Radio Access Network (E-UTRAN) access".
TS 22.346 "Isolated Evolved Universal Terrestrial Radio Access Network (E-UTRAN) operation for public safety; Stage 1“
TS 22.280 "Mission Critical Services Common Requirements (MCCoRe); Stage 1"
TS 22.261 “Service requirements for the 5G system”

## Slide 8: Gap analysis (Cont’d)
3GPP TS | Relevant texts and their purpose | Regular or public safety subscribers | Access to gNB required? | Access to core required? | Access to 5G NR sidelink required?
Emergency services 22.101 (SA1) 23.304 (SA2) 33.503 (SA3) | “10 Emergency calls” “10.12 Emergency Sessions over Relay UEs … Where the 5G system supports remote UE access to emergency sessions via relay UEs, the following requirements apply: - Subject to local regulatory requirements, the UE shall first attempt to make an emergency session via any available network. If the UE fails to find a network that allows emergency sessions, the UE shall attempt an emergency session via a relay UE.” “5.4.4 Support of emergency service from 5G ProSe Remote UE via 5G ProSe UE-to-Network Relay” “When a 5G ProSe enabled UE does not have direct connection to the network for emergency service, the UE may attempt to obtain emergency service via 5G ProSe Layer-2 or Layer-3 UE-to-Network Relay. A 5G ProSe enabled UE acting as 5G ProSe UE-to-Network Relay shall have a normal registration ....” “6.3.6 Security for emergency service from 5G ProSe Remote UE via 5G ProSe UE-to-Network” | All (for emergency calls only) | Yes (for (U2N relays) | Yes (for (U2N relays) | Yes (leveraging sidelink with U2N relays only)
TS 22.101 "Service aspects; Service principles"
TS 23.304 "Proximity based Services (ProSe) in the 5G System (5GS)"
TS 33.503 "Security aspects of Proximity based Services (ProSe) in the 5G System (5GS)"

## Slide 9: Gap analysis (Cont’d)
5G sideink use cases including V2X 23.287 (SA2) | Note: A subscriber needs to authenticate with the core first before using the services. “V2X communication: A communication to support Vehicle-to-Everything (V2X) services leveraging Uu and / or PC5 reference points.” | All | Yes for authentication / No for out-of-coverage communication* | Yes for authentication / No for out-of-coverage communication* | Yes (Pre-provisioning of security credentials is required for UEs)
Mission critical services 22.179 (SA1) 22.280 (SA1) | Note: A subscriber needs to authenticate with the core first before using the services. Off-Network Mission Critical Push To Talk (MCPTT Service): “The collection of functions and capabilities required to provide MCPTT using ProSe Discovery and the ProSe Communication path for MCPTT Users using Public Safety ProSe-enabled UEs as a direct communication between UEs.” + Mission Critical Applications (MCX): “Generic communication applications with mission critical characteristics, traditionally encompassing push-to-talk voice (MCPTT), real-time video (MCVideo) and real-time data (MCData).” Off-network Ad hoc Group Communication "The off-network MCX Service shall provide a mechanism to combine an ad hoc multiplicity of MCX Users within communication range into a group communication." | Mainly for Public safety | Yes | Yes | Yes
*1) UEs are authenticated while in-coverage with an infrastructure network (with a centralized 5G core), 2) security credentials are pre-provisioned to UEs, and then 3) UEs join the out-of-coverage network.
TS 23.287 "Architecture enhancements for 5G System (5GS) to support Vehicle-to-Everything (V2X) services"
TS 22.179 "Mission Critical Push To Talk (MCPTT); Stage 1"

## Slide 10: Seeking Feedback and Partners
We are here to seek feedback and advice from this group for the proposal.
Options:
  We may develop CRs to update current requirements to define disaster communication service (DCS) without a centralized 5G core in TS 22.261, where DCS is defined as a 5G system supports instant direct device connection with ProSe UE-to-UE Relays where a 5G core cannot be accessed during disaster’s condition for public safety subscribers.
  We may submit a R-20 mini-WID along with the CRs.
  Other?