## Slide 1
Enable Quantum-Safe Cryptography for 6G
Source: ISSDU, III, NYCU, GE Network Technologies
Agenda item: 8
Document for: Discussion
Contact: Feng-Ming Yang kelvinfomi@issdu.com.tw
Yi-Hsueh Tsai lucas@iii.org.tw
En-Cheng Liou ecl@nycu.edu.tw
Stephen F Bush stephen.bush@ge.com
S1-241240, 3GPP TSG WG1#106, May 27-31, 2024, Jeju, South Korea

## Slide 2: Outline
Quantum Safe Cryptography (QSC) for 6G?
SA3 Relevant TRs for QSC
SA3 Relevant TSs for QSC
Why 6G Need to Migrate to QSC?
Why 6G Need to Quantum Key Distribution (QKD)?
Proposal
  Enabling Quantum Safe Cryptography (QSC) in Release 20.
  Enabling Quantum Key Distribution (QKD) in future Release.

## Slide 3: Quantum Safe Cryptography (QSC) for 6G?

## Slide 4: SA3 Relevant TRs for QSC
Algorithm | Key Length | Effective Key Strength / Security Level | 
 |  | Conventional Computing | Quantum Computing
RSA-1024 | 1024 bits | 80 bits | 0 bits
RSA-2048 | 2048 bits | 112 bits | 0 bits
ECC-256 | 256 bits | 128 bits | 0 bits
ECC-384 | 384 bits | 256 bits | 0 bits
AES-128 | 128 bits | 128 bits | 64 bits
AES-256 | 256 bits | 256 bits | 128 bits
Comparison of conventional and quantum security levels of some popular ciphers

## Slide 5: SA3 Relevant TSs for QSC
SNOW 5G
AES-256
ZUC-256
MILENAGE-256

## Slide 6: Why 6G Need to Migrate to QSC?
As specified in clause 6.12.2 of 3GPP TS 33.501, the SUCI is generated using a protection scheme such as Elliptic Curve Integrated Encryption Scheme (ECIES) with the Home Network public key.
The main vulnerability of the ECIES protocol with respect to the quantum threat is actually the Diffie-Hellman key exchange step, regardless of the used profile.
Source: PQ.03-Post-Quantum-Cryptography-Guidelines-for-Telecom-Use-v1.0

## Slide 7: Why 6G Need to Quantum Key Distribution?
For industrial control system use, we are concerned that the increasing complexity of classical Quantum-Safe Cryptography (QSC) is too slow and unsuitable.
Introducing Quantum Key Distribution (QKD) technology reduces overhead, shortens latency, and provides warnings of eavesdropper attacks.

## Slide 8: Proposal
To study potential requirements for enabling Quantum Safe Cryptography (QSC) in Release 20 (part 2).
To study potential requirements for enabling Quantum Key Distribution (QKD) in future Release.
  Consider combining post-quantum cryptography (classical) and QKD (quantum).

## Slide 9: Thank You!
Source: https://youtu.be/6lPZWzR0pms?si=2R7rNE-N8VQ9Rpp9