## Slide 1
Lessons learnt from 5G study: Coordination with SA2 study
Source: Nokia
Agenda item: 10.2
Document for: Discussion
© 3GPP 2024
S1-241243 (revision of S1-241168) - 3GPP SA1#106, 27 - 31 May 2024, Jeju, Korea

## Slide 2: 5G SA2 Study on Architecture for Next Generation System
Focus the analysis on high level architectural requirements in TR 23.799
SP-160727: Service requirements are anticipated from SA1 SMARTER output. The architecture defined in this SI should be able to support those requirements.

## Slide 3: SA2 5G study analysis methodology
Include all SA2 high-level requirements and mark those irrelevant ones.
Within one requirement, include not SA1 relevant part for completeness.
For the evaluation of SA1 cover or not, only SA1 relevant part is considered.
Check TS 22.261 v16.6.0 (at the time of SMARTER_Ph2 completion Dec. 2018) and other SA1 R16 TS to see what were taken up by SA1 normative work.
Covered, partially covered, not covered

## Slide 4: High level architectural requirements (1)
SA2 requirements | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
1. Support the new RAT(s), the Evolved E-UTRA, and non-3GPP access types. GERAN and UTRAN are not supported. | TR 22.864 clause 7.13.1, 7.13.2 [PR 5.7.2.3-001] | TS 22.261 clause 6.3.2.1, 6.3.2.2, 5.1.2.2 | 
2. Support unified authentication framework for different access systems. | TR 22.861 [PR 5.1.3.5-002] | TS 22.261 clause 8.3 | Unified framework not covered.
3. Support multiple simultaneous connections of an UE via multiple access technologies. | TR 22.864 clause 7.13.1, 7.13.2 | TS 22.261 clause 6.3.2.1, 6.3.2.2 | 
4. Allow independent evolutions of core network and RAN, and minimize access dependencies. |  |  | Not relevant
5. Support a separation of Control plane and User plane functions. |  |  | Not relevant
6. Support transmission of IP packets, non-IP PDUs and Ethernet frames. |  | TS 22.261 clause 6.5.1, 6.24.2 | 
7. Leverage techniques (e.g. Network Function Virtualization and Software Defined Networking) to reduce total cost of ownership; improve operational efficiency, energy efficiency, and simplicity and flexibility for offering new services. | TR 22.864 clause 7.1, 7.2, 7.11, 7.13.6 | TS 22.261 clause 6.1.2, 6.4.2, 6.5.2, 6.6.2, 6.15.2 | TCO not covered.
8. Efficiently support different levels of UE mobility (including stationary UE(s)) / service continuity. | TR 22.864 clause 7.10, 7.14.3 | TS 22.261 clause 6.2.2, 6.2.3, 6.4.2.1 | 
9. Support different levels of resilience for the services provided by the network. | TR 22.862 [CPR 7.7-019] |  | 
10. Support different means for reducing UE power consumption while UE is in periods with data traffic as well as in periods without data traffic. | TR 22.864 [PR 5.1.2.6-010] | TS 22.261 clause 6.15.2 | Not explicit on UE in periods with and without traffic.

## Slide 5: High level architectural requirements (2)
SA2 requirements | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
11. Support services that have different latency requirements between the UE and the Data Network. | TR 22.891 clause 6.3.2 TR 22.862 [CPR 7.2-001] [CPR 7.3-001] [CPR 7.3-002] [CPR 7.4-001] [CPR 7.5-001] [CPR 7.6-001] [CPR 7.7-001] TR 22.864 [PR 5.6.2-031] | TS 22.261 clause 7.2.2 TS 22.104 clause 5.2, 5.3, 5.5, 5.7 TS 22.186 clause 5.2, 5.3, 5.4, 5.5 TS 22.289 clause 5.2.2 | 
12. Minimize the signalling (and delay) required to start the traffic exchange between the UE and the Data Network, i.e. signalling overhead and latency at transition from a period where UE has no data traffic to a period with data traffic. | TR 22.861 [PR.5.1.3.3-001] TR 22.864 [PR 5.1.2.6-002] | TS 22.261 clause 6.4.2.4 | 
13. Support access to applications (including 3rd party applications) with low latency requirements hosted close to the access network within the operator trust domain. | TR 22.864 [PR 5.1.2.2-003] [PR 5.4.2-001] | TS 22.261 clause 6.6.2 | 
14. Support optimized mechanisms to control (includes avoiding) signalling congestion. | TR 22.864 [PR 5.2.2-004] |  | More specific on the increase of signalling capacity in TR.
15. Efficient network support for a large number of UEs in periods without data traffic. | TR 22.861 [PR.5.3.3.1-002] [PR.5.3.3.1-003] | TS 22.261 clause 6.4.2.2 | Not explicitly on UEs without data traffic.
16. Support network sharing. | TR 22.864 [PR 5.5.2-006] [PR 5.5.2-007] | TS 22.261 clause 6.21.2, 6.22.2.1 TS 22.101 clause 4.9, 28 | Fronthaul/backhaul network sharing in TR.
17. Support roaming. | TR 22.864 [PR 5.7.2.1-001] | TS 22.261 clause 5.1.2.1 TS 22.101 clause 17 | 
18. Support broadcast services. | TR 22.864 clause 7.4 | TS 22.261 clause 6.13.2 TS 22.146, TS 22.246 TS 22.101 clause 32 | 
19. Support network slicing. | TR 22.891 clause 5.2 TR 22.864 clause 7.1 | TS 22.261 clause 6.1 | 
20. Support Architecture enhancements for vertical applications. |  |  | Not relevant

## Slide 6: High level architectural requirements (3)
SA2 requirements | SA1 FS_SMARTER TR reference | SA1 R16 TS reference | Comment
21. Support dynamic scale-in /scale-out. | TR 22.864 [PR 5.2.2-001] [PR 5.2.2-002] | TS 22.261 6.26.2.3 | Only for 5G LAN-VN in TS.
22. Minimize energy consumption in the overall network operation. | TR 22.864 [PR 5.6.2-025] | TS 22.261 clause 6.15 | 
23. Support critical communications, including mission-critical communications. | TR 22.862 | TS 22.104, 22.179, 22.186, 22.268, 22.280, 22.281, 22.282, 22.289, 22.468 | 
24. Support network capability exposure. | TR 22.864 clause 7.3 | TS 22.261 clause 6.10 | 
25. Support efficient transmission of user data with characteristics required by Stage 1 requirements (e.g. low throughput short data bursts) including support of SMS. | TR 22.864 [PR 5.1.2.2-007] | TS 22.261 clause 6.4.2.1 TS 22.101 clause 6 TS 22.262 | Not explicitly on SMS support in TR.
26. Support regulatory requirements for Lawful Intercept. | TR 22.864 [PR 5.1.2.2-006a] [PR 5.4.2-002a] | TS 22.261 clause 8.6 | 
27. Support a flexible information model with relationships between user related managed data, and with a level of abstraction sufficient to be independent of any specific protocols. |  |  | Not relevant
28. Support optimized distribution of the data and the location of the data repositories in the network (access and core network) for efficient management of user related data by network entities. |  |  | Not relevant
29. Support for location services as per the related service requirements and in alignment with NR RAN TR 38.913. | TR 22.862 clause 5.4 | TS 22.071 | 
30. Support regulatory requirements for Public Warning System (PWS), e.g. ETWS, CMAS, KPAS, etc. | TR 22.891 clause 5.4.2 | TS 22.268 | 

## Slide 7: Some observations from 5G
Chart: Study
| Covered | Partially covered | Not covered
Study | 18 | 6 | 1
Chart: 
| Umbrella | eMBB | mIoT | CRIC | NEO
Study | 3 | 0 | 3 | 4 | 18
Chart: 
| SMARTER | Other TS
Normative work | 20 | 8
In total, 25 high level architectural requirements relevant to SA1
Chart: Normative work
| Covered | Partially covered | Not covered
Normative work | 18 | 5 | 2
NOTE: Sum of the pie chart is not aligned with the sum of “(partially) covered” as some requirements are covered by multiple TR/TS.

## Slide 8: Lessons learnt from 5G
SA1 should provide high level input to SA2 architecture study before they start.
Alignment between SA1 and SA2 is needed.
Most high-level aspects can be input to SA2 study without deriving from detailed use case description, but justification needed.
Transversal aspects can be captured in one TR.
Numbering of normative requirements can facilitate tracking.