## Slide 1
China Telecom
Discussion on Authorization for Relay UE Based on Access Network

## Slide 2
  Motivation
Indirect network connection could provide means for UE that is out of cellular coverage to connect to the network using another UE as a relay UE. For 5G system with satellite access, it is supported that the relay UE could access via satellite in the earlier release.
Due to the low transmission rate and narrow transmission bandwidth of satellite access, when the relay UE connecting to the 5G network via satellite access, user experience of the remote UE and relay UE might be affected.
From the operator’s perspective, in order to provide better user experience, operator should be able to control the authorization for the relay UE based on the access network. For example, the operator could authorize a UE as relay UE when it is accessing via the terrestrial network but not via the satellite network.

## Slide 3
  Proposal
It is proposed to add a requirement to TS 22.261 clause 6.9.2.3 on providing network operator mechanism to authorize a UE based on the access network.
6.9.2.3 Permission and Authorization
The 5G system shall enable the network operator to authorize a UE to use indirect network connection. The authorization shall be able to be restricted to using only relay UEs belonging to the same network operator. The authorization shall be able to be restricted to only relay UEs belonging to the same application layer group.
The 5G system shall enable the network operator to authorize a UE to relay traffic as relay UE. The authorization shall be able to allow relaying only for remote UEs belonging to the same network operator. The authorization shall be able to allow relaying only for remote UEs belonging to the same application layer group.
Subject to operator policy, the 5G system shall be able to support network operator to authorize a UE based on the access network to relay traffic as relay UE, e.g. not authorized while the UE access via the satellite.
The 5G system shall support a mechanism for an end user to provide/revoke permission to an authorized UE to act as a relay UE.
The 5G system shall support a mechanism for an authorized third-party to provide/revoke permission to an authorized UE to act as a relay UE.
The 5G system shall provide a suitable API by which an authorized third-party shall be able to authorize (multiple) UEs under control of the third-party to act as a relay UE or remote UE.
The 5G system shall provide a suitable API by which an authorized third-party shall be able to enable/disable (multiple) UEs under control of the third-party to act as a relay UE or remote UE.

## Slide 4
THANKS
感 谢 聆 听