## Slide 1: New MCX Ambient Listening requirements - pause and resume
Sivasubramaniam Ramanan & Mythri Hunukumbure
UK Home Office

## Slide 2: Introduction
We propose mini-wID to introduce pause and resume option for ambient listening calls, if the ‘MCPTT User being ambient listened to’ starts an MCPTT Private Call or an MCPTT Group Call.
Pause and resume is very useful in certain operational scenarios for emergency personnel (ambulance, police) and control rooms/dispatchers.
The need to monitor the ‘ambient listened to user’ does not cease simply because they become involved in another call. Otherwise, the ‘ambient listener’ user has the overhead of having to restart the ambient listening call manually. Unless this is done automatically by the client as a locally initiated ambient listening call.

## Slide 3: Ambient Listening termination (existing requirements in SA1 docs)
3GPP TS 22.280 on Ambient Listening
Remotely initiated ambient listening requirements
[R-6.15.2.2.2-002] The MCX Service shall ensure that Ambient Listening triggered remotely is terminated only by the remote authorized MCX User (e.g., a dispatcher).
Locally initiated ambient listening requirements
[R-6.15.2.2.3-002] The MCX Service shall ensure that Ambient Listening triggered locally can be terminated by the MCX User being listened to or by the remote MCX Service Administrator and/or authorized user, who was the listening Participant.
3GPP TS 22.179 on Ambient Listening
[R-6.16.2.2.1-004] The MCPTT Service shall terminate Ambient Listening if the MCPTT User being listened to starts to transmit in an MCPTT Private Call or an MCPTT Group Call.
NOTE: An authorized MCPTT User could initiate Discreet Listening at this point if needed.

## Slide 4: Pause and resume for ambient listening
Pause – pauses the ambient listening call when an interrupting event (eg, incoming or outgoing call) detected at the “MCPTT User being ambient listened to”
Resume – “MCPTT User being ambient listened to” automatically initiating a locally initiated ambient listening call back to the originator of the initial (interrupted) remote ambient listening call, once the interrupting event (eg, incoming or outgoing call) has concluded.

## Slide 5: Potential new useful usecases
An Ambient Listening call could pause instead of termination if the ‘MCPTT User being ambient listened to’ initiates a call request for another call or receives an incoming call.
A successful call request for an ‘MCPTT User being ambient listened to’ should cause the Ambient Listening call to pause until the requested call has completed at which point the Ambient Listening call could resume.
Incoming or outgoing call requests for an ‘MCPTT User being ambient listened to’ should be treated the same way as if they were not involved in an Ambient Listening call and the calls should be setup as if Ambient Listening was not taking place.

## Slide 6: Ambient listening modes
CR S1-250069 introduce enhancements/new requirements to existing ambient listening procedures. Currently we are limiting the changes to MCPTT (i.e., voice only).
We see three options for an MCX ambient listening calls when there is an interrupting event. Choice would be left to the deployment/implementation.
Terminate mode
Pause and resume mode
Parallel mode – both ambient listening and MCPTT calls continue – allowing two calls running in parallel. This can be an additional optional requirement. In this mode ambient listening should continue without interruption during either an outgoing or incoming call.

## Slide 7: Next steps
Consider the draft new mini-WID on ambient listening, proposing additional new requirements to TS 22.179 (MCPTT), which are required by the MCX community