## Slide 1: Discussion Paper for SA2 LS on SIPTO Requirement Clarification
Agenda Item: 4
Source: NEC
S1-122157

## Slide 2: What is SIPTO@LN
SIPTO @ Local Network
  A feature that enables the mobile operator to offload “selected IP Traffic” via an H(e)NB in the Local Network in order to reduce the traffic load towards the core network
  SIPTO@LN is a new operator feature, that enables radio and core network traffic offload

## Slide 3: Background
Since Rel-10, SA1 has the following general requirement documented in TS 22.101:
It shall be possible to perform Selected IP Traffic Offload for pre-Release 10 UEs.
However, in the context of SIPTO @ Local Networks (i.e. for Femto traffic offload), SA1 also documented the following requirement for “selected IP traffic offload” in TS 22.220
The SIPTO policies may be defined per APN or per IP flow:
  SIPTO policies per APN indicate whether all traffic associated with a specific APN is subject to offload;
  SIPTO policies per IP flow are routing policies indicating which APN to use for a specific IP flow.

## Slide 4: SA2 Question
Does the general stage-1 requirement for SIPTO in TS 22.101, namely “to support ‘selected IP traffic offload’ for pre-Release 10 UEs” apply to both:
SIPTO at the granularity of APNs
SIPTO at the granularity of IP Flows

## Slide 5: What does SIPTO at the granularity of APN mean?
SIPTO at the granularity of APNs means that all traffic associated with an APN is offloaded
How do UEs associate traffic with an APN today?
  Pre-Rel-10 UEs (including most smartphones) typically support only few APNs
    For example, in the case of iPhones the following APNs are typically supported:
      Cellular Data APN: for all Internet traffic (i.e. this is the default APN which all normal Apps use)
      MMS APN: for MMS
      (Optional) Voice APN: for voice mail or VoIP
  Certain applications (e.g. MMS, voice apps) can be associated with dedicated APNs (e.g. MMS APN)
  All other applications are associated to the default cellular data APN
SIPTO at the granularity of APN means:
  “All or nothing” – either offload all internet traffic or nothing
  There is not possibility to offload certain types of internet traffic (e.g. FTP, Dropbox or NetFlix)

## Slide 6: SIPTO at the granularity of APN
S-GW
HeNB
HNBGW
P-GW
If Internet PDN connection is not offloaded
L-GW
If Internet PDN connection is offloaded
Home / Enterprise Network
Internet
Data Apps
Pre-Rel-10 UE
Internet APN / PDN Connection
Option 1: Anchored at Core P-GW
Option 2: Anchored at L-GW
Internet
“All or nothing”
EITHER offload ALL Internet Apps OR NONE
XOR

## Slide 7: What does SIPTO at the granularity of IP Flows mean?
SIPTO at the granularity of IP Flows means that selected IP flows can be offloaded
How can operators define which IP flows to be offloaded?
  Through SIPTO policies, which define exactly which IP flows should be offloaded based on source/destination IP addresses, source/destination ports, protocol types, etc.
    For example, to offload all FTP traffic, the policy could like like:
      <Src IP=*, Dst IP=*, Src Port=*, Dest Port=21, Protocol=*>  offload
    or to offload all NetFlix traffic the SIPTO policy could look like:
      <Src IP=*, Dst IP=<IP address of NetFlix Server>, Src Port=*, Dest Port=*, Protocol=*>  offload
Where are the policies enforced?
  The policies can either be enforced in the network (case 1) or at the UE (case 2)
SIPTO at the granularity of IP Flows means:
  Operators can (if they want) control in a fine-grained manner which traffic to offload
  For example, operators can offload only high-volume traffic such as YouTube, NetFlix, Dropbox, but keep other internet traffic in their network (e.g. to enforce content filtering, etc.)

## Slide 8: SIPTO at the granularity of IP Flows
L-GW
S-GW
HeNB
HNBGW
P-GW
Default Internet APN / PDN Connection
L-GW
SIPTO@LN APN / PDN Connection
Home / Enterprise Network
Internet
Data Apps
Special UE Functionality required (i.e. Rel-12)
Internet
S-GW
HeNB
HNBGW
P-GW
Internet PDN connection
Selected IP Traffic offload by L-GW (transparent to UE)
Home / Enterprise Network
Internet
Data Apps
Internet
Traffic Offload Policy
Enforcement in network
Traffic Offload Policy
Enforcement in UE
Pre-Rel-10 UE
Option 1:
Without UE impact
Option 2:
With UE impact

## Slide 9: Conclusions and Way Forward
Conclusions:
SIPTO at the granularity of APNs offers operators only “all-or-nothing” offload control
SIPTO at the granularity of IP Flows offers operators fine grained control on which traffic should be offloaded (e.g. NetFlix yes, but Email no)
SIPTO@LN at the granularity of APNs can be supported by pre-Rel-10 UEs
SIPTO@LN at the granularity of IP Flows can be supported by pre-Rel-10 UEs, but a network based traffic offload enforcement is required
SIPTO@LN at the granularity of IP Flows where the offload policies are enforced at the UE is not supported by pre-Rel-12 UEs (this functionality is currently being developed by SA2)
Proposed Way Forward:
Reconfirm the stage-1 requirements with respect to SIPTO, i.e.
  Check if operators desire traffic offload control at the granularity of IP Flows for pre-Release 12 UEs
    Option 1: YES – this means SA2 has to consider a Rel-12 solution for SITPO@LN that also works with existing UEs (and not only with new Rel-12 UEs)
    Option 2: NO – this means SA1 is happy with the “all-or-nothing” offload control until Rel-12 UEs are on the market
If YES, inform SA2 accordingly in the Response LS
If NO, clarify in stage-1 specifications (e.g. TS 22.101 and TS 22.220) the agreed requirements