## Slide 1
Discussion on Long Range Cell Operation for GCSE
Yi-Hsueh Tsai, lucas@iii.org.tw Hsuan-Li Lin, Tsung-Yu Tsai, Terng-Yin Hsu, Jian-Ya Chu
Shubhranshu shubhranshu@itri.org.tw Zheng Yan-Xiu zhengyanxiu@itri.org.tw
3GPP TSG-SA WG1 Meeting #66 S1-141011 Sapporo, Japan, 12-16 May 2014
Agenda Item 5.2 - New Study and Work Items (including related contributions)
Source: III, ITRI

## Slide 2: Long Range Cell Operation
Possible usage scenarios of Long Range Cell Operation (e.g. 10-100km [1][2])
Difficulty deployment territory
  In areas such as mountain areas, jungles, deserts, or islands, long range cell can provide broadband wireless access solution with good coverage under reasonable cost.
Disaster first responder (Public Safety)
  In major disaster, the ground based communication infrastructure may suffer a severe destruction. In such cases, long range cell could be quickly deployed to temporarily replace the ground communication infrastructure and fast recover the wireless networks to enable critical information access such as the communication for rescue mission, or emergency services.

## Slide 3: Long Range Cell Operation for GCSE (1/3)
Oscar
Dashed line shows effective uplink coverage contour
eNB with limited backhaul such as satellite link
Infrastructure Communication
Roger
Peter
Partial network coverage area
Partial Network Coverage Area: A network coverage area where UE can only listen to the eNB.
UE outside the coverage contour could still listen to the message transmitted from long-rang base station and quickly join an ongoing group call
Oscar is talking
Smith

## Slide 4: Long Range Cell Operation for GCSE (2/3)
Oscar
Dashed line shows effective uplink coverage contour
eNB with limited backhaul such as satellite link
Infrastructure Communication
Roger
Peter
Partial network coverage area
Partial Network Coverage Area: A network coverage area where UE can only listen to the eNB.
UE outside the coverage contour could still listen to the message transmitted from long-rang base station and quickly join an ongoing group call
Peter is talking
Smith
ProSe Communication
Oscar’s UE act as UE-to-network relay

## Slide 5: Long Range Cell Operation for GCSE (3/3)
Oscar
Dashed line shows effective uplink coverage contour
eNB with limited backhaul such as satellite link
Infrastructure Communication
Roger
Partial network coverage area
Partial Network Coverage Area: A network coverage area where UE can only listen to the eNB.
Smith
Peter
Local routed the group-cast media transport via X2 interface between eNBs
macro eNB
Peter is talking

## Slide 6: Discussion and Proposal
In the current GCSE architecture in TR 23.768, it requires to routine all group-cast media transports to the GCSE server in EPC and registers all GCSE members to the GCSE server. Therefore, RP-140185[3] mentions that the required end-to-end delay for media transport may exceed the requirement of 150 ms, and the required time for joining an ongoing group communication may in worse case exceed the requirement of 300 ms. However, by using long-range cell, those issues can be mitigated by two reasons.
1) Comparing with the current GCSE architecture, long-range cell can shorten the required end-to-end delay by local routed the group-cast media transports to the UEs without go back to the GCSE server in order to meet the maximum latency requirement, 150ms.

## Slide 7: Discussion and Proposal
2) Comparing with the current GCSE architecture, UE could listen to the group-cast audio channel transmitted from long-rang cell without registering to the GCSE server by using a preconfigured authorization setting. As a consequence, it could quickly join an ongoing group call anonymously.
Therefore, if long range cell communications systems were available, it can ensure the group communication among Public Safety officers within its coverage. We propose to adopt S1-141012, “Support Long Range Cell Operation for GCSE”.

## Slide 8: References
REV-090003-r1, “LTE-Advanced Physical Layer”
LTE The UMTS Long Term Evolution from Theory to Practice Ed2
RP-140185, “New Work Item Description: Group Communication for E-UTRA”