## Slide 1: SMS-outbox update on Mobile
Bruno TOSSOU
ORANGE
Discussion Paper SMS-outbox update on mobile
3GPP TSG-SA WG1 Meeting #66
Sapporo, Japan, 12 -16 Mai 2014
Notes: 1

## Slide 2: Update an outgoing SMS in mobile SMS outbox
State of the art:
Today when a mobile subscriber sends an SMS from a Web portal this SMS is not updated in the SMS outbox on the subscriber’s mobile
In order to update the outgoing SMS on the mobile the subscriber needs to download a specific application on his mobile .
use case :
An application server “A” sends an SMS S to a recipient “D” on behalf of a user “U”.
Consequence:
in order to update this SMS in “U” mobile SMS outbox. It's necessary to download a specific application of “A” in “U” mobile
server “A”
SMS “S”
from “U”
to “D”
payload “hello”
“D”
“U”

## Slide 3: Update an outgoing SMS in mobile SMS outbox
Proposal to update the SMS outbox on mobile:
“A” sends a second specific SMS to “U”. In general this SMS allows the indication in the “U” outbox that the SMS “S” is sent to “D”.
Advantage of the proposal:
there is no need to download a specific application on the mobile for updating the SMS outbox the mobile “U”
server “A”
second SMS to update “U” outbox
“D”
“U”

## Slide 4: Update an outgoing SMS in mobile SMS outbox
Orange proposal :
Orange is proposing to take into account the proposed SMS indication in section A6 of TS 22.101 for approval.