## Slide 1: Secondary Access LTE (SALTE)
July 2015
S1-152300

## Slide 2: Secondary Access LTE (SALTE)
Self contained LTE networks built into various premises
Low cost delivery of high quality mobile service on-site
Office buildings
Hotels
Hospitals
Malls
E.g. in USA there is over 100’000 commercial 100’000+ sqft buildings

## Slide 3: SALTE Concept
Shared SALTE Networks
MNO Specific Primary Networks
Dual Context SALTE enabled UEs
Maintain Primary LTE Context with the primary network while connected to a SALTE network with Secondary LTE context
Create seamless service experience when switching MNO data & voice between primary and secondary networks
Primary LTE
Secondary
LTE
Self contained SALTE Network at each premises
Operates independently of the primary LTE networks
Interacts with MNO cores only for the purposes of SIM based Authentication, Authorization & Accounting
Easy configuration of SALTE network sharing between MNOs
  SALTE sharing will have no impact on how MNO UEs select their primary networks

## Slide 4: SALTE: Deployment Roles example
Mobile Operators Use SALTE networks to cost effectively serve on-site subscribers
SALTE-as-a-Service Providers
Deploy & Operate Neutral Host SALTE Networks
Premises Owners
Motivated to ensure availability of excellent mobile service on-site
SALTE Infra Vendors
Off-the-shelf SALTE infra solutions

## Slide 5: SALTE: UE Behavior Example
MNO A NW
MNO B NW
B
B
B
B
A
A
A
A
SALTE @Hotel X
Serves devices from MNOs A & B
SALTE @Enterprise Y Serves devices from MNOs A & B
X
Y
A’,B’
A’,B’
MNO A UE switches data routing between the primary MNO network and an available SALTE network
MNO B UE switches data routing between the primary MNO network and an available SALTE NW

## Slide 6: SALTE: Possible Solution Architecture
Dual Context SALTE enabled UE
Self contained SALTE Network
‘Mini 23.401 NW’’
Local breakout to Internet
Primary Network
Parallel Primary and Secondary LTE contexts
UE creates seamless service experience
PSTN
Internet
Mobile Network
SALTE Network
3GPP Mobile NW
AAA /HSS
On-site EPC
Authentication (USIM)
Authorization
Accounting
On-site eNB
AAA roaming hubs
ePDG
IMS
Option to support MNO voice over SALTE via ePDG

## Slide 7: SALTE: Possible 3GPP Spec Enhancements
SALTE System Info
  SALTE identification
  List of PLMN-IDs for which SALTE service available
SALTE discovery & selection
  Rules for discovery and selection of SALTE networks
    Similar than WiFi discovery & selection, fully decoupled from Primary PLMN selection
Dynamic control of UE SALTE selection & use
  Option for dynamic control of UE SALTE selection & use by MNO network
    Requires MNO network upgrade
SALTE registration
  Secondary SALTE authentication, SALTE authorization & SALTE accounting
SWu over SALTE
  Possibility to route also MNO services (e.g. IMS-APN) over SALTE