## Slide 1: Data off
Discussion Paper
Data off WID
ORANGE
Bruno TOSSOU
3GPP TSG-SA WG1 Meeting #72
Anaheim, CA, USA, 16-20 November 2015
Notes: 1

## Slide 2: Data off issues
Why there is a need to specify ‘Data Off’ functionality ?
Status in LTE network :
In LTE network the always-on IP connectivity for UE/users of the EPS is enabled by establishing a default EPS bearer during Network Attachment. In this case an IP address is allocated to the UE.
UE Data Off deactivated = UE setting of “Data in mode On” :
In this case UE may send data ( uplink traffic ) to external Server (OTT server ) or receive data from external Server ( downlink traffic )
UE Data Off activated = UE setting of “Data in mode Off” :
In this case UE do not send data ( uplink traffic ) to external Server (OTT server ) and the UE is not supposed to receive any data from external Server
UE also implement a specific Data Off feature that will only apply when the UE is in roaming abroad
Observation :
It has been noticed that in some cases UE may receive data even in the case UE setting of “ Data in mode Off”
A minimum set of services must be enabled when Data Off is activated in the mobile.

## Slide 3: Charging issue when Data Off is activated
Status :
When Data Off is activated, the UE is not supposed to receive any downlink traffic from Server but it was noted that OTT Server can still send traffic to the UE. As a consequence the PGW sends additional traffic accounting info to Charging System and thus the UE is wrongly charged for the traffic.
UE
SGW
PGW
External Server –OTT Server
Data “on “
Charging system
Uplink Traffic from UE to server
PGW sends traffic accounting info to Charging System
Data “off “
Downlink Traffic from Server to UE
1
2
3
5
4
PGW sends traffic accounting info to Charging System
3
Notes: I will explain verbally that the devices that does not carry a SIM Card must be authenticated posibility via SIM Card
the introduction with As result will be made verbally

## Slide 4: Minimum set of services when Data Off is activated
The LS SA1 received from GSMA clarifies the issue when the Data Off is activated in the device.
Issue :
It was noted that turning Data Off in 2G/3G devices deactivates at least the traffic via Internet APN and therefore stops any data flow over that APN to and from the device, and may depending on implementation also stop flows to other APNs.
In current LTE device implementations the result of turning Data Off is at this time undefined, and may differ between devices
Proposal :
To define requirements and solutions in 3GPP in order to allow a minimum set of following services when data off is activated on the device :
  •IMS Voice over PS
  •SMS over IP
  •Service management via Ut/XCAP
  •Device management over PS
  •USSI
  •IMS video call
  •GSMA defined IMS services, such as RCS
UE
Data “off “
Notes: I will explain verbally that the devices that does not carry a SIM Card must be authenticated posibility via SIM Card
the introduction with As result will be made verbally

## Slide 5: Proposal for 3GPP SA1
Based on the described charging issues and also the Data Off and Services Availability requirements from GSMA (minimum set of services that must be available when data off is activated),
it is proposed to 3GPP to approve the proposed attached WID in order to provide the necessary requirements that will allow to define the appropriates solutions for the listed above issues

## Slide 6
Thank you