## Slide 1: 3GPP PS-data off
Presentation of issues around 3GPP ps-data off feature
Daniel Lönnblad
Sony Mobile Communications
© Sony Mobile Communications

## Slide 2: Introduction
Following the discussions that took place during SA#70 plenary regarding the scope and way forward for the WID in SP-150823, this presentation aims to provide some background to the WID's scope and highlight some issues that should to be considered as part of the way forward.

## Slide 3: Ps-data off today
Today most of the smart phones have a feature to switch off data traffic either when roaming or in home network
  The behavior is different pending on handset brand, specifically when it comes to new features like VoLTE.
  Intention with switching off data is to guarantee no data will be charged either when roaming or when in home network.
  Phone can still consume data over Wi-Fi network.
  Phone calls and SMS are allowed even if data is switched off. Service sms is sent about charging for these services when entering a new country.

## Slide 4: 3GPP-Ps-data off
In SP-150823 SA1 has approved a WID that aims to specify the behavior for a function called 3GPP ps data off.
Intention is to:
  Ensure no data is sent to phone when the 3GPP-ps-data off is enabled.
  Allow VoLTE and its control services to work properly.
  Get same behavior across all brands when using this new function.
  Potentially add the possibility to enable RCS features when 3GPP-ps-data-off is enabled.

## Slide 5: Problem statement
Today data off is defined in the phone and the network is not aware when the phone has switched data off. This means data that is sent to phone will be charged even if data is set to off.
With the deployment of VoLTE it needs to be specified what data off means, eg phone calls and supplementary services should still be possible to perform.
There are also other operator services like RCS that is desired to allow as a continuation for SMS.
There are today different methods of integrating RCS in operator services and also different ways of how RCS is charged
RCS services can be offered in a phone by native applications, or third party applications or third party applications using terminal api.
RCS can use IMS apn as well as internet apn pending on operator policy. RCS can also use Wi-Fi as access.

## Slide 6: Comments on “ensure no data is sent to phone”
Ensuring no data is sent to phone when data is set to off is essential to specify and implement as soon as possible.
It is foreseen to be a indication sent from phone to network indicating data is turned off in phone.
A extension to this would be to also allow this to be done during a specific period of time as a power save function and a way to minimize network signaling e.g. allow phone to indicate deep sleep during which there is no need for the operator to send facebook updates etc for a period of time for instance 30min. Note VoLTE/IMS traffic is still allowed.

## Slide 7: Comments on “Enable RCS services”
Given that RCS services can be routed via Wi-Fi or cellular network and also the variety of applications that can use RCS terminal api, it will be very hard to understand when and what services are available when enabling 3GPP-ps-data-off.
Third party applications that use both “internet data” and RCS services in same application(s) will work very differently pending on this flag
Since charging can be made in various ways, indications in phone need to be present to allow differentiating among services.
There needs to be a possibility for the phone user interface to indicate what traffic are allowed to be sent when 3GPP-data-off is enabled in the phone.
The options to configure this should be kept to a minimum to ensure a consistent behavior across operators.

## Slide 8: Conclusions
Proposal
Agree on a set of RCS services that will be possible to run when 3GPP-ps-data-off is enabled to ensure consistent behavior of the interoperable service RCS across operators and countries.