## Slide 1: Enhancements of LTE for affordable Video/HD
China Telecom
3GPP TSG-SA WG1 Meeting #76 S1-163155
Tenerife, Spain, 7-11, November 2016

## Slide 2: Background
Little users use LTE to view video
Mobile user
  Viewing video from LTE is too expensive
  I would rather use WiFi
Mobile operator
  Video is ideal service to improve ARPU
  However, video consume too much radio resource for me to reduce the price
  Ensuring video quality by dedicated QCI/bearer costs more resource
We should design solution to reduce the price by
  Reducing the radio resource cost
  Improving the video delivery efficiency
  Enabling new business model

## Slide 3: USE CASE
Operator controlled UE caching
  Delivery
    Video is delivered to UE by MBMS or delay tolerant
  Content Request
    User may subscribe to the network for interested video content
    MNO may also predict UE interested content
  Charging
    If the cached content is access by the user, the content would be charged
    Otherwise, the cached content would be overwritten by new content

## Slide 4: USE CASE
Cross-layer optimization
  Support same QoE with less radio resource; and/or
  Supports higher QoE with same radio resource cost
Example: dedicated QCI vs deadline-aware scheduling
  Dedicated QCI always treats as the high priority
  Deadline-aware scheduling prioritize the UE only when its playout buffer is about exhausted

## Slide 5: Potential scope of the SI
Delay tolerant content delivery
UE caching
Selective Acceleration
Video transmission optimization
  Video-aware optimizations by RAN
  Radio-aware optimizations by video
Sponsored connectivity and Advertisement insertion