## Slide 1: Introducing the work and result of Specialist Task Force STF 505 - IoT
Specialist Task Force STF 505 - IoT
Presented by Jumoke Ogunbekun

## Slide 2: Study on IoT Standards Landscaping and Gap Analysis
The European Commission runs the EU Research and Innovation program Horizon 2020. It supports the emergence of an eco-system capable of delivering the Internet of Things with actions like
  Validation of IoT technologies and approaches through Large Scale innovation Pilots (LSPs);
  Identification of required standards in support of global deployments and interoperability in order to support the LSPs  For this purpose ETSI has been tasked to provide two reports on “IoT Standards Landscaping“ and “IoT European LSP gap analysis“; ETSI TC SmartM2M launched a Specialist Task Force (STF505) to proceed this task in support of AIOTI WG3

## Slide 3: Main Objectives
To analyse the status of current IoT standardisation
To develop a set of deliverables, including recommendations, that are aimed at supporting material for the proposal and implementation of Large Scale Pilots (LSPs)
To leverage liaisons between SDOs, SSOs, and industrial alliances
To foster dissemination work for the development and maintenance of a global community of stakeholders involved in the standardization of IoT

## Slide 4: Main Deliverables
Technical Report on Standards landscape for IoT and identification of potential frameworks for interoperability (e.g. oneM2M)
Technical Report on Identification of gaps and proposals on how to address them in standardisation
Thematic workshop on Smart Home that cover different LSP application domains such as Smart Living, eHealth, Wearables and Smart Cities (end of February 2016)
Delivery workshop centred on the presentation of the STF results and their application by the winning LSP proposals (beginning of February 2017).
Detailed final report for the European Commission

## Slide 5: STF 505 (ETSI TC SmartM2M)
IoT Standards landscaping and IoT European Large Scale Pilots (LSP) gap analysis.
What we do:
STF505 is a group of experts, funded by the European Commission and supported by ETSI, commissioned to provide on the one hand an in-depth analysis of the IoT Standardization landscape (in particular in conjunction with AIOTI, Alliance for Internet of Things Innovation), and on the other hand, an identification of the IoT standardization gaps.
The study considers "vertical" functionalities (standards and protocols) in specific application domains, i.e., a single vertical industry, such as home automation, smart mobility and wearable medical devices, etc. and "horizontal" functionalities that are not specific to any particular domain but aim to provide common standards, protocols and solutions applicable to as many vertical industries as possible.
Emmanuel Darmois (a)
Joachim Koss (Leader) (b)
Samir Medjiah (c)
Jumoke Ogunbekun (d)
Michelle Wetterwald (e)
Technical Officer: Patrick Guillemin
FPS Administrator: Thierry Comont
Funding source: EC/EFTA
StART: 19 Oct 2015
eND: 14 MAR 2017
a
b
c
e
d

## Slide 6: ETSI TR 103375 and TR 103376 published
Both reports have been published:  Stable Draft in June 2016  Public review phase  Final Draft in August 2016  Publication as ETSI Technical Reports in October 2016
http://www.etsi.org/deliver/etsi_tr/103300_103399/103375/01.01.01_60/tr_103375v010101p.pdf
http://www.etsi.org/deliver/etsi_tr/103300_103399/103376/01.01.01_60/tr_103376v010101p.pdf
Analysing the standards landscape provides a list of existing standardised technology suggested for reuse by the LSPs
Identifying technical standards/ societal/business gaps as a good indication of the level of maturity of standardization in a given vertical domain

## Slide 7: ETSI TR 103375
http://www.etsi.org/deliver/etsi_tr/103300_103399/103375/01.01.01_60/tr_103375v010101p.pdf
TR 103 375 analysing the standards landscape provides a list of existing standardised technology suggested to be reused by the LSPs

## Slide 8: Structure of TR 103 375
Enterprise View of IoT Framework
Overview of Knowledge Areas:
  Communication and Connectivity
  Integration/Interoperability
  Application
  Infrastructure
  IoT Architecture
  Devices and Sensor Technology
  Security and Privacy
Common standards across vertical domains (LSPs)
Standards specific to vertical domain
  Smart Cities, Smart Living, Smart Farming, Smart Wearables, Smart Mobility, Smart Environment, Smart Manufacturing
Conclusion and Recommendation
List of SDOs and SSOs involved in IoT standardisation

## Slide 9: TR 103 375 - Approach
Many elements make up an IoT LSP. It’s more than just the technology. The initial concept was to present a view of the IoT framework as an enterprise architecture made of many parts that make the framework:
  To show how complex all the elements that are needed for an IoT LSP and
  To present a view that helps to put the entire element in context for the reader and users that are considering using the information in this TR for LSP operation
Next step was to start with the AIOTI WG3 report on “IoT LSP Standard Framework Concepts”. This provided several ways of visualising the landscape in order to simplify and facilitate the usage of the information in various IoT application domains.
TR 103 375 then expands on the AIOTI work by reviewing the scope of each of the relevant standards within the SDOs, those suggested by AIOTI, and often more

## Slide 10: AIOTI Knowledge Area 1/2
Communication and Connectivity knowledge area: Covers mainly specification of communication protocol layers, including PHY, MAC, NWK, Transport, Application layer, and their types, e.g. Wireless/Radio and Wire line
Integration/Interoperability knowledge area: Covers mainly specification of common IoT features required to provide integration and interoperability
Applications knowledge area: Covers the support of the applications lifecycle including development tools/models, deployment and management; including analytics, application supporting tools and application domain specific activities

## Slide 11: AIOTI Knowledge Area 2/2
Infrastructure knowledge area: Covers aspects related to the design, deployment, and management of computational platforms tailored to support IoT-based applications
IoT Architecture knowledge area: Covers integrated/complete IoT specification solutions, including architecture descriptions
Devices and sensor technology knowledge area: Covers mainly device/sensor lifecycles, including operating systems, platforms, configuration management, sensor/actuators virtualization etc.
Security and Privacy knowledge area: Covers security and privacy topics

## Slide 12: Snap shot of Common Standards Across Vertical Domains – Connectivity KA
Vertical domains
SC: Smart Cities
SL: Smart Living
SF: Smart Farming
SW: Smart Wearables
SMo: Smart Mobility
SE: Smart Environment
SMa: Smart Manufacturing
SDO: Standards Developing Organisation
SDO | Standards | Description/Analysis | SC | SL | SF | SW | SMo | SE | SMa
3GPP multi-purpose | TS 23.002 (network architecture) TS 23.401 (Packet Radio Service) TS 36.300 (Radio Access Overall description) | The 3GPP standards cover Radio, Core Network, and Service Architecture for cellular mobile networks. The different versions are named: GSM, GPRS (2G), EDGE, UMTS (3G), HSPA, LTE (or 4G), LTE-Advanced. The specifications cover all aspect of a radio telecommunication system. LTE is significantly more spectrally-efficient than 2G or 3G, hence transporting data over a 4G network can be done at a much lower cost per bit. The LTE-ADVANCED standard version is still evolving. New networks are being rolled out, and leading-edge features are being added to 4G to satisfy the market need for ever-increasing data rates. http://www.3gpp.org/specifications/specifications. | X | X | X | X | X | X | 
IETF 6lo | Definition of Managed Objects for 6LoWPANs (RFC 7388) 6LoWPAN-GHC (RFC 7400) Transmission of IPv6 Packets over ITU-T G.9959 Networks (RFC 7428) Ipv6 over BLUETOOTH® Low Energy (RFC 7668) | The IETF WG 6lo targets IPv6 over low power area networks, i.e. over networks of resource-constrained nodes in terms of memory, processing resources and bandwidth. | X | X | X | X | X | X | 

## Slide 13: Snap shot of Vertical Specific Standards e.g: Smart Mobility, Application KA
SDO | Standards | Description | Analysis
3GPP V2X | TR 22.885 ( Study on LTE Support for Vehicle to Everything (V2X) Services) ; TS 22.185 (Service requirements for V2X services; Stage 1); TR 22.891 (3GPP; Technical Specification Group Services and System Aspects; Feasibility Study on New Services and Markets Technology Enablers; Stage 1) for Smarter | 3GPP has recently started working on C-ITS for LTE-Advanced and 5G (known as Smarter). | These documents identify the main use cases where LTE could be used for V2X scenarios and the corresponding requirements. ftp://ftp.3gpp.org/Specs/archive/22_series
ACEA | Scientific Advisory Group reports | The Scientific Advisory Group reports are published regularly. | They cover topics such as Driving Innovation, eCall, Electric Vehicles, Infrastructure, Intelligent Transport Systems, Urban Logistics, Urban Transport Policy, Weights and Dimensions. http://www.acea.be/publications
AVNU Alliance | Profile for automotive use and certification tests from the automotive Certification Test Subgroup (CDS) Related standards: IEEE 802.1 Audio Video Bridging (AVB); IEEE 1722 AVB Transport Protocol (AVBTP); IEEE 1733 Layer 3 Transport Protocol for Time-Sensitive Applications in Local Area Networks | The AVNU Alliance is an industry forum dedicated to the advancement of professional-quality audio video transport by promoting the adoption of the IEEE 802.1 Audio Video Bridging (AVB), and the related IEEE 1722 and IEEE 1733, standards over various networking link-layers. | The AVNU Alliance enables deterministic networking via certification of compliance and interoperability for devices using open IEEE standards. The AVNU certification program ensures interoperability of networked devices in a broad range of applications including professional AV, automotive, industrial control and consumer. A fully networked car according to AVNU alliance allows access to all sensors and cross-domain communication. http://avnu.org/automotive/

## Slide 14: Highlights of TR 103 375 (1)
Chart: Allocation of standards
| Common standards | Smart Cities | Smart Living | Smart Farming | Smart Wearables | Smart Mobility | Smart Environment | Smart Manufacturing
Communication and Connectivity | 46 | 25 | 6 | 24 | 4 | 21
Integration/ Interoperability | 28 | 14 | 2 | 25 | 2 | 2
Application | 4 | 2 | 1 | 2 | 4 | 1 | 1
Infrastructure | 21 | 1 | 1 | 6 | 0 | 1
IoT Architecture | 9 | 2 | 1 | 1 | 6 | 12 | 2
Devices and Sensor Technology | 25 | 1 | 2 | 1
Security and Privacy | 17 | 5 | 1
329 standards in total allocated to
  7 vertical IoT Domains (LSPs) and
  7 Knowledge Areas
150 Common standards
179 vertical specific standards mostly identified in the IoT domains
  Smart Mobility
  Smart Living
  Smart Manufacturing

## Slide 15: Highlights of TR 103375 (2)
More than 70% of the standards allocated to
  Communication and Connectivity
  Integration/Interoperability
  IoT Architecture
Most of the common standards identified in the Knowledge Areas
  Communication and Connectivity
  Integration/Interoperability
  Devices and Sensor Technology
  Infrastructure
Chart: Allocation of standards
| Communication and Connectivity | Integration/ Interoperability | Application | Infrastructure | IoT Architecture | Devices and Sensor Technology | Security and Privacy
Common standards | 46 | 28 | 4 | 21 | 9 | 25 | 17
Smart Cities | 2 | 2
Smart Living | 25 | 14 | 1 | 1 | 1
Smart Farming | 2 | 1 | 1
Smart Wearables | 6 | 2 | 1
Smart Mobility | 24 | 25 | 4 | 6 | 6 | 2 | 5
Smart Environment | 4 | 2 | 1 | 12 | 1
Smart Manufacturing | 21 | 2 | 1 | 1 | 2 | 1

## Slide 16: ETSI TR 103376
Identifying technical standards/ societal/business gaps as a good indication of the level of maturity of standardization in a given vertical domain

## Slide 17: TR 103 376: Identification of standards gaps and recommendations
Nature of gaps
  Missing standards
  Missing APIs
  Duplications that would require harmonization
  Missing interoperability profiles that would clarify the use cases
  Classified as: technical, business or societal (incl. security and privacy)
Gaps identification methodology
  Survey to obtain inputs from the standardization and stakeholders community:
    215 answers, include gap identification as well as proposed solutions
  STF experts analysis to expand on the current standards landscape
    For each vertical, extract requirements from the AIOTI reports and other documentation
    Identify if SDOs/Alliances address the target requirement (using TR 103 375)
All identified gaps recorded in the TR, to serve as a reference for the LSPs
Resolution of the gaps
  Dissemination of STF 505 results: to point to gaps and allocate them
  It is left to the proper organizations of the IoT community to fill the gaps

## Slide 18: Highlights
49 main gaps result from the consolidation view (TR 103 376)

## Slide 19: Connectivity
Fragmentation of the standardization landscape, competing technologies. Availability of a large number of heterogeneous communications and networking technologies
   Choose solutions with additional criteria: IPR, licensing and monthly fees, deployment cost, security, energy consumption.
   Further criteria (may need refinement of existing standards): flexibility, prioritization of the flows, scalability, resilience to external factors and possible issues in the network, high network availability, spectrum resources availability

## Slide 20: Upper layers: service and application
Data interoperability: lack of easy translation mechanisms between different specific models. Need of a global and neutral data model. Seamless interoperability between data systems
   Develop semantic interoperability to enable harmonization
Interoperable processing rules: lack of definition for advanced analysis and processing of sensor events and data to interpret the sensor data in an identical manner across heterogeneous platforms
   Develop guidance for decision-making processes, for data organization, storage and exchange.
APIs to support application portability among devices/terminals
   Interoperability of platforms: data level (semantic) + application level (services)

## Slide 21: Integration/Interoperability
Global-level standards (international vs. regional level)
   Harmonization / Interoperability of similar messages defined at regional level
Fragmentation due to competitive platforms and standards
   Develop technical guidance of compatibility between standards
   Some clarification may be brought by refinement of the use cases
   Develop interworking / cooperation between platforms, e.g. possibility to exchange data. Manage applications heterogeneity
   Focus on the whole value-chain (devices, platform, etc.…), not only on connectivity. Enable the support of a wide range of sensors, devices, protocols, services … Ensure flexibility and scalability

## Slide 22: Applications management (life-cycle)
Usability
   Develop tools to enable ease of installation, configuration, maintenance, operation of devices, technologies, and platforms. Simplify the personalization of the system
   When suitable, allow secure remote access to perform device maintenance. Enable continued support to the client after purchase
Applications tailored to individual needs: evolution, flexibility of the components
   Built-in application performances' monitoring.
   Standardized methods to distribute software components to devices across a network, for life-cycle management in the field

## Slide 23: Infrastructure
Deployment tools
   Unified model/tools for deployment and management of large scale distributed networks of devices

## Slide 24: IoT Architecture
Identification
   Provide a global reference for unique and secured naming mechanisms
  Federate existing identification schemas. Secured IoT nodes identification model
Multiplicity of IoT HLAs, platforms and discovery mechanisms
   Develop specific solutions at the Service Layer to enable communications between the platforms (e.g., offer plugins)
   Allow smart objects to move and enter different eco-systems (e.g. during an update of the system or change of provider)

## Slide 25: Devices and sensor technology
Quality assurance and certification
   Building of certification mechanisms defining “classes of devices” and covering features such as robustness, consumption, accuracy, reliability, resilience over long periods of time (self-sufficient operation)
   Standardization of test specifications and suites (hardware and software) and proper guidelines regarding the final characteristics that correspond to the expectations
   Definition of approval processes for IoT devices conformance assessment.
Device modularity
   Standardization of the ability to add/remove hardware capabilities to a device

## Slide 26: Security and privacy [Societal issues]
Privacy and security issues can be a blocking factor for user’s acceptance and prevent large scale deployments. Security and privacy are addressed on an isolated basis for part of the applications
   Develop mature data management, data security, data privacy and ownership standards, rules to ensure trust in a common good objective, foster security by design initiatives
   Develop data rights management (ownership, storage, sharing, selling, etc.). Define samples, good practices, regulations, etc.
   Develop “classes of devices” for security
   Develop education of end users on these features
Lack of highly secure and trusted environments
   Build Risk Management Framework and Methodology
   Develop a workflow to establish trust between the players

## Slide 27: Societal gaps [including regulations]
Lack of knowledge about potentialities of IoT among decision makers, users
   Dissemination fosters awareness from the different actors
   Encourage the development of education and dissemination material of IoT standards and specifications
   Enable easy accessibility and usage to a large non-technician public
Not everything should be smart
   Definition of what is useful to society and what is useless. Adaptation to the needs
Green Technologies
   Insert low power and low energy constraints integration in the whole value chain.
   Develop pollution management

## Slide 28: Societal gaps [including regulations] (cont.)
Liability for data privacy
  Regulations to enforce the respect of privacy at all levels of the IoT systems and distribute the liability between the different providers and actors
Ethics. Transparency and choice for citizens
   Guarantee of integrity, ethical by design
  Exchange data on security breaches to raise awareness and avoid their repetition
Regulations for frequency harmonization and usage

## Slide 29: Business gaps
Lack of a reference for business cases and value chain model to guide choices for deployment
   Define an integrated vertical business architecture, considering all actors of the value chain, from manufacturers to dealers, installers, service providers, end users…
   Roadmaps to market taking into account renewal cycle. Simplify early deployments
   Foster new investment paradigms to small companies, early adopters, vs. extreme competition
   Give priority to cost effective implementations, reusable solutions
   Clarify what is proprietary, open source, subject to IPRs
   Reduce delay of standardization to avoid proprietary solutions (vendor lock-in). But in parallel, enable the insertion of existing proprietary solutions (de-facto standards) in the architecture

## Slide 30: Business gaps (cont.)
Collaboration between vertical domains, siloed applications
   Develop communication between stakeholders from technology and vertical domain
   Specify the collaboration of siloed applications and services, create a global value chain (e.g., healthcare service links with other services such as smart home for living environment, smart cities for outside activities, smart mobility)
   Develop more transversal and common solutions (compatibility) and business models. Aim at the seamless interoperability or plug and play of the different standardised IoT architectures and platforms

## Slide 31: Conclusion and summary
Interoperability will be essential for the deployment of the IoT and for ensuring seamless flow of data across sectors and value chains
Solutions should be more than technical solutions
Existing standards to be refined to address non-technical issues
Certification mechanisms are a very important topic, mandatory to complete technological developments
Security and privacy are still a limiting factor
Regulations and dissemination are needed to ensure users’ acceptance
Solutions should give advantage to transversal compatibility rather than vertical domain specifics

## Slide 32: Fujitsu - conclusion
This presentation is to make 3GPP aware of some of the work performed by ETSI STF505
In this work some gaps are identified which show some areas where standards are missing and this could potentially be new area of study for SA1