## Slide 1: Agreements and discussion points on Access Control
Atsushi Minokuchi
NTT DOCOMO
3GPP TSG-SA WG1 Meeting #79
Guilin, China, 21 - 25 August 2017
Notes: 1

## Slide 2: Agreements
SA1 CR is based on NTT DOCOMO CR S1-173422, which is revised to S1-173423.
Nokia to write LS OUT to answer CT1 and RAN2 questions and send SA1 CR.
SA1 CR is for TS 22.261 Rel-15.
Unified access control applies to E-UTRA and NR access to 5GC. (only to 5GC)
Unified access control will address backwards compatibility aspects.
Unified access control will address RRC_Idle, RRC_Inactive, RRC_Conneced.
Notes: 1

## Slide 3: Discussion points
Scope of applicability of RRC Connected
Future proof
    It’s not that the following should be specified in Rel15, but that consideration is needed to allow specifying the following in the future.
  Network slicing
  Solution for the situation when an access attempt looks to fall into multiple access categories.
  Relationships between an operator’s Operator-specific categories and another operator’s.
Notes: 1

## Slide 4
The rest is for drafting

## Slide 5: Discussion points – principle
Topic | Company’s view | Status of agreements
Scope of applicability to RRC Connected, except SSAC, whether access control is applied to CN_Connected mode? If so, in which case or with what granularity? | Docomo: (personal view) one idea is to use the start message (INVITE for SIP, GET method for HTTP or we can see into deep.) of application protocol to impose access control. For future 3GPP service at least, we know exactly what protocol is used, then it’s possible to use access control for connected mode. And HTTP. | 
“Double-checking” handling (e.g. EAB and ACB in EPC) | Docomo: In general, double-checking leads to a “double-barring” problem and to a necessity to invent “skipping” solution (e.g. ACB skip). We should seek to come up with mutually exclusive categories. The current CR does not allow “double-checking”. | 
Number of access categories (5 bit is enough? or more bits are required for future extension?) | Docomo: 5 bits is fine. | 
Network slicing (in Rel-15, network slicing should be considered?) | Docomo: Not in Rel-15. In Rel-16 onwards. | 
what should be the number of ‘standardized’ access categories? | Docomo: now 16. That’s fine. To make it more is also fine. | 
for which cases, ‘standardized access categories’ applies | Docomo: standardized category has priority over operator-specific category, as we have for ACDC. (Double checking does not happen.) | 
Notes: 1

## Slide 6: Discussion points – principle
Topic | Company’s view | Status of agreements
How future extension for access catogires are supported? How new criterion (e.g. network slicing) can be introduced in future releases? | Docomo: network slice can be considered analogous to network sharing. (we can think multiple network slice identities as if we have multiple PLMNs in principle.) other views appreciated. | 
what is the ‘general’ principle for the case whan an access attempt matches several ‘access categories’ simultaneously? (also, we need to have priciple because additional criterion in the future release may result in multiple matching categories) | Docomo: Not sure if such case happens Spec should be written categories are mutually exclusive. | 
Notes: 1

## Slide 7: Discussion points – principle
Topic | Company’s view | Status of agreements
For operator defined access categories, what should be the criterion that should be supported in Rel-15? | Docomo: Two categories might be minimum. If we have that, we can satisfy the existing NB IoT access control in terms of “mobile originating exception data” in TS 36.331. (NB IoT access control is not included in SA1 spec.) | 
How or which information is delivered for operator defined access categories? | Docomo: the same as ACDC. For configuration, OMA DM. No action needed. | 
Within one network, operator defined access categories are same for both Home UE and roaming UE? within one network, every UE has same information for operator defined access categories? or, for different UEs withine same network, same value of operator defined access categories can mean different access? | Docomo: No. This issue is examined in ACDC discussion and captured in 4.3.5.2.2 of TS 22.011. No action needed. | 
The term “broadcast” is to be used or not? |  | 
Notes: 1

## Slide 8: Discussion points – CR editorial
Topic | Status of editorial work
Reflect S1-173082 (Unified access control, LGE) | 1st draft being reviewed.
Reflect “Unified access control applies to E-UTRA and NR access to 5GC. (only to 5GC)” | 1st draft being reviewed.
Reflect backward compatibility aspects | On-going
Description on AC 11-15 related access categories (i.e. #1, NOTE 1) | 1st draft being reviewed.
Description on “the rest of MO data” (i.e. #16) | 1st draft being reviewed.
Use “delay tolerant” instead of “EAB” | Done
Notes: 1