## Slide 1: Low Power IoT Relays (LPIR)

## Slide 2: Situation in 3GPP
Release 15:
  SA1 have completed REAR work
  SA2 have completed REAR study, not agreed WID so far
  RAN have completed feD2D study, not agreed WID so far
Content:
  SA1 agreed some general service requirements that REAR should address small data services
    “The 3GPP systems shall support small data services (e,g, CIoT, eMTC) for an Evolved ProSe Remote UE when the Evolved ProSe Remote UE uses an Indirect 3GPP Communication.”
  This has not been followed up in SA2 or RAN
  Support for NB-IoT over relay is not possible in a way which preserves the battery savings at the remote UE
  Service requirements of what to support for NB-IoT over relay have not been derived
RAN & SA progressing work in Rel-15

## Slide 3: NB-IoT and eMTC
NB-IoT/Cat M work enable low cost/low power operation
  Narrowband operation; low complexity device; signaling and CN optimizations
CIoT/eMTC/NB-IoT enhancements include:
  Power Saving Mode (PSM)
  Extended Idle-mode Discontinuous Reception (eDRX)
  Control plane CIoT EPS optimisation
  User plane CIoT EPS optimisation
  Attachment without PDN
  Support for non-IP data
Enhance battery life, low cost, and coverage benefits of IoT UEs

## Slide 4: Question for SA1
What are the service requirements for the NB-IoT service via relay?
Does the remote UE expect normal NB-IoT service?
Are there new service requirements for the relay UE?
Do we exclude anything from NB-IoT and CIoT enhancements when using a relay?
Are the service requirements for NB-IoT via relay complete?

## Slide 5: Analysis

## Slide 6: D2D enhancements for IoT
Main Idea: Using unidirectional D2D link to relay UL from IoT devices
  Significantly improve battery life in deep coverage operation
  No additional cost for Relayed UL + Direct DL case
Relay UE is a mobile device that is either another IoT device or a higher capability device
Enhance battery life, low cost, and coverage benefits of IoT UEs
Relay UE
DL
DL
UL/DL
UL via D2D
UL via D2D

## Slide 7: Battery life analysis
Water meter
2 Tx/day, 4KB/Tx, 15 Wh battery
Direct access (@155dB CL)
* eI-DRX with cycle of 10.24x256sec
* No D2D-link adaptation (max power tx, 4 blind HARQ)
7.7x
D2D relayed access (@155dB CL)

## Slide 8: Battery life advantage
Improved battery life due to reduced tx bundling requirements with unidirectional L2 relays
Water meter
Traffic: 2 Tx/day, 4KB/Tx
UE: 1.4MHz NB (Cat-M), 20dBm, 15 Wh battery
* eI-DRX with cycle of 10.24x256sec
* No D2D-link adaptation (max power tx, 4 blind HARQ)
7.7x
NB-IoT
Traffic: 1 Tx/hr, 100B/Tx
UE: 180kHz NB (NB-IOT), 3dBm, 5 Wh battery
* eC-DRX with cycle of 10.24sec
* No D2D-link adaptation (max power tx, 4 blind HARQ)
1.9x
Coverage goals met at low Tx power

## Slide 9
Conclusions

## Slide 10: Conclusions
SA1 should start a short study to document the service requirements for NB-IoT and eMTC over relays
This study should elaborate the service requirements as to which NB-IoT and eMTC features are required to be supported over relay, and what the service requirements are for the Remote UE, Relay UE, and network
D2D enhancements for IoT can further battery life, low cost, deep coverage advantages for IoT

## Slide 11: Conclusions
Main idea is to enable unidirectional relays explicitly for NB-IoT and eMTC using D2D
  Explicitly not to support eMBB or URLLC use cases
  To be designed for power and computationally constrained remote UEs
  To be designed for both power and computationally constrained and unconstrained Relay UEs
Significant battery life improvement expected for deep coverage operation
D2D enhancements for IoT can further battery life, low cost, deep coverage advantages for IoT