## Slide 1: Time Sensitive Networking: Overview

## Slide 2: Background
IEEE Time Sensitive Networking (TSN) TG grew out of AVB (Audio/Video Bridging)TG
  AVB TG was renamed as TSN TG (in 2012) as focus expanded from A/V streams to including control streams (automotive and industrial control applications)
  AVB requirements
    2-ms maximum delay
    1-us maximum synchronization error
  Some key benefits of AVB
    End-points can automatically configure a bridged network to deliver A/V streams without network administration
    End-to-end QoS over multiple media, e.g., Ethernet, Wi-Fi, Ethernet over passive optical network (EPON)
Features needed beyond AVB for industrial control
  Deterministic latency (~IETF Deterministic Networking)
  Reliability and fault tolerance.

## Slide 3: TSN Goals
Support all data types (Control in addition to Audio/Video)
Achieve lower latencies
  Traffic shaping, bandwidth reservation, pre-emption
Achieve very low packet loss rates by using different redundancy schemes
Interop with existing devices
Provide a common Layer 2 for all upper layer protocols
802.1 TSN and related foundational services
(Time synchronization, QoS, Redundancy, Security, Network Configuration, etc.)
PROFINET
EtherNet/IP
IEEE 1722
OPC-UA
(Industrial M2M)
Future Industrial Protocols

## Slide 4: TSN Specs in IEEE
Feature | Document
Time synchronization (gPTP) | 802.1AS
Distributed Stream Reservation Protocol 802.1Qcc has enhancements for SRP | 802.1Qat 802.1Qcc
Forwarding and Queuing Enhancements (FQTSS, CBS) | 802.1Qav
Enhanced Transmission Selection | 802.1Qaz
Priority Based Flow Control | 802.1Qbb
Time Aware Queuing | 802.1Qbv
Cyclic Queuing | P802.1Qch
Frame Preemption | 802.1Qbu
Input Gating | P802.1Qci
Seamless Redundancy | P802.1CB
Interspersing Express Traffic | 802.3br
Notes: FQTTS (Qav) and SRP (Qat) were merged in 802.1Q-2014
Other standards:
  1722/1722a d16 AVTP (new draft is more flexible in data types that can be used for control signals)
  1733 AVTP over RTP (to traverse LANs)
  1722.1 Discovery and enumeration

## Slide 5: TSN for Industrial Automation
TSN is considered to be the future of real-time communication
  TSN growth recently forecast at CAGR of 53.8%, 2017-2024
3GPP should consider how to support TSN over 5G
  Ethernet Data Link Layer compatibility
    Learning bridge, broadcast, spanning tree
  Time-synchronization
  QoS – architecture aspects and system design aspects
    Rich QoS enabled by TSN Stream Reservation Protocol
SA1 can discuss TSN feature priorities.

## Slide 6: TSN features

## Slide 7: IEEE 802.1AS: generalized Precision Time Protocol (gPTP)
Defines generalized Precision Time Protocol (gPTP)
  Narrowly defined profile based on IEEE 1588 (PTP)
Differences between PTP and gPTP
  gPTP assumes IEEE 802 MAC PDUs; PTP defined various layer 2 and layer 3-4 communication methods
  gPTP specifies a media-independent sublayer so that multiple networking technologies can be integrated within a single timing domain, e.g., Ethernet + Wi-Fi
  For Ethernet full-duplex links,
    gPTP requires use of peer delay mechanism; PTP also allows the use of end-to-end delay mechanism
  In steady state, gPTP has a single timing domain; PTP allows multiple overlapping timing domains
  gPTP makes synchronization mandatory; it is optional in PTP (slower convergence without it)
  gPTP requires that all devices in the timing domain support gPTP.

## Slide 8: IEEE 802.1Qat: Stream Reservation Protocol
End-to-end resource reservation for streams
Talkers advertise streams by sending talker messages
  Messages contain traffic specification (Tspec): max frame size, max # frames/interval, priority
  Bridges determine whether reservation is possible; update accumulated latency field
    Updates type of message from talker advertise to talker failed if reservation is not possible
Listeners subscribe to streams by sending listener messages
  Reservations are made as listener messages are propagated back
  Bandwidth is reserved on the traffic shaper (FQTSS/CBS) for the corresponding queue
Talker may start transmitting, once it receives listener ready message
T
B
B
B
L
L
T
B
L
Talker
Talker advertise
messages
Bridge
Listener
T
B
B
B
L
L
Listener subscribe
messages

## Slide 9: IEEE 802.1Qat (2)
Emergency streams
  SRP uses stream rank to allow preemption of non-emergency stream
Automatic Network Configuration
  SRP configures VLANs, priority to queue mapping, bandwidth reservation automatically
SRP ensures that talkers reserve bandwidth before transmission
SPR protects valid streams from misbehaving talkers (transmission rate too high)
  First bridge in the path shapes the traffic to protect rest of the network (enforcement)
Non-AVB traffic is allowed to use unreserved bandwidth
802.1Qcc: SRP enhancements
  Seamless redundancy
  Explicit interoperation with centrally managed system (coexistence of centrally-managed and distributed)
  Integration with layer 3 (IP) support
  Dynamic changes to bandwidth and latency
  Reservation at a bridge based on worst case latency
  …

## Slide 10: IEEE 802.1Qav: FQTSS, CBS
FQTSS: Forwarding and Queuing Enhancements for Time-Sensitive Streams
FQTSS specifies Credit Based Shaper (CBS)
Parameters
  idleSlope (rate of accumulating credit)
  sendSlope (rate of using credit during tx)
  hiCredit (max accumulated credit)
  loCredit (min accumulated credit)
Note that the transmission of AVB packets is spread out
Interfering traffic can add to delay jitter
Source: https://www.iol.unh.edu/sites/default/files/.../UNH-IOL_TSN-Overview.pdf
Notes: Figure from 2015_UNH-IOL_TSN-Overview.pdf

## Slide 11: IEEE 802.1Qbv: Enhancements for Scheduled Traffic
Goal: reduce delay jitter for periodic traffic
A time gate is added on each queue on a port
At specific times, only one traffic class has access to the network
  Gate for this traffic class “open”; gates “closed” for other traffic classes
  Lower priority queues can be blocked so that high priority traffic has guaranteed access
  Time Aware Shaping bridges can support Cut-Through with a guaranteed performance of ~ 1 us of bridge latency
Source: https://www.iol.unh.edu/sites/default/files/.../UNH-IOL_TSN-Overview.pdf

## Slide 12: IEEE 802.1Qbu: Frame Preemption
Allows higher priority frame to interrupt transmission of lower priority frame
Fragmented frames are reassembled at the receiver
Source: https://standards.ieee.org/events/automotive/2015/03_IEEE_TSN_Standards_Overview_and_Update_v4.pdf
Notes: Taken from 2015_IEEE_TSN_Standards_Overview_and_Update_v4.pdf

## Slide 13: IEEE 802.1Qci: Per-Stream Filtering and Policing
Specifies filtering and policing of individual traffic streams
  Stream identification, filtering, metering
Ensures streams do not exceed reserved bandwidth
Source: IEEE P802.1 Qci/D2.1, Draft Standard for Local and Metropolitan Area Networks, Bridges and Bridged Networks – Amendment: Per-Stream Filtering and Policing, November 2016

## Slide 14: IEEE 802.1CB: Frame Replication and Elimination
Goal: Identify frames requiring redundant transmission, duplicate them at the source, and to identify and eliminate the duplicates at the destination
In TSN, duplicate frames transmitted over separate TSN streams
IEEE 802.1Qca is used for Path Control and Reservation
  New control protocol to explicitly control forwarding paths
  Allow use of non-shortest paths for redundant TSN streams
T
B
B
B
B
B
L

## Slide 15: Active Participants in TSN TG
Consumer Audio/Video and home
  Broadcom, Intel, Apple, …
Profession AV (e.g., ESPN DC2)
  Reidel, Harman, Bosch, Cisco, …
ADAS, Infotainment, Powertrain
  Audi, BMW, Continental, Broadcom, TI, Intel, …
Industrial control, Robotics
  Siemens, Rockwell, Hirschmann, Schneider, …