## Slide 1: UE Sourced Local Broadcast: Overview

## Slide 2: Background
Broadcast channels are currently envisioned to be utilized for three main scenarios:
  Type 1 – operator controlled content distribution
    Scheduled streaming content from sports/concert events, TV-like services, etc.
    Scheduled file distribution FOTA updates, eMedia distribution, digital signage, etc.
  Type 2 – over the top (OTT) content distribution with capacity leasing/operator partnership
    Group voice calling in a given location: e.g., MCPTT
    Broadcast TV distribution – enTV
Type 1 typically involve operator management and control of both the content and the schedule of transmission
  Operators may also leverage Consumption Reporting to decide which content to offer via broadcast – MooD (TS 26.346)
Type 2 typically involves an application/service providing content for transport over broadcast
  Application/service may be able to track load and switch to download transmissions to broadcast

## Slide 3: Motivation
Moving forward, they may be advantages in enabling end users to control content and schedule of distribution
The operator takes on a role of policy management, policing, charging and unicast off-loading.
  OTT applications already allow users to generate/capture content and share it via a Social Media network
    In congested cells, e.g., those covering a venue, this could amount to single UL/multiple DL transmissions
    Operators may enable local broadcast to single UL/single DL transmissions
Solution approaches
  Approach 1:
    eNB handles cell based broadcast with minimal assistance from application/service
  Approach 2:
    Local server near eNBs handle broadcast control with bearer establishment signaling to the eNB

## Slide 4: Required improvements that can better enable services.
Put the content generation and schedule to end user
Reduced data delivery latency
  Core network interactions required only for group management, security info exchange etc.,
  Once the initial transport is established, content is distributed via eNB without core network interactions.
Allowing control of such functions closer to the RAN nodes will allow for quicker activation and better device capability and RAN resource management.
  Activation through IP servers can be done, but having a large centralized management will come with it is set of restrictions of having to create extensive interactions with the RAN nodes where the broadcast is to happen making it prohibitive for deployment.

## Slide 5: UE initiated broadcast initiation
To enable active content generation, the proposal is :
  Allow for signaling initiated from the UE to request for broadcast to be enabled
    Note that the request to establish the broadcast session can be done to an IP server or RAN node.
    The schedule, type of content, the locale / regions where to broadcast, and the expected duration is shared with the network for authorization and activation.
    Content being shared is under the originating user control
    The charging is applied by the operator based on the information being shared.
    The user can also request this broadcast to be recorded and repeated at requested times.
  Allow for the content (including realtime content) to be generated from the UE
    The expectation is that the network acts as a reflector and sends on the broadcast channel.
    The information transmitted from the UE can already be formatted to be used directly over the broadcast channel including packetization and

## Slide 6: UE initiated broadcast initiation : Examples
Examples include :
A simple image carrying a coupon.
A small vendor advertising through a video session providing a sales pitch.
A garage sale in the neighborhood.
  The intent will be to potentially collaborate with applications that cater to information sharing based on local regions
A real estate agent walking through the house attracting people to the open house.

## Slide 7: Conclusion
Consider the suggested service enablers and provide requirement to the other 3GPP groups for discussing viable solutions and required improvements to enable such services.