## Slide 1: / Introduction to the Feasibility Study on Communication Services for Critical Medical Applications /

## Slide 2: Scope: Critical Medical Applications
Applications involving patients survival, and,
Taking place in operating rooms featured with advanced equipment allowing real time
  high resolution imaging (CT Scans, MRI, …),
  augmentation of video streams with live information, and,
  enabling minimally invasive procedures
Possibly enhanced with controlled robots allowing to perform diagnosis and operations remotely
Notes: Hybrid room equipped typically with
a bunch of HiRes screens
an operating table
in general a CT scanner (Computed Tomography) that moves through an arc taking many pictures and allowing to reconstruct a 3D view of the body, or,
MRI (Magnetic Resonance Imaging)

## Slide 3: Motivation
Give tools to surgeons to
  perform better (less side effect, shorter recovery time for patients)
  Perform quicker (increase OR throughput and hospitals’ revenues)
Increased OR flexibility
  enable equipment sharing between OR (more flexibility in procedure scheduling, resource optimization)
  On-demand addition of complementary imaging equipment (reduction of incidents rate during procedure)
Deliver high quality medical diagnosis and operation closer to patients
Improve working efficiency of medical staff
Notes: Motivation in a context of hybrid operating rooms

## Slide 4: Targeted type of use cases
Image guided surgery with combination of endoscopy/laparoscopy and vascular imaging (fluoroscopy) and/or ultra-sound
  Cooperation of OR personnel
  Storage real time video and metadata for offline replay of synchronized video streams
  ARAS: Augmented Reality Assisted Surgery, live superimposition of video streams during the procedure
  Remote Mentoring: Send synchronized and live media streams to a specialist providing advices in real time
  Post review by senior: in case the patient’s condition worsens the day after the procedure
  …
Notes: Type of video sources:
Echography
Computed Tomography scans
Magnetic Resonance Imaging
Fluoroscopy
…

## Slide 5: Targeted type of use cases
Remote Robotic Diagnosis: a patient can receive diagnosis performed by specialist remotely. This type of use case involves
  Improving quality of medical service of community hospital/ambulance/disaster scene
  Diagnosis technique of specialist can be delivered through controlling robot
  Diagnosis data from patients is transmitted back to specialists in real-time
  Video and audio communication between specialists and patients

## Slide 6: Targeted type of use cases
Remote Robotic Operation: operation conducted by a robot which is under a specialist’s control. This type of use case involves
  Improve the quality of operation in primary medical institution
  Real-time Surgical video backhaul
  Tight latency and high reliability transmission for robot control signal
  Remote monitoring data or other medical data transmission
  Both-way video and audio communication

## Slide 7: Other possible topics
Robotic Aided Surgery: In the sense of augmenting surgeons’ gesture through robotic to achieve smaller and more precise movements. Surgeons are
  Locally present in the OR
  Operate with robot and other equipment synergistically
  An example of such operation is a biopsy with haptic feedback

## Slide 8: Medical Imaging – Challenges
Visualization of small details like thin vessels
  Hi-resolution images – 8k (7680x4320)
  High color depth – HDR with 4-4-4 with 10 or preferably 12 bits depth
0.5cm gesture tracking precision at 30cm/s speed – High frame rate (60 fps)
Liability issues in case of incident and processing time for real time image processing – Uncompressed (or near lossless compression) video
Superimpose live streams generated by different sources – High instruments positioning accuracy
Ultra high reliability, safety and network integrity
Maintain patient privacy
High network availability
Notes: Starting from the service level: what surgeons do need ?
0.5cm precision @30cm/s speed -> 1/60 -> 60fps
Hi-Res/HDR Visualize very small details thin vessels
Throughput > 71Gbps for one display
safety (maintain patient information always associated with images to avoid adverse events)

## Slide 9: Remote Robotic Operations & Diagnosis – Challenges
High bandwidth requirement of medical video transmission
  Up to 10Mbps for ultrasonic image and 100Mbps for laparoscopic image
Limited processing time for real time image processing
High reliability of robot control
Differentiate medical service from other services and corresponding QoS guarantee
Diverse access modes of medical equipment inside the operating room

## Slide 10: Medical Imaging – KPIs / Requirements
Clock synchronization accuracy
  Images timestamping: 1ms
  For smooth video source switching: <1µs in 8k
Bitrate
  Uncompressed video streams (see assumptions in the previous slide) leads to 71Gbps per display
  Broadcasting needs to be considered
E2E Latency
  Application level, end to end latency is assessed to be <20ms
  Transport level E2E latency to be finely evaluated but expected well below 5ms.
Positioning accuracy
  For AR use cases, the requirement here is in the order of 1-2mm
Security
  As secured and reliable as wired communication systems
  Type ‘b’ networks
Notes: 0.5cm precision @30cm/s speed -> 1/60 -> 60fps
Hi-Res/HDR Visualize very small details thin vessels
Throughput > 71Gbps for one display
Synchronization is based on the observation of a phenomena with a given speed (50cm/s) in the patient body using different sources, each source delivers timestamped computed images and the requirement is to have an uncertainty of the phenomena position with a given accuracy (+0.5mm -0.5mm). Then the timestamp shall be accurate at 500/0.5 = 1/1000s

## Slide 11: Remote Robotic Operation & Diagnosis – KPIs / Requirements
Service differentiation:
  Identify different service flow
  Allocate corresponding resources for medical services
  High security & integrity (same level as mission critical systems)
Assist critical medical application for massive and real time image processing (MEC)
Compatible for multi-access
  WiFi/ZigBee/LoRa/Bluetooth access compatible for single network

## Slide 12: Stakeholders
Hospitals
  ‘Wireless Operating Rooms’ is a topic of interest for Rennes’ University Hospital for instances
Vendors of equipment for operating rooms
European Consortium
  5G-TOURS

## Slide 13: Timelines
Industry
  ORs get upgraded in a 10 years cycle
  Priority today to get an agreement on common application level protocols and have devices that can interoperate altogether
  Priority, tomorrow, leverage on wireless connectivity to bring flexibility to ORs
3GPP
  Rel17 targeted
  SID planned for completion at SA#84 (June 2019)