## Slide 1: Further discussion slides about multi-hop
Walter Dees
Philips International B.V.
3GPP TSG-SA WG1 Meeting #86
Suzhou, China, 6 - 10 May 2019
Tdoc#: S1-191109
Agenda item: 8.6

## Slide 2: Discussion slide 1
Within a multi-hop deployment the XXX UEs receive data from a remote UE or another XXX UE and forward it to another XXX UE or to a UE-to-Network relay.
Q1: Is XXX UE equivalent to term “multi-hop relay UE” used in REFEC draft? If not, what do we call them when we talk about multi-hop, and how does it relate to the term “UE-to-Network relay”?
Q2: What happens if more than 1 XXX UE is in coverage area of eNB? Should it be possible to designate only one XXX UE to forward traffic to the network (e.g. because it has the best connection to the eNB)? It may not lead to the best performance and may cause additional complexity if all XXX UEs will forward relay traffic to the network.
Q3: If answer to Q2 is “Yes, then will we keep the term UE-to-Network relay to denote the UE that is responsible for forwarding traffic to the network?
Existing terminology in 22.261/22.278 for single hop relay.
Terminology confusing for multi-hop relay.
UE-to- Network relay
eNB
Remote UE
Indirect network connection
UE-to- Network relay (?)
eNB
Remote UE
Indirect network connection using multi-hop
XXX UE
XXX UE
XXX UE
Terms denote different type of UEs in single-hop relay deployment:
UE-to-Network relay device receives data from remote UE and forwards it to network, and vice versa.
Remote UE sends data to and receives data from UE-to-Network relay device.

## Slide 3: Discussion slide 2
Need for requirement on dynamic adaptation of multi-hop deployment.
UE-to- Network relay
eNB
Remote UE
Indirect network connection using multi-hop
XXX UE
XXX UE
XXX UE
Setting up an indirect network connection using a multi-hop deployment is less straightforward than in the single hop case, in particular if the indirect connection needs to meet certain QoS criteria or the devices involved face certain restrictions, such as low battery or out-of-coverage of an eNB. The current arrangement may not be the most optimal one (e.g. in terms of signal quality, overall battery usage, achievable QoS etc.).
In particular if the circumstances change it should be possible to adapt the multi-hop deployment (e.g. through a re-selection process) if this leads to a better, more optimal arrangement of devices to establish an indirect network connection. For example, if the signal between the UE currently acting as UE-to-Network relay (indicated by purple rectangle) to the eNB has become pretty bad, one of the XXX UE may need to become a UE-to-Network relay if it has a better signal. In this case the XXX UE indicated by red rectangle has the best signal at that moment, and should become UE-to-Network relay (e.g. by receiving instruction from the network or application). Also, as mentioned in the elderly healthcare use case, it could be beneficial in some cases (e.g. if battery of XXX UE gets too low) that the Remote UE becomes an XXX UE, and the XXX UE becomes the remote UE.
 Requirements that describe these forms of (re-)configuration seem to be missing and should be added to FS_REFEC. See next slide for possible formulations.
.
(*) Remote UE
eNB
Remote UE
XXX UE
UE-to-Network relay
XXX UE
Current situation
After adaptation

## Slide 4: Discussion slide 3
Possible formulation of dynamic adaptation requirement (in addition to updating
the relay UE selection requirement in factory use case)
  Original proposal:
    “The 5G system shall support dynamic configuration and re-configuration of the roles that UEs take in a multi-hop relay deployment.”
     Comments received: should avoid the term “role”. Also term (re-)configuration may already imply some type of solution. Perhaps the term (re-)selection is better.
  Alternative 1:
    “The 5G system shall support re-selection of multi-hop relay UEs and remote UEs based on operational changes within multi-hop relay UEs, remote UEs or the environment.”
      NOTE: operational changes may include a multi-hop relay UE moving out of range, the battery of a multi-hop relay UE getting depleted, a remote UEs requesting additional resources or higher QoS, a new relay capable UE getting in range, etc.
  Alternative 2:
    “The 5G system shall support adaptation of a multi-hop relay deployment”
      NOTE 1: adaptation may be done by re-selection of multi-hop relay UEs and remote UEs according to various criteria, such as signal quality, QoS requirements , proximity of devices, optimal energy use, number of hops to reach the network, etc.
      NOTE 2: adaptation may be triggered by a change in circumstances, e.g. a multi-hop relay UE moving out of range, the battery of a multi-hop relay UE getting depleted, a remote UEs requesting additional resources or higher QoS, a new relay capable UE getting in range, etc.
    Suggest to use Alternative 2, since that formulation is the most solution agnostic.

## Slide 5: Discussion slide 4
In addition, the following requirement may need to be added:
  “The 5G system shall support a mechanism to trigger a multi-hop relay capable UE to start or stop acting as a multi-hop relay UE or remote UE”.