## Slide 1: Way Forward for MUSIM
S1-192588

## Slide 2: Definition of MUMS mode and MUMA mode
  Multi USIM Multi Standby (MUMS) mode: The operating mode of a MUSIM UE in which multiple USIMs on standby can be used for idle-mode but only one USIM can be in connected mode at any given time.
  Multi USIM Multi Active (MUMA) mode: The operating mode of a MUSIM UE in which a subset of the multiple USIMs can be used for connected mode at any given time. USIMs with a dedicated transceiver are excluded from this definition.
  Are UE implementations sufficient to address all service requirements

## Slide 3: The User preference of MUSIM UE
[CPR.8.1-2]: A MUSIM UE should allow the user to configure the user’s preference for the same or different services among multiple USIMs provided by the same or different MNOs.
Can we agree that user preferences is configured by the user and used by the MUSIM UE to handle the MT service?

## Slide 4: Service requirement 8.2-1
[CPR.8.2-1]: The 3GPP system shall be able to indicate to the UE as part of the paging procedure the type of traffic that triggered the paging. This information may be used by a user or MUSIM UE to determine whether it needs to respond to a mobile terminated call on one registered USIM while the UE is engaged in active communication on another USIM. The granularity of the paging information shall discriminate between the following service categories;
IMS and non-IMS based Voice service.
IMS and non-IMS based SMS or USSD
IMS service other than voice or SMS
Other service not listed above e.g. data services including video.
How to rephrase the service requirement:
  Assumption: idle mode UE or connected mode UE
  The 3GPP system shall be able to indicate to the UE upon presentation of an MT service the type of traffic corresponding to that MT service.
  Network provides assistant information to the MUSIM UE for the MT services: YES/NO?

## Slide 5: Service requirement 8.2-1
    If assistant information is beneficial?
    what are the assistant info?
      service categories to the UE
      Caller party ID
service categories:
  Assumption:
    Traffic can be identified by the network
    Generic service information
IMS and non-IMS based Voice/SMS or USSD
  Remove IMS and non-IMS?
IMS service other than voice or SMS: Yes/No
Priority Service with User perspective?

## Slide 6: Others
Suspension/Resumption
  If these are helpful for network for managing resource and handling the ongoing communication?
Paging collision issues
  Can we leave it as UE implementation?