## Slide 1: Enhance MMTEL with VR in 5G
S1-193055

## Slide 2: Content
Current level of standardization of IMS services in SA1
Current VR/XR work in 3GPP
Way forward for SA1

## Slide 3: 22.173 IP Multimedia Core Network Subsystem (IMS) Multimedia Telephony Service and supplementary services
The present document define the IMS Multimedia Telephony service and the minimum set of capabilities required to secure multi-vendor and multi-operator inter-operability for Multimedia Telephony and related Supplementary Services.
IMS Multimedia Telephony can support many different types of media.
IMS Multimedia Telephony service includes the following standardized media capabilities:
- Full duplex speech;
- Real time video (simplex, full duplex), synchronized with speech if present;
- Real-Time Text communication;
- File transfer;
- Video clip sharing, picture sharing, audio clip sharing. Transferred files may be displayed/replayed on receiving terminal for specified file formats
- Fax;
- Data (CS).
The support of each of these media capabilities is optional for a UE.
The IMS Multimedia Telephony service shall support the following handling of media
- Adding, removing and modifying individual media to/from an IMS Multimedia Telephony communication

## Slide 4: 22.101 Technical Specification Group Services and System Aspects; Service aspects; Service principles
IP multimedia services are not the evolution of the circuit switched services but represent a new category of services, mobile terminals, services capabilities, and user expectations. Any new multimedia service, which may have a similar name or functionality to a comparable standardised service, does not necessarily have to have the same look and feel from the user's perspective of the standardised service. Voice communications (IP telephony) is one example of real-time service that would be provided as an IP multimedia application.
The following basic requirements are be supported for IP multimedia [27]:
  IP multimedia session control shall be based on SIP [28].
  All session scenarios shall be supported; i.e. Mobile Originating and Mobile Terminating sessions against Internet/Intranet, CS or IM Mobile, ISDN, PSTN call party.
  MSISDN and SIP URL numbering and addressing schemes shall be supported.
  IP multimedia applications shall as a principle, not be standardised, allowing service provider specific variations.

## Slide 5: 22.228 Service requirements for the Internet Protocol (IP) Multimedia core network Subsystem (IMS)
Cap 5
  Support for IP multimedia sessions shall be provided in a flexible manner to allow operators to differentiate their services in the market place as well customise them to meet specific user needs. This shall be provided by the use of service capabilities in both networks and terminals, including both Personal Mobility and Terminal Mobility, for the creation and support of IP multimedia applications.
Cap 6
  IP multimedia applications shall, as a principle, not be standardised, allowing operator specific variations. It shall be possible to enable rapid service creation and deployment using service capabilities.
  It is important that commercially available IP multimedia applications are supported. In general compatibility shall be with these IP multimedia applications instead of building 3GPP-specific solutions.
7.10.2.3 VR Telepresence
In addition to the requirements in clause 7.10.2.2, the following apply for VR Telepresence:
- The IMS system shall be able to select media server(s) at appropriate location(s) involved in the session based on the VR capabilities and UE information (e.g. near to the location of user).

## Slide 6: 22.261 Service requirements for the 5G system
7.2.3.1 AR/VR
Audio-visual interaction is characterised by a human being interacting with the environment or people, or controlling a UE, and relying on audio-visual feedback. In the use cases like VR and interactive conversation the latency requirements include the latencies at the application layer (e.g., codecs), which could be specified outside of 3GPP.
To support VR environments with low motion-to-photon capabilities, the 5G system shall support:
- motion-to-photon latency in the range of 7-15ms while maintaining the required user data rate of [1Gbps] and
- motion-to-sound delay of [<20ms].

## Slide 7: 22.261 Service requirements for the 5G system
 | Scenario | Experienced data rate (DL) | Experienced data rate (UL) | Area traffic capacity (DL) | Area traffic capacity (UL) | Overall user density | Activity factor | UE speed | Coverage
1 | Urban macro | 50 Mbps | 25 Mbps | 100 Gbps/km2 (note 4) | 50 Gbps/km2 (note 4) | 10 000/km2 | 20% | Pedestrians and users in vehicles (up to 120 km/h | Full network (note 1)
2 | Rural macro | 50 Mbps | 25 Mbps | 1 Gbps/km2 (note 4) | 500 Mbps/km2 (note 4) | 100/km2 | 20% | Pedestrians and users in vehicles (up to 120 km/h | Full network (note 1)
3 | Indoor hotspot | 1 Gbps | 500 Mbps | 15 Tbps/km2 | 2 Tbps/km2 | 250 000/km2 | note 2 | Pedestrians | Office and residential (note 2) (note 3)
4 | Broadband access in a crowd | 25 Mbps | 50 Mbps | [3,75] Tbps/km2 | [7,5] Tbps/km2 | [500 000]/km2 | 30% | Pedestrians | Confined area
5 | Dense urban | 300 Mbps | 50 Mbps | 750 Gbps/km2 (note 4) | 125 Gbps/km2 (note 4) | 25 000/km2 | 10% | Pedestrians and users in vehicles (up to 60 km/h) | Downtown (note 1)
NOTE 1: For users in vehicles, the UE can be connected to the network directly, or via an on-board moving base station. NOTE 2: A certain traffic mix is assumed; only some users use services that require the highest data rates [2]. NOTE 3: For interactive audio and video services, for example, virtual meetings, the required two-way end-to-end latency (UL and DL) is 2‑4 ms while the corresponding experienced data rate needs to be up to 8K 3D video [300 Mbps] in uplink and downlink. NOTE 4: These values are derived based on overall user density. Detailed information can be found in [10]. NOTE 5: All the values in this table are targeted values and not strict requirements. |  |  |  |  |  |  |  |  | 
Table 7.1-1 Performance requirements for high data rate and traffic density scenarios.

## Slide 8: ITT4RT Support of Immersive Teleconferencing and Telepresence for Remote Terminals
The objective of this Work Item is to specify VR support in MTSI in TS 26.114 and IMS-based Telepresence in TS 26.223 to enable support of an immersive experience for remote terminals joining teleconferencing and telepresence sessions. For MTSI, the work is expected to enable scenarios with two-way audio and one-way immersive video, e.g., a remote single user wearing an HMD participates to a conference will send audio and optionally 2D video (e.g., of a presentation, screen sharing and/or a capture of the user itself), but receives stereo or immersive voice/audio and immersive video captured by an omnidirectional camera in a conference room connected to a fixed network.

## Slide 9: TR 26.918 Virtual Reality (VR) media services over 3GPP
5 Use cases for Virtual Reality 39
5.2 Event broadcast/multicast use cases 41
5.2.1 Introduction 41
5.2.2 "Infinite seating" content delivery via multicast 41
5.2.3 Event multicast to VR receivers 41
5.3 VR streaming 42
5.3.1 Use case 42
5.3.2 Areas of investigation 42
5.4 Distributing 360 A/V content library in 3GPP 42
5.4.1 Introduction: content library and target devices 42
5.4.2 Downloading content 43
5.4.3 Non-real-time MBMS distribution of VR content 43
5.4.4 Streaming content 43
5.5 Live services consumed on HMD 44
5.5.1 Introduction 44
5.5.2 Streaming content 44
5.5.3 MBMS delivery of content 44
5.5.4 Mixed delivery of content 44
5.6 Social TV and VR 44
5.6.1 Base use case 44
5.6.2 360-degree experience 44
5.7 Cinematic VR use cases 44
5.7.1 Introduction 44
5.7.2 Linear cinematic VR 45
5.7.3 Interactive cinematic VR 45
.
5.8 Learning application use cases 45
5.8.1 Introduction 45
5.8.2 Remote class participation 45
5.9 VR calls use cases 46
5.9.1 Spherical video based calls 46
5.9.2 Videoconferencing with 360 video 46
5.9.3 Gap analysis for VR calls use cases 46
5.10 User generated VR use cases 46
5.10.1 User generated 360 video and audio recording 46
5.10.2 User generated live streaming - "See what I see" 47
5.11 Virtual world communication 47
5.11.1 In-Game Communications 47
5.11.2 Virtual Meeting Place 47
5.12 HMD-based legacy content consumption 47
5.12.1 Introduction 47
5.12.2 Private TV 48
5.12.3 Floating mosaic 48
5.12.4 Enriched TV 49
5.13 Use cases for Highlight Region(s) in VR video 49
5.13.1 Initial view point for on-demand content 49
5.13.2 View point for random tuning in 49
5.13.3 Director view from artistic intent 49
5.13.4 Region-of-Interest (RoI)-driven content consumption 50

## Slide 10: Enhance MMTEL with VR in 5G Way Forward SA1
Use the use cases in VR/XR studies in SA4 as baseline.
Make gap analysis of VR enablers in 22.261
May add Immersive audio and video media into the 22.173.
IMS Multimedia Telephony service includes the following standardized media capabilities:
      Full duplex speech;
      Real time video (simplex, full duplex), synchronized with speech if present;
      Real-Time Text communication;
      File transfer;
      Video clip sharing, picture sharing, audio clip sharing. Transferred files may be displayed/replayed on receiving terminal for specified file formats
      Fax;
      Data (CS).
      Immersive audio and video media
If we specify new requirement for VR in SA1 it needs to trigger work in downstream groups.