## Slide 1: 3GPP TSG-SA WG1 Meeting #88 S1-193131 Reno, Nevada, USA, 18 - 22 November 2019 (revision of S1-19xxxx) Title: Discussion on on network performance requirements in FS_eCAV Agenda Item: Source: Nokia, Nokia Shanghai Bell, Vodafone, Bosch Contact: Betsy Covell betsy.covell@nokia.com
Abstract: This paper discusses the open issues on network performance requirements in 22.832 and proposes how they can be addressed.
Proposal: Agree the related CR in S1-193133

## Slide 2: 5G QoS characteristics as identified in TS 23.501
The 5G QoS characteristics specified in TS 23.501 describe the packet forwarding treatment that a QoS Flow receives edge-to-edge between the UE and the UPF.
  Packet Delay Budget (PDB) defines an upper bound for the time that a packet may be delayed between the UE and the UPF that terminates the N6 interface. For a certain 5QI the value of the PDB is the same in UL and DL. In the case of 3GPP access, the PDB is used to support the configuration of scheduling and link layer functions (e.g. the setting of scheduling priority weights and HARQ target operating points).
  Packet Error Rate (PER) defines an upper bound for the rate of PDUs (e.g. IP packets) that have been processed by the sender of a link layer protocol (e.g. RLC in RAN of a 3GPP access) but that are not successfully delivered by the corresponding receiver to the upper layer (e.g. PDCP in RAN of a 3GPP access) within the packet delay budget. Thus, the PER defines an upper bound for a rate of packet losses. The purpose of the PER is to allow for appropriate link layer protocol configurations (e.g. RLC and HARQ in RAN of a 3GPP access). For every 5QI the value of the PER is the same in UL and DL.

## Slide 3: Survival Time
According to the SA1 studies, for most of the IIoT applications individual packet errors can be tolerated, while exceeding survival time has more severe consequences.
This implies that: required PER >> 1 - Communication Service Availability (CSA)
If survival time is known and greater than 0, 5GS could dynamically switch to more stringent PER target if survival time is about to exceed.
If survival time is not known, 5GS would need to assume the same PER for all packets. This is problematic especially for applications that require very high availability and have a survival time greater than 0.
  If PER is set to be > 1 - CSA, the applications’ availability requirements may not be met (even if 5GS would have had means to improve the availability e.g. by activating duplication after losing one packet)
  If PER is set to be <= 1 – CSA, the system efficiency may be significantly reduced due to overprovisioning.
We propose to include ‘survival time’ as part of 5GS QoS characteristics, as this clearly helps to
Better address the IIoT applications’ reliability and availability requirements
Improve URLLC efficiency (allows more URLLC and eMBB traffic per MHz to be admitted and/or reduces resource conflicts with other URLLC traffic)

## Slide 4: Adjustable PER example
For many IIoT applications individual packet errors can be tolerated but exceeding survival time cannot. This allows for
PER >1 – Communication Service Availability
For example, when PER = 1e-3, Communication Service Availability = 1 - 1e-8, and survival time is greater than 0 and known in the 5G system, the 5G system could use PER < 1e-3 most of the time, and only if packet errors are detected adjust to PER < 1e-8 to avert a failure.
In other words, the 5G system could use PER=1e-3 for ~99.9% of the time, and PER=1e-8 for ~0.1% of the time.

## Slide 5: Other potential QoS enhancements
Communication Service Availability
If 5GS would be aware of “communication service availability”, this could be potentially used as the “more stringent” PER target. This would provide some additional efficiency improvements (on top of ‘survival time’).
Alternatively, if 5GS is not aware of CSA, 5GS could simply try to minimize the probability of exceeding survival time (which is by definition less efficient due to some overprovisioning).
However, the significance of the efficiency improvement would deserve some further analysis.
  E.g. If ‘survival time’ is provided, the “CS availability” requirement can be assumed to be very high (otherwise one could simply use PER only to achieve similar efficiency) => The “more stringent PER” target is quite rarely used (which limits the gain potential).
Communication Service Reliability (Mean-Time-Between-Failures)
Depending on the application requirements and correlation of the packet delivery failures, MTBF requirement may imply that even more stringent PER target should be used (than the one implied by CS availability)
MTBF should be taken at least as a design target, but benefit of introducing it as a QoS parameter is not fully clear.
Again, it may be enough if 5GS simply uses all possible means to avoid exceeding survival time. This maximizes the MTBF, and the benefits in terms of efficiency would benefit from some further analysis.
We propose to consider the “CS Availability” and “CS Reliability” requirements at least as design targets for 5GS, but leave it for downstream WGs to study the benefits of introducing them also as part of QoS characteristics.

## Slide 6: Message vs Packet
From application perspective, survival time refers to time that application can survive without receiving expected message. What is the mapping between “message” and “packet” (PDCP SDU)? Various solutions can be found to address any relationship between messages and packets.
  If the application message fits into a single packet;
    If packet delivery fails, it is known that (at least one) message has failed (i.e. unavailability can be detected).
    If packet delivery succeeds, it is known that (at least one) message has been successfully delivered (i.e. availability can be detected).
  If the application message is segmented into multiple packets;
    Similar to above, message failure can be detected if packet delivery fails.
    In most cases all the packets that belong to same message would arrive at same time, but at least in theory some packets of a message may arrive to 5GS later than other packets. All packets associated with a message must be successfully delivered within PDB in order to trigger a survival time restart.

## Slide 7: From TS 38.300 for Packet Error Rate