## Slide 1
Feasibility Study on 5G Timing Resiliency System (FS_5TRS)
3GPP TSG SA WG1 Meeting #90e S1-202082
E-meeting, 18-22 May 2020

## Slide 2
Overall motivation
GTTS
GPS
Fiber based timing services rolled out (e.g., GTTS)
Lawmakers mandate land-based backup/alternate systems for GPS
Vision:
5GS as timing backup/alternate for GPS offering same performance
5GS resilient to loss of GNSS/GPS, incl. integration with global fiber-based timing services for 5G resiliency
5GS as Positioning backup/alternate for GPS, especially for dense/indoor areas and working in concert with other positioning backup systems (ex. eLoran) for wide area
5G System
Critical infrastructure of society relies on timing acquired from GPS / satellite
Telecoms, finance, transportation, power, utility sector, banking, etc.
Estimated economic impact of GPS is $1.4 trillion dollars in US alone
~3% of companies rely on timing from GPS
Satellite and GPS is prone to vulnerabilities
Spoofing, jamming, and other malicious attacks
Space junk, solar storms, etc.
Insufficient for high-availability cases

## Slide 3
Potential drivers for 5G Time Synchronization Service & GPS resiliency
3GPP as organization to solve critical use-cases of society with 5G technology
Cellular Service Providers who distribute sync (and PNT) services from their network and also need GPS resiliency solution integration
5G Infrastructure Vendors to align their products with critical use-cases addressed by lawmakers
5G synchronization device vendors offering products for vertical integration
Vertical users in need of GPS resiliency or backup solutions for their use-cases, incl.
Regulatory drivers for many use-cases, e.g., NIST, ATIS, governmental contacts, etc.
Power systems sector, e.g., organizations such as CIGRE, NASPI, ABB, etc.
Banking sector, e.g., NIST, European Securities and Markets Authority (ESMA), Securities and Exchange Commission (SEC), (e.g., fraud detection in mobile transactions)
Transportation, Smart City, Autonomous cars, e.g., Deutsche Telecom, Mobatime, NIST, etc.
Traditional clock systems, incl 5G test devices, e.g., Rhode & Schwartz, Apple, etc.

## Slide 4
Where are envisioned gaps in 5G solution after R17?
5G Timing Resiliency System
Scope for Rel-17*
Scope for Rel-18
5G Time-Synchronization service decoupling from TSN
Synchronization service/capabilities exposure
Extending and reusing Rel-16 mechanisms
Introduction of TT/S as a subset of sync functionalities
PTP support over UPD/IP
Distribution of 5G clock with PTP
TT/S acting as a PTP Boundary Clock
Enhancements to 5G resiliency if GPS is compromised
5GS integration with other timing reference systems (i.e., GTTS)
Tightened holdover capabilities for network equipment
Robustness towards jamming, coverage extensions, etc.
5GS serving as timing backup/alternate for GPS offering high performance
Time reference management and distribution requirements within the whole 5GS network
Positioning backup/alternate for GPS,
especially for dense/indoor areas and
working in concert with other positioning backup systems (ex. eLoran) for wide area
*) Service requirements already established and are pre-requisite for FS_5TRS proposal

## Slide 5
Backup Slides

## Slide 6
Some market messages
1.5 million Synchronization Nodes world-wide in 2017 (ref: GNSS agency)
*) Area under consideration for growth by e.g. CIGRE organization
Source ISBN 978-92-9206-032-9 report, Albedo Telecom, Inc
Criticality and vulnerability of GPS provided timing to infrastructure has been assessed in many recent reports
  E.g., US ATIS, EU UFM, etc.
Sync services are mainly consumed by the telecoms sector, but other sectors usage is growing
  E.g., Power/utility sector is looking into adopting 5G as alternative to GPS timing systems (ref: CIGRE)
Such use-cases cannot be addressed by existing gPTP/TSN solution
*

## Slide 7
US National Timing Resilience and Security Act (TRSA)
Movement by lawmakers – mandating land-based GPS alternatives
Key requirements
Terrestrial, wireless
Synchronized to UTC
Difficult to disrupt
Able to penetrate underground/inside buildings
Capable of deployment to remote locations
Expandable to provide position, navigation and timing (PNT), and, work in concert with similar systems such as eLoran
5G can match above requirements
5G will be attractive alternative due to global footprint and infrastructure justified by many diverse use-cases

## Slide 8
Smart Grid industry exploring use of 5G for Time Sync
CIGRE is a global community for power system:
JWG N° B5/D2.67: Time in Communication Networks, Protection and Control Applications – Time Sources and Distribution Methods
  Telecom distribution of timing signals as back-up to local clocks
  Within the WG purpose they are considering 5G as one of the potential way of doing synchronize time in power system substations
WG N°D2.42: Synchronization and time distribution in communication networks for time sensitive distributed operational applications in the power grid
    In the motivation the adequate design of telecommunication networks is mentioned
CIGRE and NASPI efforts mainly focus on identifying methods for reliable delivery of precise, accurate time signals for wide-area device and data synchronization
NASPI (North American SynchroPhasor Initiative)
Time Synchronization Task Force goals: help the user community implement consistent, reliable time across a substation and synchronized across a power system
Notes: JWG N° B5/D2.67 Scope: Establish a reference document for time sources and time distribution in Protection, Automation and Control Systems (PACS) including recommendations and best practices for related specifications and designs
WG N°D2.42 Scope: Assess time distribution and frequency synchronization requirements and solutions for synchronizing power System automation applications

## Slide 9
Example applications and mapping to 5G synchronization performance
Release 18+
Release 17
Sync error*:
250ns
*) For wide applicability, the achieved time synchronization error should be achievable in the frequency bands applicable for wide area deployments (e.g., 30kHz sub-carrier spacing, FR1)
500ns
1ms
Release 16
10ms
100ms
1ms+
Smart grid:
Synchro-phasors
IRT loops:
UE-UE sync (5G R17)
Prof. audio production
Automation, VIAPA, TSN, etc. (5G R16/R17)
HFT for automated orders
Railway, metro solutions
Tele-surgery, tele-diagnosis
HFT for manual orders
Basic clock systems, incl. smart watches
Power grid: Dynamic disturbance recorders

## Slide 10
Proposed way forward
3GPP to engage with Public and Vertical eco-system to investigate potential of supporting 5G synchronization beyond manufacturing use-cases (US gov, ATIS, CIGRE, etc), including
Timing backup/alternate for GPS offering same performance and fulfilling requirements of e.g. the National Timing Resiliency & Security Act
Enhancements to 5G resiliency if GPS is compromised
Positioning backup/alternate for GPS, especially for dense/indoor areas and working in concert with other positioning backup systems (e.g., eLoran) for wide area
Approach in 3GPP and time-line
Collect requirements and use cases in new Release-18 SID

## Slide 11
Selected references
Synchronization market: http://www.albedotelecom.com/src/lib/WP-Sync-Market.pdf
National Timing Resiliency and Security Act: https://www.congress.gov/bill/115th-congress/senate-bill/2220/
Other emerging requirements: https://ec.europa.eu/docsroom/documents/28325/attachments/1/translations/en/renditions/native
Some studies related to GNSS/GPS vulnerabilities
https://www.gps.gov/governance/advisory/meetings/2016-12/calabro.pdf
https://www.gps.gov/systems/gps/performance/2018-GPS-SPS-performance-analysis.pdf
https://ufm.dk/publikationer/2019/denmarks-economic-vulnerability-to-a-loss-of-satellite-based-pnt
https://www.raeng.org.uk/publications/reports/global-navigation-space-systems
https://assets.publishing.service.gov.uk/government/uploads/system/uploads/attachment_data/file/619544/17.3254_Economic_impact_to_UK_of_a_disruption_to_GNSS_-_Full_Report.pdf
Additional reading:
https://www.gpsworld.com/gps-backup-demonstration-projects-explained/
https://insidegnss.com/gps-backup-may-get-more-attention-as-lawmakers-highlight-risks-to-space-assets-critical-infrastructure/
https://electronics.howstuffworks.com/everyday-tech/why-united-states-needs-backup-for-gps.htm
https://www.silicon.co.uk/security/support-gps-backup-hacking-219441
https://www.pts.se/sv/bransch/internet/robust-kommunikation/atgarder/korrekt-och-sparbar-tid-och-takt/
https://www.netnod.se/time-and-frequency
https://www.npl.co.uk/npltime
http://www.refimeve.fr/index.php/en/presentation-eng/description-of-the-project.html
http://empir.npl.co.uk/tifoon/