## Slide 1: Study on Support for Service Function Chaining in 5G System (FS_SFCin5GS]
Ellen Liao (ELLEN.C.LIAO AT INTEL.COM)
3GPP TSG-SA WG1 Meeting #90-e S1-202102
E-meeting, 18-22 May 2020

## Slide 2: Concept of Service Function Chaining
The examples of service functions include, but are not limited to the following: firewall functions, NAT, URL filter, Lawful inspection (LI), deep packet inspection (DPI), IP tunnel endpoints, Packet classifiers, application detection and control (ADC), TCP proxies, load balancers, transcoders, application policy control, protocol and video optimization, etc.
ITU-T-Y.Sup41: Service chaining service (SCS) provides a mechanism to dynamically build service function chains (SFCs) and then make incoming packets forward through the SFC. With these dynamics, the SFC can rapidly and easily be generated and modified according to the service features carrying in packets.

## Slide 3: Service Function Chaining Use Cases considered in 3GPP
(S)Gi-LAN is one the use case of service function chaining, which is the middle box provided by a wide variety of vendors and out of 3GPP scope, used to differentiate and monetize services between the mobile network and the packet data network.
However, (S)Gi-LAN in EPS is currently considered out of scope of 3GPP as indicated in TS22.101. As such, the policy control of (S)Gi-LAN needs to be coordinated with the existing traffic steering policy in EPS.
The same assumption applies to N6-LAN in 5G context. The fragmentation of the network functionalities result in many challenges in 5G system.
Ref: 3GPP TR 22.808 V14.1.0

## Slide 4: Challenges in 5G System
Lacking consolidated network resource management of service chaining between 5GS and N6-LAN would cause potential interoperability issues even within the mobile network of the same network operator and result in uncoordinated and inefficient service function path settings for routing the E2E service with desired service functions;
Losing control over the chained service functions in N6-LAN, which contribute to delay in every hop in N6-LAN, results in difficulties to achieve the latency requirement for some services targeting at ultra-reliable low-latency.
For example, interactive AR/VR gaming, remote control of UAV, Audio-Visual Service Production, industrial automation, critical medical applications, self-driving vehicles, etc.
Providing compromised service experiences to the users when considering service continuity, e.g . upon mobility between HPLMN and VPLMN, or between HPLMN and NPN.
Lacking of flexibilities to provision versatile vertical services in different networks and services deployment scenarios and in fulfilling required KPIs for the services.
Missing consideration of many advanced features in 5G network, e.g. network slicing, network function virtualization, non-public network, and edge computing, etc., in support of FMSS/eFMSS.
Notes:   The lack of a standards developing organization with oversight for N6-LANs has resulted in a wide range of N6-LAN architectural approaches even within the same mobile network operator group. It has led to a broad vendor solution mix, making the management, maintenance, and evolution of the N6-LAN operationally challenging.

## Slide 5: Other SDOs Activities
ITU-T Y.2242 considers the cases when relevant network functions are virtualized and provides Recommendations to support service function chaining in mobile networks.
IETF RFC 7665 and IETF RFC 8300 introduce service function chaining architecture with a chain orchestrator and provide methods of coordinating dynamic service function chaining in mobile networks.
In summary,
  5GS support to consolidate service functions and service function chaining can provide flexibility to manage required service functions into one network instance.
  The service deployment and configuration can be greatly simplified and at scale. As such, it is foreseen as a promising enhancement to tackle the aforementioned challenges in 5GS.

## Slide 6: Example of Use Cases (1/3)
For the use case of streaming video service, different content providers may need different service functions for video optimization and security functions based on users subscription, network service subscription, etc.
With the control and management of the SFCs in 3GPP network, the network operators can provision the service function chaining service by including value added services and security features to the content service providers.

## Slide 7: Example of Use Cases (2/3)
In an AR/VR production use case in NPN, different broadcasters may need different service functions for their on-site devices, e.g. camera and mics.
Currently, each broadcasters need to manually configure its N6-LAN or provide the configuration of N6-LAN to NPN provider as part of service agreement.
With service chaining service enabled in a NPN, the network provider can exposure service function chaining service to third parties and allow them to configure required service function paths for their devices.

## Slide 8: Example of Use Cases (3/3)
In a 3GPP V2X use case, when a vehicle moves in its HPLMN or across different roaming networks, it is beneficial that the same service functions, e.g. TCP proxies, transcoders, firewall, etc., are provided, configured, and managed by the mobile networks in order to ensure the provisioning of required KPIs and security functions with the consistent carrier grade performance in 5GS.
For example, in TR22.886 clause 5.27.6: Support of automated driving in multi-PLMN environments.
However, in case of roaming, current eFMSS supports only home routed traffic steering.

## Slide 9: Considerations on existing 3GPP requirements
Some existing requirements related to FMSS/eFMSS are captured in TS 22.101, addressing only part of the target use cases and functionalities, e.g.:
  support to define and modify traffic steering policies that are used to steer traffic in (S)Gi-LAN (considered out of scope) containing operator or 3rd party service functions
  The 3GPP Core Network shall be able to define different traffic steering policies for a user’s traffic on a per session basis (e.g. for applying parental control, anti-malware, DDoS protection, video optimization).
  The 3GPP Core Network defines traffic steering policies based on one or more pieces of information such as: network operator’s policies; user subscription; application characteristics such as: application type, protocol, target address name (URL) and application provider, etc.
  In case of roaming, the HPLMN shall be able to apply traffic steering policies for home routed traffic.
New use cases, requirements and gaps should be studied, e.g. considering:
  Service functions in 5G system
  Network slicing, edge computing, non-public network, and network functions virtualization
  Service continuity and roaming support

## Slide 10: SA1 Rel-18 Study Proposal - SID Objectives
Study use cases and requirements in support of service function chaining service in 5G system, including:
    Support of on demand service function chaining service in 5GS related to:
      provide definition of supported service functions and service function paths;
      Create, configure and control service functions and service function paths in 5GS per application or per user;
      coordinate service function paths with consolidated orchestration and control;
      Exposure service function and service function paths provided by 5GS to third parties;
    Support of the coexistence of service chaining aware traffic and service chaining unaware traffic.
    Support of service continuity in the following scenarios:
      upon mobility between the HPLMN and a VPLMN,
      upon mobility between the HPLMN and an NPN,
      upon mobility between a temporary serving network and a temporary service provider.
Gap analysis of the identified requirements versus existing 5G requirements or functionalities.

## Slide 11: BACKUP Slide

## Slide 12: 3GPP TS22.101 clause 30: FMSS
3GPP 22.101, FMSS, the following requirements apply:
The 3GPP Core Network shall be able to define and modify traffic steering policies that are used to steer traffic in (S)Gi-LAN containing operator or 3rd party service functions e.g. to improve e.g. the user’s QoE, apply the bandwidth limitation and provide valued added services.
Traffic steering policy shall be able to distinguish between upstream and downstream traffic.
The 3GPP Core Network shall be able to define different traffic steering policies for a user’s traffic on a per session basis (e.g. for applying parental control, anti-malware, DDoS protection, video optimization).
The 3GPP Core Network defines traffic steering policies based on one or more pieces of information such as:
  network operator’s policies
  user subscription (e.g. user’s priority, the status of optional subscriber services from the subscription data, based on service provider used, subscribed QoS)
  user's current RAT
  the network (RAN and CN) load status
  application characteristics such as: application type (video, web browsing, IM, etc), application protocol ( HTTP, P2P, etc), target address name (URL) and application provider (My tube, etc)
  Time
  UE location
  information (e.g. APN) of the destination network (i.e. a PDN or an internal IP network) of traffic flow
  In case of roaming, the HPLMN shall be able to apply traffic steering policies for home routed traffic.
Note: Traffic steering policies for local breakout is not specified.

## Slide 13: BACKUP Slides For Presentation

## Slide 14: Motivation of FS_SFCin5GS
Ref: 3GPP TR 22.808 V14.1.0
(S)Gi-LAN is one use case of service function chaining, which is the middle box provided by a wide variety of vendors and out of 3GPP scope as indicated in TS22.101, used to differentiate and monetize services between the mobile network and the packet data network.
  The examples of service functions include: firewall functions, NAT, URL filter, Lawful inspection (LI), deep packet inspection (DPI), IP tunnel endpoints, application detection and control (ADC), TCP proxies, load balancers, transcoders, and video optimization, etc.
  The policy control of (S)Gi-LAN needs to be coordinated with the existing traffic steering policy in EPS. The same assumption applies to N6-LAN in 5G context.
  The fragmentation of the network results in many challenges in 5GS.
Other SDOs activities: ITU-Y provides recommendations to consolidate service functions and service function chaining configuration and management with mobile network. IETF specs provides some mechanisms for supporting dynamic SFCs.
  The 5GS support to consolidate service functions and service function chaining can provide flexibility to manage required service functions into one network instance. The service deployment and configuration can be greatly simplified and at scale.
New use cases, requirements and gaps should be studied, e.g. considering: Service functions in 5G system, network slicing, edge computing, network functions virtualization, non-public network, and service continuity and roaming support.
Notes: The examples of service functions include, but are not limited to the following: firewall functions, NAT, URL filter, Lawful inspection (LI), deep packet inspection (DPI), IP tunnel endpoints, Packet classifiers, application detection and control (ADC), TCP proxies, load balancers, transcoders, application policy control, protocol and video optimization, etc.
ITU-T-Y.Sup41: Service chaining service (SCS) provides a mechanism to dynamically build service function chains (SFCs) and then make incoming packets forward through the SFC. With these dynamics, the SFC can rapidly and easily be generated and modified according to the service features carrying in packets.

## Slide 15: Examples of Use Cases
Use Case1: Streaming video service
Different content providers may need different service functions for video optimization and security functions based on users subscription, network service subscription, etc.
With the control and management of the SFCs in 3GPP network, the network operators can provision the service function chaining service by including value added services and security features to the content service providers.
Use Case 3: V2X
When a vehicle moves in its HPLMN or across different roaming networks, it is beneficial that the same service functions, e.g. TCP proxies, transcoders, firewall, etc., are provided, configured, and managed by the mobile networks in order to ensure the provisioning of required KPIs and security functions with the consistent carrier grade performance in 5GS.
TR22.886 clause 5.27.6: Support of automated driving in multi-PLMN environments.
Currently eFMSS supports only home routed traffic steering.
Use Case2: AVPROD
Different broadcasters may need different service functions for their on-site devices, e.g. camera and mics. Currently, each broadcasters need to manually configure its N6-LAN or provide the configuration of N6-LAN to NPN provider as part of service agreement.
With service chaining service enabled in a NPN, the network provider can exposure service function chaining service to third parties and allow them to configure required service function paths for their devices.

## Slide 16: Challenges of supporting SFs/SFC outside of 5GS
Lacking consolidated network resource management of service chaining between 5GS and N6-LAN would cause potential interoperability issues even within the mobile network of the same network operator and result in uncoordinated and inefficient service function path settings for routing the E2E service with desired service functions;
Losing control over the chained service functions in N6-LAN, which contribute to delay in every hop in N6-LAN, results in difficulties to achieve the latency requirement for some services targeting at ultra-reliable low-latency.
For example, interactive AR/VR gaming, remote control of UAV, Audio-Visual Service Production, industrial automation, critical medical applications, self-driving vehicles, etc.
Providing compromised service experiences to the users when supporting service continuity, e.g. upon mobility between HPLMN and VPLMN, or between HPLMN and NPN.
Lacking of flexibilities to provision versatile vertical services in different networks and services deployment scenarios and in fulfilling required KPIs for the services.
Missing consideration of many advanced features in 5G network, e.g. network slicing, network function virtualization, non-public network, and edge computing, etc., in support of FMSS/eFMSS.
  Enabling support of SFC in 5GS is foreseen as a promising enhancement to tackle the aforementioned challenges in 5GS. It is proposed to study the use cases and potential requirements in this study of FS_SFCin5GS.
Notes:   The lack of a standards developing organization with oversight for N6-LANs has resulted in a wide range of N6-LAN architectural approaches even within the same mobile network operator group. It has led to a broad vendor solution mix, making the management, maintenance, and evolution of the N6-LAN operationally challenging.