## Slide 1: Motivation for R18 5G enables Smart Grid SID
China Telecom,
ZTE, China Southern Power Grid, CEPRI-China, Huawei, Fudan

## Slide 2: Basic Concepts of Smart Grid
Source: White Paper of 5G Assists Smart Grid Application
Power generation
Resource Optimization
Smart Grid
Usage Efficiency
Interactive Consumption
Flexible & Reliable for Distribution
Safety & Efficiency for Transmission

## Slide 3: Challenges for Smart Grid
Clean & Friendly power generation
Safety & High efficiency power transforming & transmission
Flexible & Reliable power distribution
interactive & On-demand power consumption

## Slide 4: Example of Distribution Automation system
KPI required for the differential protection:
Throughput: 2Mbps
Latency < 10ms, Clock sync < 10us，latency jitter<+-50us/<40km,
Reliability: 99.999%
Isolation and safety: need to be isolated with other management working area III and IV
Connection density: x * 10/km2
Compared with TS22.104 Table 5.2-1, more KPI need to be studied.
Source: WP of 5g-network-slicing-enabling-the-smart-grid
White Paper of 5G Assists Smart Grid Application

## Slide 5: Example of metrology automation & on-demand power supply
KPI required:
Throughput: UL >2Mbps, DL 1Mbps
Latency < 200ms for accuracy charging control; 3s for information acquirement
Reliability: 99.9%
Isolation and safety: need to be isolated with other management working area III & I
Connection density: x * 100/km2 for concentrated reading mode; for user mode, x*10000/km2
Compared with TS22.104 , this kind of KPI need to be studied.
Source: WP of 5g-network-slicing-enabling-the-smart-grid
White Paper of 5G Assists Smart Grid Application

## Slide 6: Example of smart and accurate on-site patrol & remote maintain
KPI required:
Throughput: 4-10Mbps(transformer substation & electric transmission line), 20-100Mbps(distribution substation & remote control & emergency ad-hoc network)
Latency < 200ms
Reliability: 99.9%
Isolation and safety: belong to III area
Connection density: 1-2/area, 5-10/area
Source: WP of 5g-network-slicing-enabling-the-smart-grid
White Paper of 5G Assists Smart Grid Application
Compared with TS22.261, TS22.104, TS22.125 , this set of KPI need to be evaluated.

## Slide 7: Example of distributed power supplies
KPI required:
Throughput: >2Mbps
Latency < 1s(control type), 3s(collection type)
Reliability: 99.9% for collection type, 99.999% for control type
Isolation and safety: across I,II,III area, the application need to be isloated
Connection density: million or 10 million/area
Compared with TS22.261, TS22.104, TS22.125 , this set of KPI has not been supported.
Source: White Paper of 5G Assists Smart Grid Application

## Slide 8: Object of the SID
The aim of this work is to study use cases and potential new service requirements for 5G system to support smart grid, including:
  To investigate potential new 5G system service requirements and KPIs to support emerging Smart Grid services required defined in other bodies, e.g. IEC.
  To investigate 5G service requirements and KPI to support Smart Grid applications in specific phase or across multiple phases: e.g. on-demand power supply, distributed power supply system, distribution automation, higher accuracy power load measurement and control, metrology automation, etc.
  gap analysis on between potential new requirements and existing requirements and functionalities for smart grid communications supported by 3GPP specs TS22.104/125/261 etc.