## Slide 1: Motivation for R18 5G multi-media enhancements SID
Huawei

## Slide 2: Challenges to support multimedia services in 5GS
4K/8K UHD multimedia services will become more and more popular in next 5 years. It provides high quality video experience for customers, however, it has challenges to support various 4K/8K UHD media services which require both high bandwidth and low latency；
Use Cases | Characteristic parameter (KPI) |  | 
 | Max Allowed End-to-end latency | Service bit rate: user-experienced data rate | Reliability
Gaming or Interactive Data Exchanging | 10ms | 0.1-[1] Gbit/s supporting visual content (e.g. VR based or high definition video) with 4K, 8K resolution and up to 120fps content. | 99.99%
Consume VR content via tethered VR headset | [5 -10] ms | 0.1-[10] Gbit/s | [99,99%]
3GPP TS 22.261 Table 7.6.1-1 KPI Table for additional high data rate and low latency service
It is necessary to study potential 5GS enhancements to improve the QoE of multimedia services and increase the system capacity at the same time.

## Slide 3: Example of current optimization-- Adaptive Bitrate Streaming
Obvious delay，25s
  ABS makes it possible to switch the video quality during the playback in order to adapt to the current network conditions.
  Based on network measurements by the client itself, the client-side requests the next part of the video from the server-side in the appropriate bit rate level which is best suited under current network conditions.
Problems without network coordination:
  ABS in application layer may not be synchronized in real time with the current conditions, which results in long react delay or large video quality fluctuations；
  Concurrent access from multiple clients leads to network resource contention and unfairness.
Source: An experimental evaluation of rate-adaptive video players over HTTP, Signal Processing: Image Communication 27 (2012)271–287
There would be potential network enhancements to further improve the QoE of high quality multimedia services, for example, if 5G network could have close coordination with these popular optimization mechanisms on application layer.
Figure: Adaptive Bitrate Streaming
Instable video quality and unfairness for the contention from multi-users
Random competition leads to waste of resources and collisions.
Source: Probe and Adapt: Rate Adaptation for HTTP Video Streaming At Scale, IEEE JOURNAL ON SELECTED AREAS IN COMMUNICATIONS, VOL. 32, NO. 4, APRIL 2014

## Slide 4: Use case 1: video traffic priority awareness
Codec characteristics : I, B, P frame
Potential enhancements:
The usage of network resource can be optimized if the 5G network can learn the different priorities for video traffic (e.g., different video frames/layers would have different priorities) . For example, the 5G network could provide guaranteed transfer service for base-layer stream while providing best-effort transfer service for enhanced-layer stream.
Codec characteristics : SVC Layer
Codec characteristics : FOV/non-FOV streaming
  360-degree omnidirectional video
Low quality omnidirectional video streaming
FoV tiles/slices with high quality
  VR video encoder

## Slide 5: Use case 2: Playback behavior awareness
Potential enhancement:
When being aware of playback behavior (e.g. initial start-up, pause or jump), the network could temporarily provide a higher DL data rate for multimedia services during initial start-up stage for reducing the waiting delay
Initial start-up
Index download，
Playback buffering
Start-up waiting delay
Playback buffering
Normal playback
Jump to new segment
Normal playback
Index download，
Playback buffering
Start-up waiting delay

## Slide 6: Use case 3: Traffic pattern awareness
Background:
Traffic Pattern of media segment: traffic pattern of media segment based on its resolution, frame rate, encoding level, GoP size.
ON-OFF behavior of client: The ON-OFF behavior of client is related with buffer pre-filling operation of client and actual bandwidth of network.
ON-OFF behavior of client
Potential enhancement:
The resource scheduling of 5G network can be optimized when serving multiple UEs (e.g., avoid burst traffic), if knows about the on-off behavior of the video playback client
Parameters of Media Assumption: The ratio of I frame, P frame and B frame is 1:6:18; GoP size is 5 Sec.. |  |  |  |  | Size of I, P and B; buffer pre-filling time Assumption: Buffer size of client is 10 Sec.; BW of network is 100Mbps |  |  | 
resolution | Vertical Pixels | Horizontal Pixels | Frame Rate, frames/Sec. | GOP size, Sec. | I frame，kbit | P frame，kbit | B frame， kbit | buffer pre-filling time, Sec
4K | 3840 | 2160 | 60 | 5 | 9257 | 3240 | 1296 | 12
1080P | 1920 | 1080 | 60 | 5 | 2314 | 810 | 324 | 3
720P | 1280 | 720 | 60 | 5 | 1028 | 360 | 144 | 1
480P | 720 | 480 | 24 | 5 | 385 | 135 | 54 | 0.2
Buffer Pre-filling time (time needed to complete buffer pre-filling)
Relationship between size of 10s Media Segment and data rate
e.g., for media stream with data rate 503kbps, the maximum size of the segment is 1400KBytes.

## Slide 7: Use case 4: Computation Power/capacity awareness
3rd party VR
CPU/GPU
User Plane
Function
FOV rendering
Edge Computing Node
API
Background:
The computation of AR/VR rendering is off-loaded to an edge computing node in which the VR game is rendered based on user's field of view (FoV) and control actions, can be used to provide better QoE for e.g., real-time VR gaming services.
This kind of use cases would consume the computation power/capacity on the Edge Computing Node and thus the computation power/capacity may become another critical bottleneck impacting the overall output of the network.
Potential enhancement:
Existing requirements in TS 22.261 only take the latency as the only factor (i.e., the shortest user plane path) into account.
The network is able to achieve a better QoE for VR users if better coordination between the performance of the network and the computation power/capacity can be made.
Existing Requirements in TS 22.261 Clause 6.5.2
The 5G system shall support mechanisms to enable a UE to access the closest Service Hosting Environment for a specific hosted application or service.
The 5G network shall enable instantiation of applications for a UE in a Service Hosting Environment close to the UE's point of attachment to the access network.

## Slide 8: Object of the SID
The objective of this SID includes:
  Studying the use cases for providing better QoE for various type of consumer-oriented multimedia service (e.g., live and on-demand video streams, Augment Reality (AR) / Virtual Reality (VR) service) in 5GS, in particular, to study how 5GS could cooperate with typical and mostly used mechanisms in multimedia application layer (e.g., DASH, Playback buffer management and FOV/edge rendering) to increase the network capacity and also improve QoE of these multimedia services.
  Identifying potential performance and service requirements based on above use cases.
Note: This study will not cover those use cases discussed in AVPROD/VIAPA.