## Slide 1: Motivation for R18 enhanced Network controlled interactive service WID
Huawei, Huawei Device
3GPP TSG-SA WG1 Meeting #90
Electronic Meeting, 18 - 22 May 2020
S1-20

## Slide 2: Background
In Rel17, use cases and KPIs for network controlled interactive service have been specified. One of them is
  Use Case：
  KPI：
Consume VR content via tethered VR headset – This use case involves a tethered VR headset receiving VR content via a connected UE; this approach alleviates some of the computation complexity required at the VR headset, by allowing some or all decoding functionality to run locally at the connected UE. The requirements in the table below refer to the direct wireless link between the tethered VR headset and the corresponding connected UE.
Use Cases | Characteristic parameter (KPI) |  |  | Influence quantity |  | 
 | Max Allowed End-to-end latency | Service bit rate: user-experienced data rate | Reliability | # of UEs | UE Speed | Service Area (note 2)
Consume VR content via tethered VR headset (note 6) | [5 -10] ms (note 5) | 0.1-[10] Gbit/s (note 5) | [99,99%] | - | Stationary or Pedestrian | -
NOTE 5: The decoding capability in the VR headset and the encoding/decoding complexity/time of the stream will set the required bit rate and latency over the direct wireless link between the tethered VR headset and its connected UE, bit rate from 100 Mbit/s to [10] Gbit/s and latency from 5 ms to 10 ms. NOTE 6: The performance requirement is valid for the direct wireless link between the tethered VR headset and its connected UE. |  |  |  |  |  | 

## Slide 3: Consume VR content via tethered VR headset
The use case covers the following scenarios:
  Cloud VR
    Scenario 1
    Scenario 2
  Local VR
    Scenario 3
    Scenario 4
In scenario 1/3, the VR headset can be directly controlled by network
In scenario 2/4, the VR headset can be indirectly controlled by network

## Slide 4: Requirement Gap Analysis
Requirements for the direct wireless link have been studied for EPS and captured in TS 22.278 7A. They should be applied to 5GS, according to the statement in TS 22.261 5.1.2.2.
For the consumed tethered VR headset services, the requirements in TS 22.278 7A can cover scenario 1/3, but not fully cover scenario 2/4.
  Gap1: ProSe is only available for public safety use case to the ProSe-enabled UE when the UE is not served by network:
  Gap 2: Pre-configuration with the permission to use ProSe is only available for the public safety use case
  Gap 3: Network-controlled use of resources for ProSe is only available when the UE is served by network

## Slide 5: Objective of the WID
  Add the requirements to enable a device not served by NG-RAN to perform communication over direct wireless link between devices.
  For this objective, the potential requirements include:
    ProSe-enabled UEs can use ProSe for commercial when not served by NG-RAN when at least one of two ProSe-enabled UEs is served by NG-RAN.
    The operator shall be able to pre-configure ProSe-enabled UEs (e.g., in the USIM or ME) not served by NG-RAN with the permission to use ProSe with another ProSe-enabled UE which is served by NG-RAN for commercial when using operator’s spectrum.
    The 5G network shall be able to continuously control the use of NG-RAN resources for ProSe, as long as the ProSe is using operator's spectrum.

## Slide 6: Thanks!