## Slide 1: Use Case for Determination of 5G Time Synchronization Budget
Michael Bahr, Siemens

## Slide 2: Time Synchronization in Vertical Domains
Different vertical domains have their specific requirements on and profiles for time synchronization:
  IEC/IEEE 60802 Time-sensitive networking profile for industrial automation
  Energy distribution IEC 61850-9-3 [3]
  Audio/Video production

## Slide 3: IEEE 60802 – Definitions Time Synchronization
Relative time error TER(A,B) is the difference between the time of clock A (TA) and the time of clock B (TB), i.e., TER(A,B) = TA – TB. (IEC/IEEE 60802 [1-3.2] [14])
Maximum absolute relative time error max|TER| is the maximum of the absolute value of the relative time error. (IEC/IEEE 60802 [1-3.2][14])
Constant time error cTE is the time error or relative time error that is constant in time (i.e., static). (IEC/IEEE 60802 [1-3.2] [14])
Dynamic time error dTE is the zero-mean, random component of the time error. (IEC/IEEE 60802 [1-3.2] [14])
The term time synchronization or synchronicity budget of the 5G system corresponds to the maximum absolute relative time error of the 5G system.

## Slide 4: IEEE 60802 – Requirements on Time Synchronization
 | Constant Time Error | Dynamic Time Error
PTP Link [1-5.1.8.2] | 10 ns | 0 ns
PTP Instance [1-5.1.8.2] | 5 ns | 50 ns
Transfer of time from ClockSource to ClockMaster entity at sync master [1-5.1.8.3] | 10 ns | 20 ns
Transfer of time from ClockSlave to ClockTarget entity at sync device [1-5.1.8.3] | 10 ns | 20 ns
Working Clock domain
Longest path between sync master and any sync device is 64 hops [1-5.1.5]
max|TER| <= |1µs| [1-5.1.5] between application clock outputs of sync master and any sync device

## Slide 5: From wired TSN networks to integrated 5G networks / TSN networks
preferred deployment

## Slide 6: Use Case 1: Manufacturing Robots (wireless/wired)

## Slide 7: Use Case 1b: Manufacturing Robots (wireless/wired) with Sync Master in network

## Slide 8: Use Cases: Manufacturing Robot (wireless)
graphic only simplified illustration of manufacturing robot  can be much more complex in reality
time-synchronized devices are connected in line topology  up to 16+ wired hops inside manufacturing robot
up to 8 wired hops inside manufacturing robot already cover reasonable set of varied use cases
UE in „non-rotating“ part to have stable position of antenna  UE rather at the beginning of local network

## Slide 9: Use Case 2: Manufacturing Robots (wireless)

## Slide 10: Smart Grid - PMUs
Border clock is allowed to have a time sychnronization error of  250 ns [IEC 61850-9-3].

## Slide 11: Proposal for 5GS Time Sync Budget Requirement
5GS Time Sync Budget needs to provide some flexibility for non-3GPP network parts wrt number of hops (e.g. internal wired network of manufacturing robots, path from sync master to NW-TT).
Many industrial use cases have constraints from the application and the operational technology, that require more hops as the at least required, minimalistic two hops (in each non-3GPP network part).
  a general, hierarchical network structure that follows the structure of the different processes and of the factory organization. It might be necessary to pass through several switches in the hierarchy or structure from the sync master to the NW-TT.
  Many working clock domains are deployed in a factory, each with its own sync master. The various sync masters are distributed all over the factory at different places. It might be difficult to place all the corresponding NW-TTs close to the sync master.
  Mechanical constraints that require a line topology such as manufacturing robots.
~800 ns of synchronicity budget for the 5GS (scenarios with up to 8 hops in manufacturing robot). With installation guidelines in place that limit the number of hops for an optimized network layout of the non-3GPP network, this sync budget level is sufficient.
 800 ns is the proposed value for the 5GS time synchronization budget requirement.
 The time synchronization budget assigned to the 5G system in integrated 5G TSN networks for a working clock domain shall be at most 800 ns.

## Slide 12: References
[{12}] IEC 65C/987/CD. “Time-sensitive networking profile for industrial automation”, Committee Draft (CD), Sep 2019
[14] IEC/IEEE 60802, "Constraints about Sync", v1.0, 23 Aug, 2019, 60802-Steindl-ConstraintsAboutSync-0919-v10.pdf.
[15] IEC/IEEE 61850-9-3: "Communication networks and systems for power utility automation – Part 9-3: Precision time protocol profile for power utility automation“
3GPP TR 22.832 “Study on enhancements for cyber-physical control applications in vertical domains”