## Slide 1: Study on Support for Service Function Chaining in 5G System (FS_SFCin5GS)
Ellen Liao (ELLEN.C.LIAO AT INTEL.COM)
3GPP TSG-SA WG1 Meeting #91-e S1-203161
E-meeting, 24 Aug.-02 Sept. 2020

## Slide 2: Motivation of FS_SFCin5GS
Ref: 3GPP TR 22.808 V14.1.0
(S)Gi-LAN is one use case of service function chaining, which is the middle path between the mobile network and the packet data network for providing services differentiation and monetization.
  The examples of service functions include firewall functions, NAT, URL filter, Lawful inspection (LI), deep packet inspection (DPI), IP tunnel endpoints, application detection and control (ADC), TCP proxies, load balancers, transcoders, and video optimization, etc.
  The policy control of (S)Gi-LAN needs to be coordinated with the existing traffic steering policy in EPS. The same assumption applies to N6-LAN in 5G context.
  In TS22.101, service function chaining is considered as out of 3GPP scope. The fragmentation of the network results in many challenges in 5GS.
Other SDOs activities:
  ITU-Y provides recommendations to consolidate service functions and service function chaining configuration and management with mobile network.
  IETF specs provides some mechanisms for supporting dynamic SFCs.
The 5GS support for service function chaining services can provide flexibility to manage required service functions into one network instance. The service deployment and configuration can be greatly simplified and scalable.
Notes: The examples of service functions include, but are not limited to the following: firewall functions, NAT, URL filter, Lawful inspection (LI), deep packet inspection (DPI), IP tunnel endpoints, Packet classifiers, application detection and control (ADC), TCP proxies, load balancers, transcoders, application policy control, protocol and video optimization, etc.
ITU-T-Y.Sup41: Service chaining service (SCS) provides a mechanism to dynamically build service function chains (SFCs) and then make incoming packets forward through the SFC. With these dynamics, the SFC can rapidly and easily be generated and modified according to the service features carrying in packets.

## Slide 3: Examples of Use Cases
Use Case1: Streaming video service
Different content providers may need different service functions for video optimization and security functions based on user's subscription, network service subscription, etc.
  Currently, each content providers may deploy and configure their N6-LANs or provide the configuration of N6-LAN to network provider as part of service agreement.
Use Case 3: V2X services
For V2X services, when a vehicle moves in its HPLMN or across different roaming networks, it is important that the same service functions, e.g. TCP proxies, transcoders, firewall, etc., are provided, configured, and managed by the 5G networks, e.g. TR22.886 clause 5.27.6: Support of automated driving in multi-PLMN environments.
  Currently, eFMSS supports only home routed traffic steering.
Use Case2: AVPROD
Different broadcasters may need different service functions for their on-site 5G devices, e.g. camera and mics.
  Currently, each broadcasters need to manually configure their N6-LAN or provide the configuration of N6-LAN to NPN provider as part of service agreement.
With SFC service enabled in 5GS, the network operators can provision service function chaining services in 5G network to content providers
With SFC service enabled at NPN, the network provider can exposure service function chaining service to third parties and allow them to configure required service function paths for their devices.
With SFC service enabled in 5GS, it becomes possible to provision V2X services with consistent carrier grade performance in 5GS.

## Slide 4: Challenges of supporting SFs/SFC outside of 5GS
Potential interoperability issues:
  due to lack of consolidated network resource management of service chaining between 5GS and N6-LAN even within the mobile network of the same network operator, which results in uncoordinated and inefficient service function path settings for routing the E2E service with desired service functions;
Unexpected Latency in every hop of N6-LAN:
  due to lose control over the chained service functions in N6-LAN, which results in difficulties to achieve the latency requirement for some services targeting at ultra-reliable low-latency. For example, interactive AR/VR gaming, remote control of UAV, Audio-Visual Service Production, industrial automation, critical medical applications, self-driving vehicles, etc.
Compromised service experiences to the users requiring same service functions:
  upon UE moves between HPLMN and VPLMN, or between HPLMN and NPN.
Limitation on provisioning versatile vertical services:
  in different networks and services deployment scenarios and in fulfilling required KPIs for the services.
Missing consideration of many advanced features in 5G network
  network slicing, network function virtualization, non-public network, and edge computing, etc.
  Enabling support of SFC in 5GS is foreseen as a promising enhancement to tackle the challenges in 5GS. It is proposed to study the use cases and potential service requirements of service function chaining service in 5GS.
Notes:   The lack of a standards developing organization with oversight for N6-LANs has resulted in a wide range of N6-LAN architectural approaches even within the same mobile network operator group. It has led to a broad vendor solution mix, making the management, maintenance, and evolution of the N6-LAN operationally challenging.

## Slide 5: Objectives of FS_SFCin5GS
The aim of this work is to study use cases and potential new service requirements in support of service function chaining for value-added services in 5G system, including:
Use cases and service requirements to enable service function chaining service in 5G system provided by network operators to third parties related to:
  Support of on-demand service function chaining for value-added services with the following aspects:
    provide definition of supported service functions and service function paths;
    configure and control service functions and create, configure, and control service function paths in 5GS per application or per user(s) of an application;
    handle and consolidate service functions chaining in 5GS for service functions of value-added services, e.g. provided by 5GS only or both of 5GS and 3rd parties.
  Support of the coexistence of traffic with and without service function chaining.
  Support of continuing same service function chaining service as UE moves between networks with local breakout, e.g. PLMN and NPN.
  Gap analysis between the identified service requirements and existing 5GS service requirements or functionalities.
Note: the gap analysis takes into account previous work related to stage 1 services requirements on SFC already developed in other SDOs (e.g. IETF RFC 7665, IETF RFC 8300, IETF RFC 8459, ITU-T Y.2242

## Slide 6: BACKUP Slide

## Slide 7: Concept of Service Function Chaining
The examples of service functions include, but are not limited to the following: firewall functions, NAT, URL filter, Lawful inspection (LI), deep packet inspection (DPI), IP tunnel endpoints, Packet classifiers, application detection and control (ADC), TCP proxies, load balancers, transcoders, application policy control, protocol and video optimization, etc.
ITU-T-Y.Sup41: Service chaining service (SCS) provides a mechanism to dynamically build service function chains (SFCs) and then make incoming packets forward through the SFC. With these dynamics, the SFC can rapidly and easily be generated and modified according to the service features carrying in packets.

## Slide 8: Service Function Chaining Use Cases considered in 3GPP
(S)Gi-LAN is one the use case of service function chaining, which is the middle box provided by a wide variety of vendors and out of 3GPP scope, used to differentiate and monetize services between the mobile network and the packet data network.
However, (S)Gi-LAN in EPS is currently considered out of scope of 3GPP as indicated in TS22.101. As such, the policy control of (S)Gi-LAN needs to be coordinated with the existing traffic steering policy in EPS.
The same assumption applies to N6-LAN in 5G context. The fragmentation of the network functionalities result in many challenges in 5G system.
Ref: 3GPP TR 22.808 V14.1.0

## Slide 9: Challenges of supporting SFs/SFC outside of 5GS
Potential interoperability issues:
  due to lack of consolidated network resource management of service chaining between 5GS and N6-LAN even within the mobile network of the same network operator, which results in uncoordinated and inefficient service function path settings for routing the E2E service with desired service functions;
Unexpected Latency in every hop of N6-LAN:
  due to lose control over the chained service functions in N6-LAN, which results in difficulties to achieve the latency requirement for some services targeting at ultra-reliable low-latency. For example, interactive AR/VR gaming, remote control of UAV, Audio-Visual Service Production, industrial automation, critical medical applications, self-driving vehicles, etc.
Compromised service experiences to the users requiring same service functions:
  upon UE moves between HPLMN and VPLMN, or between HPLMN and NPN.
Limitation on provisioning versatile vertical services:
  in different networks and services deployment scenarios and in fulfilling required KPIs for the services.
Missing consideration of many advanced features in 5G network
  network slicing, network function virtualization, non-public network, and edge computing, etc.
Notes:   The lack of a standards developing organization with oversight for N6-LANs has resulted in a wide range of N6-LAN architectural approaches even within the same mobile network operator group. It has led to a broad vendor solution mix, making the management, maintenance, and evolution of the N6-LAN operationally challenging.

## Slide 10: Other SDOs Activities
ITU-T Y.2242 considers the cases when relevant network functions are virtualized and provides Recommendations to support service function chaining in mobile networks.
IETF RFC 7665 and IETF RFC 8300 introduce service function chaining architecture with a chain orchestrator and provide methods of coordinating dynamic service function chaining in mobile networks.
In summary,
  5GS support to consolidate service functions and service function chaining can provide flexibility to manage required service functions into one network instance.
  The service deployment and configuration can be greatly simplified and at scale. As such, it is foreseen as a promising enhancement to tackle the aforementioned challenges in 5GS.

## Slide 11: Example of Use Cases (1/3)
For the use case of streaming video service, different content providers may need different service functions for video optimization and security functions based on users subscription, network service subscription, etc.
With the control and management of the SFCs in 3GPP network, the network operators can provision the service function chaining service by including value added services and security features to the content service providers.

## Slide 12: Example of Use Cases (2/3)
In an AR/VR production use case in NPN, different broadcasters may need different service functions for their on-site devices, e.g. camera and mics.
Currently, each broadcasters need to manually configure its N6-LAN or provide the configuration of N6-LAN to NPN provider as part of service agreement.
With service chaining service enabled in a NPN, the network provider can exposure service function chaining service to third parties and allow them to configure required service function paths for their devices.

## Slide 13: Example of Use Cases (3/3)
In a 3GPP V2X use case, when a vehicle moves in its HPLMN or across different roaming networks, it is beneficial that the same service functions, e.g. TCP proxies, transcoders, firewall, etc., are provided, configured, and managed by the mobile networks in order to ensure the provisioning of required KPIs and security functions with the consistent carrier grade performance in 5GS.
For example, in TR22.886 clause 5.27.6: Support of automated driving in multi-PLMN environments.
However, in case of roaming, current eFMSS supports only home routed traffic steering.

## Slide 14: Considerations on existing 3GPP requirements
Some existing requirements related to FMSS/eFMSS are captured in TS 22.101, addressing only part of the target use cases and functionalities, e.g.:
  support to define and modify traffic steering policies that are used to steer traffic in (S)Gi-LAN (considered out of scope) containing operator or 3rd party service functions
  The 3GPP Core Network shall be able to define different traffic steering policies for a user’s traffic on a per session basis (e.g. for applying parental control, anti-malware, DDoS protection, video optimization).
  The 3GPP Core Network defines traffic steering policies based on one or more pieces of information such as: network operator’s policies; user subscription; application characteristics such as: application type, protocol, target address name (URL) and application provider, etc.
  In case of roaming, the HPLMN shall be able to apply traffic steering policies for home routed traffic.
New use cases, requirements and gaps should be studied, e.g. considering:
  Service functions in 5G system
  Network slicing, edge computing, non-public network, and network functions virtualization
  Service continuity and roaming support

## Slide 15: Reference: 3GPP TS22.101 clause 30-FMSS
3GPP 22.101, FMSS, the following requirements apply:
The 3GPP Core Network shall be able to define and modify traffic steering policies that are used to steer traffic in (S)Gi-LAN containing operator or 3rd party service functions e.g. to improve e.g. the user’s QoE, apply the bandwidth limitation and provide valued added services.
Traffic steering policy shall be able to distinguish between upstream and downstream traffic.
The 3GPP Core Network shall be able to define different traffic steering policies for a user’s traffic on a per session basis (e.g. for applying parental control, anti-malware, DDoS protection, video optimization).
The 3GPP Core Network defines traffic steering policies based on one or more pieces of information such as:
  network operator’s policies
  user subscription (e.g. user’s priority, the status of optional subscriber services from the subscription data, based on service provider used, subscribed QoS)
  user's current RAT
  the network (RAN and CN) load status
  application characteristics such as: application type (video, web browsing, IM, etc), application protocol ( HTTP, P2P, etc), target address name (URL) and application provider (My tube, etc)
  Time
  UE location
  information (e.g. APN) of the destination network (i.e. a PDN or an internal IP network) of traffic flow
  In case of roaming, the HPLMN shall be able to apply traffic steering policies for home routed traffic.
Note: Traffic steering policies for local breakout is not specified.