## Slide 1: Disscussion paper of Addition of requirements on Data Integrity in 5GS
China Unicom
weiqun5@chinaunicom.cn

## Slide 2: Motivation
The requirement of data integrity in verticals
  Data collected from IoT devices/sensors is mostly sent to service platform directly at the present, e.g. position data in logistics services.
  However IoT data for finance related services may be very crucial. Hence verticals such as supply chain finance and insurance have strict requirements for data integrity, e.g. environment data(e.g. temperature and windspeed) for agricultural insurance and warehouse data (e.g. number and weight of goods) for inventory financing. Those services require to data exchange from UE to the third party SP（service provider).
  Gap between 3GPP and requirement of verticals
  While data integrity methods are provided within the 3GPP network, there are gaps in ensuring end-to-end data integrity service from a UE to 3rd party Service Providers using the 3GPP Network.
  Moreover, data integrity protection is important for data verification services(e.g. an insurance claim)
  In any case, all kinds of IoT UEs and SPs of the enterprises above are connected to MNO’s networks, especially the more extensive cross industry SP business model.
  MNOs need to get ready to provide a mechanism to realize data integrity service for the community in the interest alliance.
3GPP System
3GPP UE
Data integrity and Encryption in 3GPP
Data integrity from UE to SPs
UPF
3rd party SPs
Cross industry
WID Study Area

## Slide 3: What SA1 can do?
Solution | UE(App) | UE(Module) | UE(SIM) | SP | 3GPP
 |  |  |  |  | 
 |  |  |  |  | 
 |  |  |  |  | 
 |  |  |  |  | 
A data integrity protection service which can be used as a 3GPP capability.
A data integrity protection service which is provided by operators and cover lots of UEs and SPs.
A data integrity protection service which is end-to-end from UEs and the SPs.
Many SPs may have realized data integrity services in several ways. That’s depends on SP themselves, however the data protected of SP private data integrity cannot be fully trusted by other SPs. In other words, it is not easy to achieve a wide coverage of UEs and SPs.
3GPP
Data Integrity Service solutions

## Slide 4
Cold chain logistics
During the transportation of vaccines/drugs, vaccines/drugs containers in cold chain logistics may be equipped with IoT sensors which send data to the vehicles. Those vehicles connect to a SP platform by 3GPP network for data gathering and processing. Monitoring is very critical since the products in the container may exceptionally sensitive to changes in pH, temperature and even light conditions.
Ensuring the trustiness of the collected environment data in each container/sensor is necessary to the service in order to guarantee vaccine/drug activity.
In this use case, the requirements are to achieve the data integrity for the environment data from IoT sensors to the SP.
Moreover, If problems arose, SP (hospital or vaccine company) would claim to trace and verify all the environment data during transportation afterwards.
Example Use Case

## Slide 5: Data exchange between UE and SP
Third parity service providers
IoT UE
IoT UE
Data+data signature
Data+data signature
Verify Data integrity
3GPP System
UE access network
Data Generation
Integrity Verification
Example of Logistics
IoT UE=Vehicles belonging to logistics companies that deliver vaccines and medicines.
Data+data signature=application data(temperature in the container) and related digital signature (IoT UE source) .
NOTE: Application data and data signature is only transmitted .3GPP would not store or process any of this part of data. (3GPP does not want to repeat the work of OPC UA)
Application collected data(temperature in the container)+hash algorithm+UE private key->Data signature
Hospital
Logistics
UE : Application data(temperature in the container)
+Data signature
The red circle is the way of work of logistics company and UE in the application layer. These UE are usually the terminals of the Internet of things, which is the scope of our discussion.

## Slide 6: Operator's Role
Third parity service providers
IoT UE
IoT UE
Data+data signature
Data+data signature
Verify Data integrity
UE access network
Data Generation
Integrity Verification
MNOs play the trusted party
CR part 1 : Subject to regulatory requirements and based on operator policy, the 5G system shall provide a mechanism to support integrity protection service for data exchange between a UE and an application server offered by a third-party service provider.
3. Third parity service providers’ Problem
When SPs are cross industry, for example hospital and Logistics. UE and the application server are the two parties that want to communicate. But in that case the application server is not offered by a trusted third party, as the trusted third party is not one of the end-points in the communication. MNO plays the role of trusted third party, as it is trusted by both the UE and the application server.
Hospital
Logistics
3GPP System

## Slide 7: How to play
Third parity service providers
IoT UE
IoT UE
Data+data signature
Data+data signature
Verify Data integrity
Gap
UE access network
Data Generation
Integrity Verification
One way to achieve
4. Verify the integrity
Logisics company requires to verify the data in ” Data+data signature” has not be tampered.
  Data+data signature” is transmitted via 3GPP system.
  IoT UE belong to 3GPP. If ” Data+data signature” have no changes, the vaccine is correctly transported.
CR part2: Subject to regional or national regulatory requirements and based on operator policy, a 5G system shall provide suitable mechanisms to allow a UE, third party service provider application servers, each to verify the integrity of the data exchange between a UE and application servers.
Hospital
Logistics
3GPP System

## Slide 8: How MNOs help
Third parity service providers
IoT UE
IoT UE
Data+data signature
Data+data signature
Verify Data integrity
Obtain UE Public key
UE’s public Key
3GPP System
UE access network
Data Generation
Integrity Verification
3GPP can provide data integrity verification of multiple SPs of one UE
5. 3GPP network：have “UE’s public Key”，and the “banding information” of the UE identifier and other necessary metadata for integrity verification 。
6. Obtain UE Public key: The Third parity service providers could
  obtain “UE’s public Key” from the 3GPP system.
  verify the “Data+data signature” by using “UE Public key”.
UE’s public Key
banding information
CR part2: Subject to regional or national regulatory requirements and based on operator policy, a 5G system shall provide suitable mechanisms to allow a UE, third party service provider application servers, each to verify the integrity of the data exchange between a UE and application servers.
Hospital
Logistics

## Slide 9: Service Flow
7. Hospital requires to verity the data in ” Data+data signature” has not be tampered.
  Repeat procedure 5-6
  The vaccine transportation data in hospital may obtain from logistics company.
  The vaccine transportation data in hospital may obtain from IoT UE directly.
Third parity service providers
IoT UE
IoT UE
Data+data signature
Data+data signature
Verify Data integrity
Obtain UE Public key
3GPP System
UE access network
Data Generation
Integrity Verification
What 3GPP do
UE’s public Key
banding information
CR part2: Subject to regional or national regulatory requirements and based on operator policy, a 5G system shall provide suitable mechanisms to allow a UE, third party service provider application servers, each to verify the integrity of the data exchange between a UE and application servers.
Hospital
Logistics

## Slide 10: Real time and non real time
Real-time Verification
Third parity service providers
Data+data signature
Verify Data integrity
Obtain UE Public key
3GPP
System
UE access network
Data Generation
Integrity Verification
UE’s public Key
banding information
Hospital
Logistics
Third parity service providers
IoT UE
Data+data signature
Verify Data integrity
Obtain UE Public key
3GPP
System
UE access network
Data Generation
Integrity Verification
UE’s public Key
banding information
Hospital
Logistics
Non-real-time Verification
Hospital
Hospital
PGP
Data+data signature
IoT UE
Data collector
Data verifier
Data collector
Data verifier
Data collector
Data verifier
Data verifier
The communication is real-time, but the service can be non real-time
Data+data signature

## Slide 11: Non real-time Service
real-time integrity protection service
After the data is transferred from IoT UE to SP, the SP verifies the data integrity, if the data haven’t been changed, and then stores it in SP. (this kind of SP can be called the Data collector)
If the upstream SP wants to obtain data, it needs to have direct interaction with UE. (The upstream SP is also the Data collector)
Logistics’s SPs and UE usually belong to real-time integrity protection.(application layer data process)
Non real-time integrity protection service
After the data is transferred from IoT UE to SP, the SP verifies the data integrity, if the data haven’t been changed, and then stores it in SP.
The upstream SP can obtain the data of SP (Data collector) through PGP technology. The upstream SP do not need to be Data collector, but Data verifier.
The data trust between SP and upstream SP depends on paper contract, in PGP technology without 3GPP.
The data trust between SP and upstream SP depends on PGP technology with 3GPP by using the public key shared by 3GPP system. This part belongs to non real time integrity protection service. However, 3GPP does not participate in data preservation.
The communication is real-time, but the service can be non real-time

## Slide 12: Non real-time Service
Typical use cases
The post audit of insurance industry usually takes place within 1-2 weeks. For example, after the occurrence of agricultural disasters, the insurance industry can query whether the data reported by IOT equipment is true.
The collection of drug transportation data in logistics, continues in the process of transportation. When the logistics equipment arrives at the location(hospital), SP(hospital) will trigger the verification of data.
Generally speaking, insurance companies and hospitals do not have the ability to collect UE data on a large scale.

## Slide 13: Requirement Gap Analysis
AKMA
  TS 33.535 specifies the security features and mechanisms to support authentication and key management aspects for applications based on subscription credential(s) in 5G system.
  GAP1: AKMA is an authentication mechanism.
  GAP2: The keys used in AKMA would be refreshed.
Study on Data Integrity in 5GS
  This WID is designed to provide an end-to-end IoT data integrity from 3GPP UE to a third party SP based on 3GPP system..
  NOTE: Only 3GPP UE is considered in this study.
GBA
  TS 33.220 describes the security features and mechanisms to bootstrap authentication and key agreement for application security.
  GAP1:GBA provide an authentication mechanism.
  GAP2: The keys used in GBA would be refreshed.

## Slide 14: Thank you