## Slide 1: Title: New WID proposal - Ad hoc Group Communication (AHGC) support in Mission Critical Services
Agenda Item: 4
Source: Samsung, FirstNet
Document for: Discussion

## Slide 2: Background
An ad hoc group can be formed extemporaneously with a random set of MCX Users by an authorized MCX User. Unlike user regroup grouped, an ad hoc group does not persist until canceled: it ceases to exist when the communication concludes.
Initially (Rel-13 – Rel-14) it was decided not to include ad hoc groups in MCX Services.
Since then, interest has grown to specify this.
There are no corresponding requirements in stage 1.

## Slide 3: Motivation
Ad hoc group call is a feature found in commercial PTT systems such as those based on OMA-PoC.
The feature has proven useful in the field, though not yet standardized or supported by the MCX service standard.
Operation of this feature is well understood (so there is no need to study case studies in SA1.)

## Slide 4: Proposal
Introduce the concept of MCX Service Ad hoc Group Communication, which is the same as MCX Service Group Communication except that the ad hoc group
  Does not exist until spontaneously created.
  Ceases to exist when the communication terminates.
  Does not support ‘persistent state’ communication, e.g. emergency state.
These requirements are added as a new 6.X clause to 22.280
  Additionally four other requirements are added throughout.
  The changes to the specification as a whole are modest.
A WID (S1-213129) + CR (S1-213105) are provided to this meeting.