## Slide 1: Proposal on Human readable name for NW slices
Qualcomm
3GPP TSG-SA1 Meeting #95e S1-213161
E-Meeting, 23 August –2 September 2021

## Slide 2: Use Case 1
Large business park with multiple warehouses each belonging to different business enterprises
Each warehouse has its own PNI-NPN (from the same PLMN)
Each slice is isolated from each other and gives access to a network belonging to a specific enterprise (PNI-NPN)
There is overlapping between NPNs/Slices
Problem
  How does the user know to which S-NSSAI is connected at a certain time?
One PLMN, two NPNs, two Isolated Slices
NPN-1
NPN-2
UE
RAN-1
RAN-2
5GC
S-NSSAI-1
S-NSSAI-2
Which S-NSSAI is the user connected to?

## Slide 3: Use Case 2
One PLMN (or PNI-NPN)
Each enterprise has its own S-NSSAI
Slices are available over the entire PLMN
Each slice (S-NSSAI) is isolated from each other and gives access to services belonging to a specific enterprise
Problem
  How does the user know to which S-NSSAI is connected at a given time?
One PLMN (or NPN), two isolated slices
UE
RAN
5GC
S-NSSAI-1
S-NSSAI-2
Which S-NSSAI is the user connected to?

## Slide 4: Human readable name per S-NSSAI - Service Flow
Serving PLMN or NPN
  Provides NSSAI(s) to the UE together with associated human readable name(s), e.g. during UE registration
UE
  UE displays the human readable name per S-NSSAI in the user interface (device screen) in addition to PLMN/NPN Network name, if received
  UE may also display the human readable name of a S-NSSAI for which a data session for the associated application can not be established

## Slide 5: Human readable name per S-NSSAI - Examples
Examples of User’s display
OPERATOR A
Warehouse A
App1
App2
App3
Derived from PLMN-id
Derived from Allowed S-NSSAI name(s)
OPERATOR A
Warehouse B
App1
App2
App3
Derived from PLMN-id
Derived from Allowed S-NSSAI name(s)
Move to new NW/Slice
Access to Warehouse A not possible
Derived from not-Allowed S-NSSAI name(s)
App2
See another example in next slide…

## Slide 6: Human readable name per S-NSSAI - Examples
Examples of User’s display – Cont.
OPERATOR A
Warehouse B
App1
App2
App3
Example#2: when user presses e.g. App2 and UE tries to establish PDU session to the associated S-NSSAI, if UE knows that is not allowed UI can pop up a message indicating the human readable name of the non-allowed S-NSSAI
App related to Warehouse A not allowed here

## Slide 7: Existing requirements and gaps
Existing requirements
22.261 includes a requirement on broadcasting HRNN for NPNs (sec.6.25):
The 5G system may broadcast a human readable network name that a UE may display for manual selection of a non-public network.
There are also other reqs on displaying PLMN network name, in 22.101 and 22.042
  Including different mechanisms to derive NW name, e.g. broadcast, USIM/UE based, NITZ
Gap: existing requirements do not cover the ability to associate human readable names to specific NW slices, allowed or not allowed for a certain UE

## Slide 8: Proposal for SA1
Add a new requirement, part of NW slice requirements in 22.261 (sec. 6.1), i.e.
The 5G system shall support mechanisms for the NW to provide UEs with human readable name(s) associated to allowed/not allowed NSSAI(s), to be displayed to the user
Procedurally, the change can be made under Rel-18 EASNS (cat. B/C CR)
See corresponding CR in S1-213162, submitted to S1-95e
Open to discus other options, e.g. TEI-18 or mini-WID
For S1 discussion & approval