## Slide 1
China Telecom
Minimization of Service Interruption during Core Network Failure
Motivations, Use Cases and Proposal

## Slide 2
  Motivations (1/2)
The continuity of the 5G CN service is critical, because the number of the users that are impacted by the CN is large. For example, the number of users controlled by an AMF set could be millions in some countries. Once the 5G CN service is failed, the communication for millions of users would be interrupted.
To enhance the network service continuity, some studies have been made in history. For example:
work item CNO:
  enhance the overload control in the CN of 4G and 3G, etc;
work item LOLC:
  overload control mechanisms for service based interfaces;
work item MINT:
  the mechanism only dealing with 5G RAN failure.
However, for the scenarios with 5G CN failure, there are still cases that the current requirements could not cover.

## Slide 3
  Motivations (2/2)
Network sharing is an important part of 3GPP systems. In TS 23.501 R15, the 5G Multi Operator Core Network (5G MOCN) network sharing architecture is supported, in which only the RAN is shared in 5G System. Operators with 5G MOCN architecture could utilize the cooperation in network sharing to minimize communication service interruption. For example, when a network cannot provide communication service to its users due to CN failure, its users may be switched to one of the cooperative operators serving as the backup CN. Thus, 5G MOCN can be considered as an example scenario to study minimizing service interruption during the failure of 5G CN.

## Slide 4
  Use Cases
Use case#1 CN failure due to failed network control
Failed upgrade of NF/NE(s), computer virus, software bugs, incorrect network configurations or malfunctions may cause abnormal behavior of the CN network and put the entire network out of service. Many operators have reported network service outage due to the above problems in recent years.
Use case#2 CN failure due to natural disasters
Natural disasters such as storms, floods and fires may lead to extreme and sudden damage to CN network NF/NE(s) in a particular region. Such events have led to lots of network service disruptions in the past few years.
For example:
In the 5G MOCN scenario, when a natural disaster (e.g. fire) happens in Location A, the CN of Operator A is severely damaged and unable to serve its users (shown in red). Its users may be switched to the CN of one of its cooperative operators (e.g. Operator B in Location B).
Meanwhile, to minimize the impact to the home users of Operator B, it might be possible that only part of the users or services are switched.

## Slide 5
  Proposal
The aim of this study is to gather and analyse scenarios of 5G CN failure and derive potential service requirements out of these scenarios. Potential aspects to be addressed to derive relevant potential service requirements include e.g.:
The scenarios, scales or causes of interruption of communication service;
Allowing impacted users to be authorized to access some essential service (e.g. voice, SMS) of the functioning 5G CN, while not affecting the service provided to its home users;
Other aspects, including security and privacy requirements;
Gap analysis between the identified requirements and what is already defined by existing 3GPP requirements.
This study considers both the MOCN network sharing and non-MOCN scenarios. In this study, the scope is limited to the case during 5G CN failure.

## Slide 6
THANKS
感 谢 聆 听