## Slide 1: Discussion on UE-Network Coordinated AI/ML service OPPO
3GPP SA WG1 #97-e
Electronic Meeting, 14 – 24 Feb. 2022
S1-220038

## Slide 2: Background
R18 SA1 study on AMMT identify the requirements for AI/ML model transfer on 5GS regards 5GS as a channel to transfer data about AI/ML, e.g. very high data rate is required for model distribution and device-NW split inference/Federated Learning. However, some of further work needs to be studied in R19:
  As the AI/ML model transfer for device-NW coordinated AI/ML operations often requires very high data rate, the 5G hotspot coverage and UE power consumption become a challenging problem.
  Fully applying the device-side AI resource to the device-NW coordinated AI/ML operations (e.g. D2D for distributed learning) was not well considered.
This study aims at solving the above problems by introducing following requirements:
- AI/ML model transfer in 5G hotspot with device route planning
- Distributed AI training/inference with D2D enhancement
- Charging, security, privacy of above objectives

## Slide 3: AI/ML model transfer in 5G hotspot with device route planning – Description
Device-side AI operation is needed in many scenarios. High data rate connection becomes precondition (e.g. for AI model downloading, AI training with NW) for 5G devices to finish some AI/ML task, as shown in Rel-18 FS_AMMT KPI.
Ultra-high data rate (via high-order MIMO/mmWave) is a valuable resource for 5G operators and UEs, but has not fully utilized because it only covers hotspot or LOS beam directions.
Some AI devices (Robots, Drones, Smart cars (also a moving smart home/office during a self-driving travel)) can autonomously move to the hotspot/LOS beam to access the ultra-high data rate for AI services (AI/ML model downloading, Split inference/training) with AI-based route planning, based on the predicted achievable data rate throughout the unvisited area.
“To Go or Not to Go: On Energy-Aware and Communication-Aware Robotic Operation”, IEEE TRANSACTIONS ON CONTROL OF NETWORK SYSTEMS, VOL. 1, NO. 3, SEPTEMBER 2014

## Slide 4: AI/ML model transfer in 5G hotspot with device route planning – Gap Analysis
However R17/R18 5GS cannot support the device route planning for hotspot access because the necessary information is not exchanged between 5G network and device, e.g., the information 5G NW obtains from network planning or statistic analytics on experienced QoS of other devices.
The gap is analyzed below:
Potential functions enabled by SA2 R18 SID on “5G System Support for AI/ML-based Services” | Requirements of device route planning for 5G hotspot access
NW plans the route for device (assuming having full knowledge for the route planning). | Device plans the route itself (NW may not have professional knowledge for the vertical application).
NW predicts a UE’s QoS consistency along a route reported by the UE (assuming UE has planned the route). | Mobile UEs needs to predict the hotspot locations /beam directions throughout the unvisited area (UE cannot plan the route without the apriori information).
NW predicts a UE’s QoS consistency without considering the real wireless channel conditions (assuming UE has planned the route). | Mobile UEs needs to predict the achievable data rate based on channel conditions, e.g. channel fading, blockage.
  SID Objective:
  AI/ML model transfer in 5G hotspot with device route planning, in which UEs can predict the achievable data rate in real channel conditions throughout the unvisited area, e.g., with NW-assisted information (RAN/CN/Combined) exposure implying device or 3rd party how to plan a route via hotspot locations/the direction the gNB beam can cover, or by NWdevice split AI route planning.
    Note: It is not required to disclose sensitive information about the network infrastructure to end users.

## Slide 5: Distributed AI training/inference with D2D enhancement
Potential scenarios
For Distributed Learning, controlled by network, each device uses the localized data while transfer the intermediate data to other nodes in order to train a big model,
For Distributed Inference, the device, holding valuable input data but with low power/computation resource, may calculate the first few layers of a AI model and offload the intermedia data to another device using D2D link for the finial inference result.
For Federated Learning, Using D2D can involve devices outside 5G hotspot for distributed AI training/inference, partly offload computation to neighboring device, and improve the training accuracy/generalization and save device power.
  SID Objective:
    Distributed AI training/inference with D2D enhancement, which anticipate the KPI and discovery enhancement of Device to Device communication for distributed learning/inference among multiple end users and network node(s), e.g., KPI values for AI/ML model/data transfer different from that in uplink and downlink and extending sidelink information exposure supporting cooperative AI/ML
Potential requirement to 5GS
KPI enh.
(E.g., different KPI requirements between Uu and sidelink)
Discovery enh. taking multiple factors into account
(e.g. application, model, user consent)
Other aspects such as charging and security

## Slide 6: Back slide

## Slide 7: Distributed AI training/inference with D2D enhancement - Example use cases
UC-1: Hybrid splitting architecture based on model parallelism with the participation of UEs and networks
UC-2: Factory service flow (Intermediate data can be changed between two robots and the robot with low battery can continue working)
UC-1: By using the model parallelism, the transmission of intermediate training results between different nodes can realize data sharing between UEs under the premise of ensuring privacy, expand the training set of the model, and improve the training efficiency.
UC-2: When the battery level reaches a certain value, a part of the AI/ML model can be transferred to another robot by splitting the AI/ML model