## Slide 1
S1-220008, 3GPP TSG SA1#97e, 14 - 24 February 2022, e-meeting
Motivation of supporting computing aware network
China Mobile

## Slide 2: Motivation of computing aware network
Provide better end-to-end service experience
  Now network consider from UE to N6, and have very little view on the rest, the end-to-end service experience is cut into two part, with static way to do the global optimization
More efficiency in utilizing existing computation capability
  For different computation capability providers, expose computation related information to each other and bring collaborated service.
Lower energy consumption on UEs
  For high computation demand APP or service, help UE in offloading computation task for lower energy consumption and lower processing time
Computing aware network, which provides the capability to be aware of computation capability within network(e.g. computation capability on the edge) and those computation capabilities belong to 3rd party, so that 5GS can consider both network mesh and service endpoints to optimize network path, offload computing task to available computing resource, and guarantee the quality of service (QoS) for end users.
What is the computing referring to?
Computation capability on edge computing resources, data centers, etc.
Who is the customer?
Service which has high computation capability demand, such as XR, metaverse, V2X, cloud gaming, etc.

## Slide 3: Use case 1
3rd party give a list of target servers (blue ones)
network have no information about the allocation of other servers (grey ones)
Network can only provide the best path according to allocation of the servers which are provided
This may not be the global best as neither 3rd party knows the network mesh nor network knows allocation of 3rd party servers.
Provide the best network path
Provide the best network path + best service endpoint
The original network path is the red ones, and the server suddenly broke down.
UPF knows nothing about the server’s status, AF need to tell the 5GC about this fault, provide other server’s allocation, and network find the path then, which cause much more time
If 3rd party could expose some status information to 5GS, the re-path will be much more quicker

## Slide 4: Use case 2: Computing load sharing from terminals to network
Some service（e.g. AR, VR） may need UEs lot of computing resource and storage, so UE may need to share some of the computing load or storage through 5GS to other computing resource, to achieve lower energy consumption and processing latency.
5GS
Load share
Load distribute
Load share

## Slide 5: Objectives:
Study use cases related to leverage 5GS to provide computing aware service and potential requirements, e.g.
  Quantify computing resource (including 5GS internal computing resource and external computing resource) and computing requirements.
  Authentication and registration of 3rd party computing resource (data centre of cloud service providers, computing capability in UE, edge computing service providers, computing capability in customer-premise networks, etc).
  Discovery and utilization of computing resources based on service requirements.
  Communication requirements to achieve optimal computing resource usage.
  Potential enhancement on QoS when considering the computation capability need for services which have high demand of computation (e.g. new parameter in describing computation capability need)
  Interactions between different computing capability providers (e.g. data centre, edge data networks, personal GPU, etc.), whether and how the 5GS can enable users of the compute service to support efficient selection of computing capabilities inside and outside of 5GS.
  Computing load sharing to lower the energy consumption and lower processing time (e.g. from UEs to network).
Identify KPIs regarding computing capability including latency (include network latency and processing latency), reliability, etc.
Other aspects include security, charging and privacy

## Slide 6
Thank you!