## Slide 1
China Telecom
Study on Enhancement of relay communication for eMBB
3GPP SA WG1 Meeting #97e
Electronic Meeting, 14 – 24 Feb 2022
S1-220080

## Slide 2
  Motivations
Relays have been introduced for IoT devices, vertical scenarios and public safety use cases in the earlier releases. Relay network could be enhanced for eMBB scenarios under operator control.
Enhanced relay network for eMBB
Service requirements have been introduced of having one-hop and multi-hop relays, which are focusing on IoT and low latency cases. This might be not enough for the need of reliable eMBB services.
High frequency becomes widely used. With the same deployment of base stations for lower frequency, there will be white spots in some areas. Cellular coverage could be extended by relays to cover these white spots.
Relay UE is easy to install than IAB nodes, which needs radio cell planning.
Nomadic relays could be placed at some areas, e.g. city center. They could be placed somewhere with continuous power supply so that power supply won’t be considered during relay selection.
Charging and security
Relay owners could benefit from incentives scheme offered by operators with enough charging information.
Relay network should be secured so that people would have confidence in sharing their UEs as relays and using others’ UEs as relays for better user experience.

## Slide 3
  Example Use Cases
Extended coverage with multi-path relay
The higher frequency we used, the coverage would be smaller. If we don’t have full coverage, user might get into the area that has no coverage as shown in the figure on the right.
If there are two multi-path relays within the coverage range of two gNBs, user could connect to the relays which are relatively closer to obtain cellular connection.
with nomadic relay UE
Nomadic relay UE has continuous power supply and is relatively stationary than other relay UE that might be moving all the time. For example, the shop owner sets a UE at the shop as relay UE for other passerby and customers. Nomadic relay UE could have higher priority when selecting relay, because it won’t have power shortage problem as other relay UEs do. Moreover, it is often stationary for a long period of time, so it can provide stable connection for the remote UE.
Road
Nomadic Relay UE
Coffee Shop
gNB

## Slide 4
  Proposed objectives and Related Work Items
The objectives of this study are to define:
Use cases and corresponding requirements, including:
  Multi-path multi-relay connection,
  Nomadic relay UE, e.g. relay UE selection, authorization, etc.,
Other aspects, including charging and security,
Gap between the identified requirements for the relay enhancement and the existing requirements for 5G system.
Related Work Items:
New Services and Markets Technology Enablers (SMARTER)
Enhanced Relays for Energy Efficiency and Extensive Coverage (REFEC)

## Slide 5
Pre-conditions:
Some of the UEs have subscription with the operator to act as relay and they would get reward according to the data being relayed or the time they act as relay.
John has subscription with the operator to use other UEs as relays.
John is at the Christmas market, where he cannot have direct network connection due to the heavy load of the gNB nearby.
Service Flows:
John’s phone has poor connection and would like to share videos and photos with his family.
John turns on his “finding relays” function on his phone.
John finds the available relay UEs nearby.
John’s phone build connection with the available gNB through two paths, including one path with one-hop relay and the other path with multi-hop relays.
Based on the situation of the current connections (e.g. congestion, bad quality), network could dynamically schedule the traffic flows on both paths.
  Detailed Example Use Case
Post-conditions:
John can share videos and photos with his family. John could also make video call with his family.
Owners of the involving relays could get reward at the end of the month.
Potential requirements:
Dynamic traffic scheduling
Charing related
Notes: At the city center or busy area during special events (e.g. Christmas market), the cellular coverage would be poor. With different relays from multiple paths, user could get good coverage and could share videos that has good quality with his family.

## Slide 6
THANKS