## Slide 1
5G Enabled Open-SON.
Reliance Jio, Radisys.

## Slide 2: Issues of SON in 4G HetNet deployment.
Vendor specific SON Implementations.
SON solutions as independent node with proprietary interfaces, supporting either or both Non-Real Time (Non-RT) and Near-Real Time(Near-RT) SON functions, adds to cost and deployment complexity.
SON implementations today exist in Management and/or RAN entities but is tightly coupled with proprietary implementations and interfaces.
Lack of SON coordination across vendor solutions, leading to ping-pong effects and swinging phenomena.
Generally, Vendors are not open to integrate 3rd party solutions or the integration process is very expensive.
Even after integration, no assurance on overall KPIs of the Network, due to design constraints of involved parties.

## Slide 3: Issues of SON in 4G HetNet deployment. [Cont…]
Existing SON solutions are either reactive or proactive based on the available data.
Existing SON functions support proprietary limited analytics functionality to aid proactive decisions.
The input and output data from an Analytics entity for SON are still specific to proprietary implementation.

## Slide 4: Introduction of Analytics functionality in 5G.
NWDAF is introduced in 5GC to generate Analytics data from the CN perspective.
MDAS is introduced in Management entities to generate Analytics data using both RAN data and the CN analytics data from NWDAF. These analytics data can provide meaningful end-to-end network perspective.
MDAS can aid both Domain and Cross-Domain SON solutions.
“RAN data Collection” is being introduced within RAN to aid Near Real Time SON solutions. In this work, the Model training and Model Inference functionalities are still implementation specific. The Actor, which can be SON functionality, can exist collocated or independent of other analytics entities. Actor is again implementation specific.
The input and output data for the Analytics model is alone being standardized, which are necessary but not sufficient.

## Slide 5: Is 5G Analytics functionality solving the HetNet SON issues?.
Really not solving the Multi-vendor issue.
Off course, it may improve the Vendor specific SON solutions in silos, but not the SON coordination aspects across the Multi-vendor solutions.
Proprietary implementations and Proprietary interfaces can continue to play a critical role to hinder the smooth HetNet Deployments.

## Slide 6: Possible ways to resolve SON issues in HetNet.
Defining Non-RT SON functionality as part of Management entity (Using MDAS).
Defining Near-RT SON functionality as part of the gNB in extension of the RAN Data collection work.
Defining an Open interface between Management entity and the gNB to exchange the SON data and other management data.
Enhancing the Xn interface with standard behavior for SON coordination. [Also, F1, E1 and NG]
Either SON algorithms behavior needs to be defined or Deterministic KPI targets needs to be defined.
This avoids unnecessary additional deployments of multi vendor Management entities, Independent SON entities, reduces Complexities, cost and OPEX to the service provider.

## Slide 7
Thank You.