## Slide 1
Discussion on Sensing Scenarios and Use Case
3GPP TSG-SA WG1 Meeting #97e
S1-220108
Electronic Meeting, 14 – 24 Feb. 2022

## Slide 2: Scenario and Use Case
Main Services
Sensing-Assisted Communication
  Beam Management
  Smart Scheduling
  Mobility Management
  Sensing-assisted AI communication
Communication-Assisted Sensing
Vertical Applications
Smart Home, Room sensing
  Home monitoring: Presence detection, Proximity detection, Movement detection
  Home security: intruder detection
  Healthcare: health conditions of human beings, e.g., walk (gait), sleep, fall, breath, heart beats
  Interactive control: Motion sensing gaming, controlling smart devices
Smart Factory
Proposal: in Release 19 Sensing, the first priority is the indoor/local area scenarios, e.g. Smart Home/Factory etc., to identify the use cases where UEs or IoT devices are involved and their requirements.
  indoor/local area scenarios have high technical feasibility and its signal transmission is relatively more stable and simpler than outdoor area scenarios.

## Slide 3: Sensing Mode
Only UE involved
  Mode 1: Sidelink Sensing between UE1 and UE2
    => For indoor scenario, Mode 1 has benefit than Uu-interface sensing(Mode 3/4), since for indoor short-distance scenarios PC5-interface is more likely to have LoS paths than Uu-interface.
  Mode 2: monostatic radar (UE)
    => Need technical progress at physical layer, e.g. full-duplex, can be considered with lower priority
UE and gNB involved (bistatic radar)
  => Minimum impact on legacy RAN, can be considered with the highest priority
  Mode 3: Uu-interface Downlink Sensing
  Mode 4: Uu-interface Uplink Sensing
Only gNB involved
  Mode 5: bistatic radar between gNB1 and gNB2
  Mode 6: monostatic radar (gNB)
    Need technical progress at physical layer, e.g. full-duplex, but it seems to be easier than Mode 2 since gNB has better capability than UE, can be considered with lower priority
Note 1: Sensed objective can be within and out-of 3GPP network
Note 2: Both single link sensing and multiple link sensing are considered
Note 3: IoT as a special case of UE, is also involved in above modes
Proposal: in Release 19 Sensing, Mode 1/3/4 are first priority, and open to discuss other of these sensing modes including Uu and PC5 sensing, if needed.

## Slide 4: Summary
Proposal
Focus on the indoor/local area scenarios, e.g. Smart Home/Factory etc., to identify the use cases where UEs or IoT devices are involved and their requirements, considering that it has high technical feasibility and its signal transmission is relatively stable and simple.
Mode 1/3/4 are first priority, and open to discuss other of these sensing modes including Uu and PC5 sensing, if needed.
Mode 1: Sidelink Sensing between UE1 and UE2
Mode 2: monostatic radar (UE)
Mode 3: Uu-interface Downlink Sensing
Mode 4: Uu-interface Uplink Sensing
Mode 5: bistatic radar between gNB1 and gNB2
Mode 6: monostatic radar (gNB)

## Slide 5
Thanks!