## Slide 1: Usage of Non-3GPP Digital Terrestrial Broadcast Networks (DTT) for Multicast/Broadcast Services (MBS) in 5GS
S1-220168
Source: Saankhya Labs, Ligado Networks, Hewlett-Packard Enterprise, One Media 3.0, Fraunhofer IIS, CEWiT, Tejas Networks, IIT Bombay, IIT Kanpur, IIT Madras, IIT Hyderabad, IIT Kharagpur, Reliance Jio
3GPP SA Proposal

## Slide 2
Usage of Non-3GPP DTT within 5GS for MBS - Motivation
Non-3GPP Digital Terrestrial Broadcasting Technologies
  Purpose-built for optimum broadcast/multicast performance
  Large and Small Coverage Area Support
  Improved Mobility Support
  Multi Frequency as well as Single Frequency Networks
  High Spectral Efficiency - Higher Mod-Cod support like 4K-QAM (ATSC3)
Use Cases - Non-3GPP DTT Broadcasting Technologies
  Data Offload (Video/Audio and other Content)
    Offload of unicast sessions or MB session in NG-RAN to a MB session in non-3GPP DTT
    Reduced Congestion in Cellular Network
  Rural (Sparsely Populated Area) Coverage

## Slide 3
Usage of Non-3GPP DTT within 5GS for MBS - Motivation
Improved Resource Utilization across non-3GPP access (DTT) and 3GPP 5G NG-RAN
Compatible with existing DTT Spectrum rasters (6/7/8Mhz)
Mature Standards that have regulatory approval
New business opportunities in conjunction with 5GS
  ATSC3 Deployed in USA, Korea, DVB-T2 is deployed in 144 countries & ISDB-T in 24 countries
Coverage (service) continuity
  Service continuity to a user outside 3GPP NR coverage
Broadcast Capacity on-demand update as per traffic needs
Flexible capacity allocation through usage of non-3GPP DTT network
On-demand Coverage improvement for Broadcast mode delivery of OTT content/TV services

## Slide 4
Usage of Non-3GPP DTT within 5GS for MBS
TS 22.261 - Clause 6.3
  Support for both 3GPP (NR, E-UTRA…) and non-3GPP Access Technologies (WLAN, Wireline…)
  Selection of most appropriate 3GPP or non-3GPP access technology for a service
    For optimization and resource efficiency
  Allow more than one access technologies to be used simultaneously
    For one or more services active on a UE
TS 22.261 - Clause 6.13
  Support multicast/broadcast services
However TS 22.261 does not specify
  Usage of non-3GPP DTT for multicast/broadcast service in 5GS
Considering the advantages of using non-3GPP DTT for MBS it is requested to
  allow usage of non-3GPP DTT for MBS in 5GS through interworking of non-3GPP DTT with 5GS and update the specifications accordingly.

## Slide 5: Thanks