## Slide 1: Discussion on Live Migratable Services in the 5G System
China Telecom
3GPP SA WG1 Meeting #98e S1-221122
Electronic Meeting, 9 May – 19 May 2022

## Slide 2: Background
Live Migration is known as a Network Function Virtualization technology to save or restore a Virtual Machine in real-time. It usually saves the running status of the entire VM and quickly restores the VM to the original or even different hardware platforms. After recovery, the virtual machine continues to run smoothly while users will not notice any difference.
5G system is designed and implemented base on Service-Based Architecture which brings more flexibility and scalability. Indeed, live migration can be used for some specific communication services in 5G system.
When a group of UEs access to a local network which can not provide a specific communication service the UEs want, and the UEs must access to the service locally for low latency and service continuity, a bad QoE or even a network failure will occur. To overcome this difficulty, the service can be migrated from the the source network to the destination network before the UEs comes.
Indeed, we would like to investigate the use cases and potential new requiement of Live Migratable Services in the 5G System.

## Slide 3: Logical Relationship
We can treat the new features separately from the existing Network Function Services. The communication services brought by new features will be provided by two logical parts of the network. One is basic communication functionalities from the existing NFs and NF Services, the other is optional advanced functionalities that may be composed of new NF services in different corresponding NFs. Considering this decoupling design, the adding, updating, removal of the optional advanced functionalities will have no significant influence on basic communication functionalities.
NF 1
NFS 1
NFS 2
NFS 3
NF 2
NFS 1
NFS 2
NFS 3
Live Migratable Service
is composed of

## Slide 4: Use Cases:
The communication service a group of UEs want to access locally may not exist in the local network, also the local network is not able to generate one by itself.
To meet the requirement of low latency and service continuity, the service can be migrated from central network to the local network as well as between two adjacent local network, before the UEs move to the target serving area.
Central 5GC
Service Migrating Path
UE
Local 5GC
UE Moving
Track
AMF
Similar migration processes also happens in:
  Local breakout roaming scenarios, migration from HPLMN to VPLMN.
  5GC in satellite scenarios, migration from the current to the next satellite before the serving satellite flies away and the next comes.
  etc...
AMF service
AMF
AMF service
UE
Local 5GC
AMF
AMF service

## Slide 5: SID Objectives:
The objective of this study is to study use cases and potential new requirements for Live Migratable Services in the 5G System. The study aims to cover:
  Use cases for enhanced 5G system support of the migrating processes between networks for specific communication services.
  Potential new service requirements, including:
    Enabling UEs to use specific communication services which are migrated from the sourcing serving network to a temporary accessing network (e.g., local networks, NPN, VPLMN, etc) that do not have such services originally;
    Network functionalities to negotiate and perform to transfer a specific communication service.
    Policy management and interaction between networks and other mobile operators (offering the service)
  Consideration of charging, regulatory and security aspects.
  Gap analysis between potential new requirements and existing requirements and functionalities supported by 3GPP, e.g., PALS, NPN, slicing, etc.

## Slide 6: Thank you