## Slide 1
CATT, China Telecom
Discussion on new use cases for FS_5GSAT_Ph3

## Slide 2: New Proposed Use Cases
it is proposed to consider following use cases in FS_5GSAT_Ph3:
  Use Case 1: Connectivity of temporary satellite local CN
  Use Case 2: Prioritisation of satellite based transport network resources for high priority users

## Slide 3: Use Case 1: Connectivity of temporary satellite local CN
Use case description:
  As satellite can provide ubiquitous coverage, it is appropriated to be used to serve some special cases, e.g., scientific expeditions or mission critical services etc., when terrestrial network is not available. In such cases, the user, e.g., scientists, may need to setup local data center on the site for data storage, analytics or retrieval locally.
  To support this and allow the scientists to visit the local network directly via the satellite, without going back to the core network deployed far away, a local network needs to be deployed, and can connect to satellite enabled RAN directly via a Gateway.

## Slide 4: Use Case 1: Connectivity of temporary satellite local CN
Service flow:
  1. A scientific investigation team arrives in Antarctica, and set up a camp, where a local network is to deployed, e.g., for data collection, analytics and storage.
  2. As there is no terrestrial network, the team members have to access operator’s network and/or the local network via satellite access. So the local network has to connect with gNB on the satellite.
  3. To allow the local network to connect with gNBs on-board, in the camp, there may be a light satellite gateway which can search available gNBs on-board, establish connection with a gNB on-board., and work as a local UPF or local 5GC.
  4. To add this local UPF or 5GC, the light satellite gateway (e.g., as a UE) may send a request to remote 5GC in operator’s data center to ask for network configuration for being a local UPF or 5GC.
  5. The remote 5GC will authenticate the light satellite gateway, and determine it can work as a local UPF or 5GC.
  6. After receiving configuration data, the light satellite gateway works as a local UPF or 5GC, e.g.,:
    The local UPF will setup N4 connection towards a SMF(s) in the operator’s data center
    The local 5GC may setup more TNL associations with the gNB on board after NG setup is completed.
  7. Any team member has to be authorized to visit the local network:
    If a local UPF is deployed, the SMF may authenticate the user, and determine whether a PDU session towards the local UPF is allowed.
    If a local 5GC is deployed, it is up to the local 5GC to authenticate the user.
  NOTE: To completely isolate this local network, a standalone 5GC may be setup.

## Slide 5: Use Case 1: Connectivity of temporary satellite local CN
Potential objectives for study:
  1. How does the local network connect to the 5G system, including the role of the Gateway that connects the local network with the satellite (e.g. a UE vs a NTN gateway)?
  2. Whether 5G entities need to be deployed in the local network to support such use cases, e.g. UPF+MEC or a mini 5GC including control plane entities.
  3. Authentication/Authorization/Accounting for the connectivity of the local network.
  4. How to protect the communication from the satellite to the Gateway in the local network.
  5. Authentication of the end users who want to access the local network

## Slide 6: Use Case 2: Prioritisation of satellite based transport network resources for high priority users
Use case description:
  User's requirements are agnostic to the satellite operation center, i.e. NTN control function defined in RAN3, so the NTN control function can not take users' requirements into account to reserve satellite resources, e.g., space transport network resource, which then can not promise users' experience.
Service flow
  1. A government user attached to the 5GS via satellite access;
  2. To serve this high priority user, the 5G system will reserve radio resources for this user, and set ARP to high priority for QoS flows belonging to this user;
  3. The 5G system also informs NTN control function to reserve transport network resources between the gNB on-board and the satellite gateway on the ground for this user, i.e., the satellite backhaul resources, so that user data transmission over N3 connection can be promised.
  4. The 5G system may also tell the NTN control function that there is a high priority user in a designated area to avoid the NTN control function to change this satellite beam to serve other services/systems, e.g., not to schedule this satellite beam to serve another area for mission critical system.
  Potential objectives for study
  Whether the 5G system can request the satellite system to reserve backhaul resources for a gNB on-board serving the high priority users.
  Whether the 5G system can indicate the satellite system the QoS requirements to satellite transport network for serving high priority users.
  Whether the 5G system can indicate the satellite system the location of a priority user for satellite resources scheduling.

## Slide 7
Thank You!