## Slide 1: 3GPP SA1 Proposal cUE signalling as a user service (Companion to S1-221036)
S1-221204
Source: IIT Bombay, Saankhya Labs, Tejas Networks, IIT Kanpur, CEWiT

## Slide 2
UE Signalling as User Service (or as User Data)
Control plane of 5G system exchanges signalling messages with UEs
  TS 22.261, “Clause 6.4.2.4 Efficient Control Plane”
Signalling message examples
  NAS messages - UE “Registration”, “Authentication” etc.
  AS messages - “RRCSetup”, “MeasurementReport” etc.
Exchange of signalling messages between UE and the 5GS
  Requires a path to be established through the 5G network, e.g., SRB over the radio link
  Signalling paths (SRBs) similar to data paths such as DRB
  But 5GS treats UE signalling traffic differently from the user data traffic
The SID would study
  If it is possible to treat “UE signalling” as user (data) service
  Can signalling and data traffic be treated in a similar manner by 5GS?
  Are there any advantages thereof?

## Slide 3
Key Difference between UE signalling and User Service (Data)
UE signalling and user data
  Different end points in 5G network
UE signalling end points
  Control plane functions in 5GS
  AMF, AUSF…
User service end points
  Part of user plane
  Functions in data network
  AF/AS …

## Slide 4
UE Signalling as User Service (or Data) – An Example
Placing UE signalling end points in user plane (or data network)

## Slide 5: Summary and Potential Benefits
Change in perspective
  UE Signaling and UE Data – similar from network perspective
Decoupled “UE signalling” and “User Plane Control” functions
  Dedicated UE signalling service functions
    For Signalling exchange with UEs and UE control & state management (RRC Server, NAS Server)
  User Plane Control Functions
    Controls user plane as in SDN paradigm
    But does not exchange signalling messages with UEs
Flexible function placement and chaining for UE signalling services
  RRC Server, NAS Server, Auth Server… (signalling servers) can be chained together to serve UEs
Use case specific variants of UE signalling protocols – possibly easy to support
Enhanced modularity
Simpler message flow & simpler protocols
Possibly built-in services such as PDU Connectivity, Handover and user services such as IMS/Streaming (i.e. AF/AS based services) can be handled in a similar manner
  Right now they are handled differently

## Slide 6: Thanks