## Slide 1: CIoT Drafting Output (revision of S2-160523)
S2-160541

## Slide 2: Agreements from drafting session
UE requests “Non-IP” ESM session w/ PDN type = “Non-IP”
MME creates a PDN connection depending on APN and/or HSS information. MME selects SCEF or P-GW based on APN information.
UE is informed by MME which transmission method (CP and/or UP) it shall use
  If MME determines that PDN connection via SCEF shall be used, “CP only” is indicated to the UE in the ESM response.
MME will grant EBI (present range 5-15) to PDN connections via SCEF as well
No change from drafting agreement

## Slide 3: For further discussion offline
APN related stuff
  NB-IoT UE need not provide APN information in PDN CONNECTIVITY REQUEST
     For such UEs wanting Non-IP support, APN corresponding to Non-IP has to be the default APN in HSS
     The HSS has one default APN for PDN Type = “Non-IP”. It may point to SCEF or PDN
  Same handling for NB-IOT UE, eMTC UE and multimode NB-IOT+eMTC UE
  To allow MME to distinguish which selection procedure (S/PGW or SCEF) to invoke, a well known APN partial APN string (eg SCEF*) is used for “Non-IP” APNs
     To ensure consistent service behaviour whilst roaming, GSMA agreement might have to be obtained?
  SCEF selected by MME must be the same as SCEF selected by SCS/AS (see S2-160276)
     APN-based address resolution (scefabc.mccX.mncY.3gpp.org) can’t guarantee this
    Proposal: HSS needs to be configured w/ either hostname (scef.vf.com) OR IP address of SCEF. Similar config will be on SCS/AS.
      For SCEF hostnames which resolve to multiple SCEF IP addresses it must be ensured that those SCEF which share the hostname can share the SCEF contexts
No change in text from drafting

## Slide 4: Header Compression CRs
Header compression updates to Attach procedure
  S2-160322
  It was agreed that changes should be in ESM signalling
  No need to transfer header compression context during inter node change. Header compression configuration parameters would be transferred.
  S2-160322 will be revised to S2-160516
Header compression updates to CP optimization procedure
  S2-160314
  Changes should be merged with CR in S2-160422
  S2-160422 will be revised to S2-160517
No change from drafting agreements

## Slide 5: For a Non-IP APN, how HSS tells MME to invoke SCEF selection logic v/s S/P-GW selection logic? (/3/ from slide#3)
Introduce a new flag “Select SCEF” on per user per APN basis in HSS subscription
  Include the new flag only for PDN type = “Non-IP” and operator wishes for serving node to select SCEF for that PDN connection
Introduce concept of default APNs per PDN-type category (atmost 1 default APN for IP, atmost 1 default APN for Non-IP)
    This is to support the use-case that an eMTC UE wanting 2 PDNs (1 for Ip, 1 for Non-iP) is able to get the PDNs without having APN configuration being done on the UE.
    1 default APN for IP refers to having 1 default APN with a single PDN-Type of either v4, v6, or v4v6
Agreement from unofficial offline drafting during Thu 2H coffee break
Agreement: Both /1/ and /2/ are to be supported for Rel-13

## Slide 6: How to ensure that SCEF selected by MME is the same as SCEF selected by SCS/AS ? (/4/ from slide#3)
Configure SCEF identity for the required Non-IP APN(s) which are to provide PDN connectivity through SCEF
  either hostname (scef.vf.com) OR IP address of SCEF
  (out of 3GPP scope, but must be ensured by operator) Same configuration is to be mimicked @ SCS/AS
Agreement from unofficial offline drafting during Thu 2H coffee break
Agreement: Along w/ “select SCEF” indicator (from previous slide), SCEF Identity (hostname or IP address) is provisioned for Non-IP SCEF APN(s)

## Slide 7: What parameters does MME use to initiate T6a towards SCEF?
Note, presently T6a is an implicitly terminated diameter connection. MME never sends a msg to SCEF unless MONTE/AESE configuration (containing SCEF Ref-Id, SCEF Id, UE identifier) is configured on the MME
Required parameters to allow T6a initiation on MME:
  (Mandatory) UE identifier:
      Operator decides (based on MME and SCEF configuration) Either IMSI, MSISDN, or external ID(s)
        Note, S6a needs to be updated to allow sending of External-ID(s) from HSS to MME.
  (Mandatory) EBI for a given PDN connection when assigned by MME
Agreement from unofficial offline drafting during Thu 2H coffee break

## Slide 8: Impacted CR(s) where these agreements are to be reflected
Non-IP via SCEF (CR 0160)
Attach (CR 2951)
TAU (CR 2959)
CIoT data procedures (CR 2942)
Non-IP service introduction (CR 2934)
...