## Slide 1: SA2 Work Status: RAN-CN functional split
Rapporteurs
Devaki Chandramouli (Nokia), Sun Tao (China Mobile)

## Slide 2: SA2 work status
RAN-CN Functional split
Way Forward proposal

## Slide 3: 1 RAN – CN function split (1/2)
SA2 achieved “Interim Agreements on NextGen RAN and NextGen Core functional allocation”
  Focuses on functionalities for basic building blocks MM, QoS, SM, authentication.
Location: Function: | NextGen RAN | NextGen CN | Comments
Key Issue #1 – Network Slicing |  |  | 
CN instance selection when UE attach to a CN network slice | FFS | FFS | 
Key Issue #2 QoS |  |  | 
Radio Resource Admission Control | X |  | 
Radio Resource management (QoS attributes) | X |  | Packet scheduling with regards to resource utilization and availability (RRM)
Max rate control | X | X | Maximum bitrate policing in the CN and RAN in UL and DL.
QoS Policy Control |  | X | 
Transport marking | X | X | Used for prioritization in the transport network.
Charging Data Collection |  | X | 
Packet classification of DL packets for QoS differentiation on the Radio | FFS | FFS | Some companies think the QoS classification for QoS differentiation of DL packets is performed in RAN.
QoS differentiation and verification for UL packets | FFS | FFS | Some companies think the QoS verification for UL packets is performed in RAN and/or CN.
Key Issue #4 - Session Management |  |  | 
PDU Session address allocation |  | X | FFS for non-IP PDU Sessions
PDU Session Termination Point |  | X | Note that this refers to the ownership of the specification for the function supporting the termination point. In a NW deployment this function may be deployed on or close to a RAN site.
Session Management |  | X | 
Termination of UP security | FFS | FFS | FFS
Subscription Data Handling (incl. default QoS profile) |  | X | 

## Slide 4: 1 RAN – CN function split (2/2)
Location: Function: | NextGen RAN | NextGen CN | Comments
Key Issue #3 – Mobility Management |  |  | 
Mobility management control, (Subscription and Policies) |  | X | 
Determination of mobility restriction |  | X | 
Roaming restrictions execution |  | X | 
Mobility restrictions execution, [CN Connected] | X |  | 
Mobility restrictions execution, [CN Idle] |  | X | If CN Idle exists.
UE registration |  | X | 
Area tracking | FFS | FFS | The need for Hierarchical tracking is FFS. Depends also on the existence of a CN Idle state
UE unreachability detection |  | X | Assumed to be supported in CN for UEs in CN Idle state. If CN Idle exists.
RAN UE unreachability detection | X |  | Assumed to be supported in RAN for UEs in RAN Inactive state. If RAN inactive state exists.
NAS state transitions |  | X | 
RRC state transitions | X |  | 
Paging initiation and control in RAN Inactive state | X |  | RAN Inactive state is RAN state that corresponds to CN connected state. If RAN inactive state exists.
Paging initiation in CN Idle state |  | FFS | CN Idle state is FFS. Some companies assume that the CN Idle state is replaced by a RAN "Inactive" State. Some companies think that the CN Idle state remains but is used more seldom due to the new RAN "inactive" state
Access Stratum UE Context storage in RAN Inactive state | X |  | If RAN inactive state exists.
Control of connected state mobility | X | X | 
UP buffer for UE in CN Idle state |  | FFS | Same comment as on Paging initiation in CN Idle state
UP buffer for UE in RAN Inactive state | X |  | If RAN inactive state exists.
Key issue #12 |  |  | 
Authentication and Key Agreement |  | X | 

## Slide 5: RAN – CN function split (SA2#115 working assumptions on QoS)
Support for Reflective QoS | X | x | Support Reflective QoS over radio under control of the network. The network decides on the QoS to apply, marks the DL traffic and the UE mirrors the QoS.
Location: Function: | NextGen RAN | NextGen CN | Comments

## Slide 6: 2 Way Forward
SA2 believes RAN-CN function split will be continuously summarized based on the solutions being developed for the key issues
Eventually RAN-CN interface requirements should be derived based on the solutions developed for the key issues and RAN-CN functional split.
Ideally, joint meeting should decide the WG responsible for addressing the opens (e.g. items with FFS) that impact both RAN/CN to avoid duplication of effort.

## Slide 7: Reference
3GPP SA2 TR 23.799