## Slide 1: Report of NextGen work status in SA2: Network Slicing
China Mobile, Nokia
(Rapporteurs)

## Slide 2: 1. Definition and Assumption
Network Slice (NS): is composed of all the NFs that are required to provide the required Telecommunication Services and Network Capabilities, and the resources to run these NFs.
  NOTE 4: In this document a Network Slice is equivalent to a Network Slice Instance.
  Editor’s Note: It is for the RAN WG to determine how the Network slicing applies to RAN. It is FFS whether some aspects of level of isolation/separation should be part of the NS definition.
  NOTE 5: The PLMN may consist of one or more network slices. The special case of just one Network Slice is equivalent to an operator’s single, common, general-purpose network, which serves all UEs and provides all Telecommunication Services and Network Capabilities that the operator wants to offer.
Assumption: It shall be possible to verify that the UE is allowed to access a specific network slice.

## Slide 3: 2. Interim Agreement on solution aspects
The network slice is a complete logical network (providing Telecommunication Services and Network Capabilities) including AN and CN. Whether RAN is sliced is up to RAN WGs to determine.
  a) AN can be common to multiple network slices.
A UE may provide NS selection assistance information to the network.
If a network deploy network slicing, then it may use UE provided NS selection assistance information to select a NS.
A UE may access multiple slices simultaneously via a single RAN. In such case, those slices may share some control plane functions, e.g. MM.

## Slide 4: 3. Work Tasks of Identified Network Slicing
ID | Work Task(s) | Work Task Description
WT_#1 | Network Slice Instance Selection and Association | Initial network slice instance selection to support UE’s service establishment and re-selection to support UE mobility and other scenarios that are TBD, Network slice instance identification, Service authorization for UE association with network slice instance Network assistance information support for UE network slice instance association with corresponding PLMN
WT_#2 | Network Slicing Isolation | Security isolation Resource isolation OAM support isolation (e.g. Usage and Fault isolation etc.)
WT_#3 | Network Function Determination | Identifying what are the network functions comprise of a network slice for particular network services
WT_#4 | Network Function Sharing support | Identifying network function(s) that need to be shared between network slice instances Defining what needs to be done for enabling the NFs identified above under 1) for supporting the sharing
WT_#5 | Enable operators to use the network slicing concept to efficiently support multiple 3rd parties (e.g. enterprises, service providers, content providers, etc.) that require similar network characteristics. | Handling of UE’s subscription between MNO and its 3rd parties to enable MNO to leverage the network slicing solution to efficiently utilize system resources to support multiple 3rd parties’ network services with adequate QoS, mobility, service continuity etc. support
WT_#6 | UE Simultaneous Association with Multiple Network Slice Instances | Coordination on security, MM and SM support, if any, and any other required operations.
WT_#7 | Network Slicing Roaming support | Determination what visiting and home Network Function(s) are required to support roaming.
WT_#8 | Network Slicing terminology & definitions | If Network Slice Instance is agreed to apply E2E system, then, we should consider new terminology for Access slice instance and Core slice instances.
To be updated
Notes: Solution in general on selection

## Slide 5: 4 Proposed Way Forward
It is suggested RAN groups takes into account the slicing progress as above
SA2 understands that RAN WG will decide whether and how Network Slicing applies to NextGen Radio (NR). SA2 kindly requests RAN WG to inform SA2 in case RAN WG believe that, for a given UE’s access via NR, NextGen Core Network should be made aware of Network Slicing when applied to/in RAN.