## Slide 1
SA WG2 Meeting #117 S2-165500
17-21 October 2016, Kaohsiung City, Taiwan
Data Off solutions comparison and evaluation

## Slide 2
Contents
Comparison of the solutions, per Key Issue
Evaluation, per Key Issue

## Slide 3
Key Issue 1 - UE informing the network about the UE’s status
Solutions comparison
Delivered
Proceeding to plan
Urgent attention required
Solution | Main principle | Description | Comments/Evaluation
Solution 1.1 | UE’s status reported via NAS and SIP Register | UE's DOFF Status in Attach/TAU Request + status storage in MME MME provide DOFF Status to each PGW SIP Register with UE's DOFF Status to S-CSCF | No signalling to HSS Allows verification of IMS services by IMS Not transparent to the VPLMN
Solution 1.2 | UE’s status reported to 3GPP Core Network | Same but IMS network is not informed | It is based on the principle that no verification needs to be made by the network for IMS services. This cannot be used to stop MT SMS over IP. Not transparent to the VPLMN
Solution 1.3 | UE’s status reported via single NAS message | UE's DOFF Status in Attach/TAU Request + status storage in MME MME informs HSS + storage in HSS MME provide DOFF Status to each PGW HSS provides DOFF Status to S-CSCF | DOFF status HSS-based solution. May result in more HSS signalling Allows verification of IMS services by IMS Not transparent to the VPLMN
Solution 1.4 | UE’s status reported to HSS using USSD and USSI | UE's DOFF Status in MO USSD or USSI + storage in the HSS | DOFF status HSS-based solution. May result in more HSS signalling Allows verification of IMS services by IMS Transparent to the VPLMN
Solution 1.x | UE’s status reported using PCO for non-SIP services and via SIP register for SIP services | UEs send their DOFF Status in PCO (for non-SIP services) on all new and established PDNs SIP Register with UE's DOFF Status to S-CSCF | No signalling to HSS Allows verification of IMS services by IMS Transparent to the VPLMN

## Slide 4
Key Issue 2 - Making the UE aware of 3GPP PS Data Off Exempt Services
Solutions comparison
Proceeding to plan
Urgent attention required
Solution | Main principle | Description | Comments/Evaluation
Solution 2.1 | using filters for non-SIP services and enumeration/ICSI for SIP services | DM-based configuration: configuration with data covering all PLMNs with roaming agreements Non-SIP based services identified by APN and uplink filter. Also based on allowed destination IP addresses for non-SIP services SIP based services identified by enumeration or by ICSI | Decentralized database requiring UE/EPC/IMS . Requires O&M coordination Configuration data for all PLMNs need to be downloaded to the UE (with DM, a UE needs to receive configuration for the VPLMN before attachment) If one new VPLMN or changes in configuration in any VPLMN, all UEs should be updated IMMEDIATELY (even if UEs are roaming in another VPLMN) Identification of non-SIP based services at L3/L4 is not sufficient. Need to be at application layer Fixed destination IP addresses would not work in all deployments Transparent to the VPLMN
Solution 2.2 | Using non-standard filters and services | Same as solution 2.1 except that Filters and SIP based services are not standardized and based on UE implementation | Same as solution 2.1; plus: How can it works in DM server? What happen if the user changes UE (UICC move) and the UEs (old, new) are from different vendors?
Solution 2.3 | using a list of Data Off Exempted Services (DOES) | HSS provides a list of Data Off Exempted Services" (DOES) . Could be ICSI for SIP services For deployments where VPLMN should not be impacted, use of GSMA DM to provide the List of DOES, valid in all PLMNs. | HSS provides the list of services only for the PLMN the UE is attaching to. It is also provisioned early enough (in the Attach Accept) -> minimize data exchange Identification of non-SIP based services is at application layer For deployments where VPLMN should not be impacted, there is a fallback mode (same list of DOES valid for all VPLMNs).
Solution 2.4 | Using USIM provisioning | Provisioned data for a UE can be provisioned on a USIM via e.g. OTA. | Configuration data for all PLMNs need to be downloaded to the UE (otherwise if a UE is roaming it will receive the configuration for the VPLMN too late) If one new VPLMN or changes in configuration in one VPLMN, all UEs should be updated even roaming UEs Transparent to the VPLMN

## Slide 5
Key Issue 3 (1/2) - Support for controlling non-SIP based services
Solutions comparison
Proceeding to plan
Urgent attention required
Solution | Main principle | Description | Comments/Evaluation
Solution 3.1 | PCRF based using CSR/MBR to inform PGW/PCC + filters on IP@ | MME indicates DOFF Status to PGW via CSR/MBR and PCRF via IPCAN Modification PGW indicates whether to reject/release the PDN connection to the MME/SGSN PCRF must be provisioned with the necessary IP addresses for non-SIP based services that are Data Off exempt FIlters are ONLY IP addresses and configured in the PGW/PCRF | PCRF based solution: PCRF or PGW requires configuration: How is consistency with UE via DM ensured? Only IP addresses are addressed. Not transparent to the VPLMN How can LBO APNs can be controlled and under the responsibility of the home operator?
Solution 3.2 | PCRF based using CSR/MBR to inform PGW/PCC + flexible filters | MME indicates DOFF Status to PGW via CSR/MBR and PCRF via IPCAN Modification PCRF or PGW configured with filters for DL Covers 2G/3G | PCRF based solution: PCRF or PGW requires configuration: How is consistency with UE via DM ensured? Not transparent to the VPLMN How can LBO APNs can be controlled and under the responsibility of the home operator?
Solution 3.3 | PCRF based and UE learning | Based on downlink TFT filters provided by PCRF No solution if PCRF does not apply The UE learns if an APN is forbidden by rejections from PGW | PCRF based solution. No solution if PCRF not applied How can a UE know when an APN is allowed again? Transparent to the VPLMN How can LBO APNs can be controlled and under the responsibility of the home operator?

## Slide 6
Key Issue 3 (2/2) - Support for controlling non-SIP based services
Solutions comparison
Proceeding to plan
Urgent attention required
Solution | Main principle | Description | Comments/Evaluation
Solution 3.4 | HSS based and using CSR/MBR to inform PGW/PCC | Based on PS Data Off status provided by the UE to the MME/SGSN. HSS provides list of exempted APNs (no S6a/S6d/Gr changes)+ additional filters to MME. MME provides APN/filters to PGW/PCRF and releases PDN connections of non exempted APNs | HSS based solution Not transparent to the VPLMN for Home Routed services.
Solution 3.x (new) | using HSS knowledge of PS Data Off UE status avoiding VPLMN impacts for early deployments | Based on PS Data Off status provided by the UE to the HSS transparently to the VPLMN. HSS provides list of exempted APNs (no S6a/S6d/Gr changes)+ additional filters to MME. MME provides APN/filters to PGW/PCRF and releases PDN connections of non exempted APNs For deployments w/o VPLMN impacts, HSS only provides exempted APNs (existing mechanism) . | HSS based solution Transparent to the VPLMN for Home Routed services.
Solution 3.y (new) | using PCO for carrying PS Data Off UE status avoiding VPLMN impacts for early deployments | Based on PS Data Off status provided by the UE to the PGW via transparently to the VPLMN (PCO). HSS provides list of exempted APNs (no S6a/S6d/Gr changes)+ additional filters to MME. MME provides APN/filters to PGW/PCRF and releases PDN connections of non exempted APNs For deployments w/o VPLMN impacts, no control of DL data for LBO (UE controls UL data). | HSS based solution Transparent to the VPLMN for Home Routed services.

## Slide 7
Key Issue 4 (1/2) - Support for controlling SIP based services
Solutions comparison
Solution | Main principle | Description | Comments/Evaluation
Solution 4.1 | CSCF based config, UE status via IMS and CSCF based control | the UE prevents sending not exempted UE-originating SIP requests and SDP offers/answers the UE sends a (re-)REGISTER request to actovate/deactivate DOFF the IMS domain, and specifically the S-CSCF rejects non-exempted MT SIP requests CSCF configured with the list of exempted IMS services | CSCF configured with list of IMS exempted services UE's DOFF Status sent via IMS registration Transparent to the VPLMN
Solution 4.2 | HSS based config , UE status via IMS and 3rd party registration to AS based control | the UE prevents sending not exempted UE-originating SIP requests and SDP offers/answers the UE sends a (re-)REGISTER request to activate/deactivate DOFF 3rd party registration to an Application Server (AS) HSS is configured with the list of IMS exempted services and passed to the AS | HSS-based solution for the list of services UE's DOFF Status sent via IMS registration Transparent to the VPLMN
Solution 4.3 | HSS based config, UE status via IMS and S-CSCF/TADS based control | the HSS sends the list of IMS exempted services within the "list of Data Off Exempted Services" (DOES). The UE blocks the non exempted SIP/SDP requests the S-CSCF is informed by the HSS on the "list of exempted IMS services" (e.g. ICSIs) only for the VPLMN is the UE is currently registered to. the IMS domain rejects non-exempted MT SIP requests T-ADS is informed and determines if a call can be delivered to CS or WLAN. | HSS-based solution for the list of services UE's DOFF Status sent via IMS registration or via HSS Transparent to the VPLMN

## Slide 8
Key Issue 4 (2/2) - Support for controlling SIP based services
Solutions comparison
Solution | Main principle | Description | Comments/Evaluation
Solution 4.4 | S-CSCF based config , HSS based UE status and CSCF based control | The S-CSCF is configured with the list of 3GPP PS Data Exempt Services / Or the list of 3GPP PS Data Exempt Services is part of subscription. The HSS receives UE's DOFF Status from the MME and provides it to the IMS | CSCF configured with list of IMS exempted services HSS-based solution for the UE's DOFF Status Conditional transparency to VPLMN
Solution 4.5 | S-CSCF based config , HSS based UE status and T-ADS based control | The S-CSCF is configured with the list of 3GPP PS Data Exempt Services / Or the list of 3GPP PS Data Exempt Services is part of subscription. The T-ADS fetches the UE's DOFF Status by querying the MME via the HSS | CSCF configured with list of IMS exempted services HSS-based solution for the UE's DOFF Status Conditional transparency to VPLMN
Solution 4.6 | HSS based config , HSS based UE status and AS based control | HSS is provisioned with a list of 3GPP Data Off exempt services and contains the 3GPP PS Data Off status AS queries the HSS, which replies to the AS with the decision to route the service to PS domain, to degrade it or to reject it | HSS-based solution for the list of services HSS-based solution for the UE's DOFF Status The solutions are for Voice and Video services only No impact to S-CSCF Transparent to VPLMN

## Slide 9
Key Issue 1 - UE informing the network about the UE’s status
Evaluation
Solutions can be categorized as follows
  For non-SIP services,
    UE notifying the MME/SGSN via Attach/TAU procedures + storage in the MME/SGSN
    UE notifying the HSS directly, then the HSS notifying the MME
    UE notifying the PGW via PCO (new 1.x) for each PDN connection.
  For SIP services,
    UE not notifying the network (CN or IMS). Would not block services that carry info in Invite e.g. SMSoIMS service
    UE notifying the IMS network directly via SIP (re)register
    UE notifying the HSS (via MME/SGSN or directly)
Observation: UE notifying the HSS will add HSS signalling
Conclusions: For SIP services, the SIP (re)register solution is recommended . For non-SIP services, depending on requirements for DL data in LBO (no VPLMN impact case) either the HSS should be informed by the UE on PS Data Off w/o impacts to the VPLMN (e.g. solution 1.4, but implies lots of signalling exchanges) or the PCO-based solution should be selected (simpler solution).

## Slide 10
Key Issue 2 - making the UE aware of 3GPP PS Data Off Exempt Services
Evaluation
Three kinds of solutions for the provision of DOFF exempted services in the UE
  Provided by the HSS or by an External Database, or learnt from PGW rejections (issue for last one)
  The list of DOFF exempted services shall be available in the UE as soon as the UE is attached
    If provided by HSS, it is done at Attach. Only current VPLMN data is sent to the UE.
    If provided by an external database, the list of DOFF exempted services for all PLMNs shall be provided before the UE attaches to a VPLMN.
  Consequences of a change of exempted services in a PLMN or of the addition of a new PLMN
    If provided by the HSS, only a change on the current PLMN generates signalling to the UE.
    If provided by an external database, any change of exempted services (or addition of a PLMN) in any PLMN generates the immediate download of all necessary data to all the UEs of the operator.
Summary: there are strong drawbacks of using an external database
Conclusion: it is recommended that the list of DOFF exempted services are configured in the HSS and provided to the UE via MM procedures. For deployments w/o VPLMN impacts, use of GSMA DM to provide the List of DOES, valid in all PLMNs.

## Slide 11
Key Issue 3 - Support for controlling non-SIP based services
Evaluation
Solutions can be categorized as follows
  PCRF-based/PGW-based configuration: the PGW indicates to the MME/SGSN whether to reject/release a PDN connection.
  HSS-based configuration: the HSS only provides exempted APNs (no S6a/Sd/Gr changes) and associated filters to the MME/SGSN, which sends APN/Filters to PGW/PCRF and rejects/releases PDN connections with non exempted APNs.
  Solutions that have a fallback mode avoid VPLMN impacts in case of early deployments versus solutions that haven't any.
Observation: with PCRF-based/PGW-based solutions, how can LBO APNs can be controlled and under the responsibility of the home operator? Moreover, non-SIP services in UE and in network should remain consistent. Requires a proprietary O&M system with synchronized external databases. Key Issue 2 shows issues for External Database for UE provisioning.
Conclusions: HSS-based configuration solution, which has a fallback mode avoid VPLMN impacts in case of early deployments, shall be selected.

## Slide 12
Key Issue 4 - Support for controlling SIP based services
Evaluation
Solutions can be categorized as follows
  List of exempted SIP services configured in the HSS and provided to the IMS network (S-CSCF or AS)
  List of exempted SIP services configured in the S-CSCF
Observation: Both types of solutions can be used. However, an HSS configuration would allow extensibility for a different list of SIP services for different UEs or UE categories Some solutions impact the VPLMN and should be ruled out.
Conclusions: As long as the solution does not add HSS signalling, the list of exempted SIP services configurable in the HSS is preferred.